| Subgroup Name | Digital Subsystem |
| --- | --- |
| Subgroup Leader | Osamu Miyakawa ICRR U-Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-06-2 | Kick-off draft written in wiki format |
| Rev. A-1 | 2009-08-07 | Converted to MS-Word format |
| Rev. A-2 | 2010-04-15 | Fixed several parameters by the experience at CLIO digital system |

Glossary

| ADC | Analog to Digital Converter |
| --- | --- |
| DAC | Digital to Analog Converter |
| AA | Anti aliasing |
| AI | Anti imaging |
| UGF | unity gain frequency |
| IFO | interfoemter |

- Definition of subsystem

This system provides the functions which digitalize analog sensing signals extracted from interferometers, produce signals in computers for controlling the interferometers and data acquisitions, and re-produce analog signals to actuate the interferometer.

- Task area

| No. | Function | Description, equipments |
| --- | --- | --- |
| 1 | Digital control system | Main system. PC, ADC/DAC, AA/AI filter, whitening/dewhitening filter, real time OS, control software, monitor software, data storage. |
| 2 | Detector tuning system | Adjusts interferometer parameters. Tuning software. |
| 3 | Detector diagnosis system | Interferometer self diagnosis. Diagnosis software. |
| 4 | Long term monitor | Monitor software, data storage |
| 5 | Auto lock / auto alignment sequencer | Real time lock code (fast), auto lock and alignment scripts (slow). |
| 6 | Detector operation system for GW observation | Operators, operation scheduling, auto lock scripts. |
| 7 | GW search data calibration | Real time calibration shown in the control room. Projectors, calibration signals, real time calibration software |
| 8 | Real time data analysis | Real time data analysis shown in the control room. Projectors, real time data analysis software |

3. Required specifications

| Item | Requirements | Comment |
| --- | --- | --- |
| Sampling rate | >16kHz |  |
| Dynamic range of input | >+/-15V | Half on differential |
| Dynamic range of output | >+/-10V | Half on differential |
| ADC noise | <3uV/rHz |  |
| DAC noise | <3uV/rHz |  |
| time delay | <100usec | To realize 300Hz UGF |
| Input channel numbers | >1024ch | (16kHz:>128ch, 2kzHz:>256ch, 64Hz>512ch) |
| Output channel numbers | >256ch | for suspensions, PZTs |
| Stored channel | 16kHz:>64ch, 2kzHz:>256ch, 64Hz>512ch |  |

4. Interface between systems

|  | Item | Related sub-system | Requirements | Agreement |
| --- | --- | --- | --- | --- |
| * | Sampling rate | Data acquisition, Data analysis, IFO control | 16384Hz(sampeled at 65536Hz and decimated to 16384Hz) option:up to 65536Hz for limited number of channels | not yet |
|  | Number of channels | Data acquisition, Data analysis, IFO control | 16kHz:64ch, 2kHz:256ch, 64Hz:512ch 16Hz:2048 epics channels (see channel list) | not yet |
| * | Data bit resolution | Data acquisition | 24bit = 4 Byte integer | not yet |
|  | Data transfer rate | Data acquisition | 4MB/sec for 16kHz, 2MB/sec for 2kHz, 128kB/sec for 64Hz 128kB/sec for 16Hz | not yet |
|  | Saved parameters (using conlog) | Data analysis, IFO control | See parameter list | not yet |
| * | ADC dynamic range | IFO control | Full differential +/-10V = effective range +/-20V | not yet |
| * | DAC dynamic range | IFO control | Full differential +/-5V = effective range +/-10V | not yet |
| * | through delay | IFO control | 80usec | not yet |
| * | ADC noise level | IFO control | 2uV/rHz | not yet |
| * | DAC noise level | IFO control | 1.5uV/rHz | not yet |
| * | AA filter noise level | IFO control | 0.1u V/rHz | not yet |
| * | AI filter noise level | IFO control | 0.1u V/rHz | not yet |
| * | whitening filter noise level | IFO control | 1n V/rHz | not yet |
| * | dewhitening filter noise level | IFO control | 1n V/rHz | not yet |
| * | whitening filter input impedance | IFO control | TBD | not yet |
| * | dewhitening filter output impedance | IFO control | TBD | not yet |
|  | Connector shape | IFO control | D-SUB9 @ AA and AI BNC or SMA (or LEMO) for single 2pin LEMO for differential @ whitening / dewhitening and binary switch | not yet |
| * | Power consumption | Infrastructure | TBD | not yet |
| * | Waste heat and cooling | Infrastructure | TBD | not yet |
|  | Network capability | Infrastructure | 10Gbps ethernet | not yet |
| * | Optical fiber cable capability for real time PC, clock timing system | Infrastructure | TBD | not yet |
|  | GPS antenna | Infrastructure, Data acquisition | TBD |  |
|  | Location and space | Infrastructure, Data acquisition, IFO control | 3 racks at center room, 1 rack at X end room, 1 rack at Y end room for control system 10 racks at data center | not yet |
| * | Remote control switch | Vacuum, Infrasturucture | TTL(0V-5V) | not yet |
|  | Wireless LAN (digital system on laptop PC) | Infrastructure | IEEE802.11n(300Mbps) | not yet |

↑ Mark * on items which this subsystem needs to define.

5. Other related subsystems

| No. | Function | Related sub-system | Description, equipments |
| --- | --- | --- | --- |
| 1 | CCD monitor | IFO support |  |
| 2 | Inter lock | Infrastructure, IFO support |  |
| 3 | Entrance monitor system | Infrastructure |  |
| 4 | Real time monitors at control room | Infrastructure, IFO support, Data acquisition, Data analysis |  |
| 5 | Control PCs at control room | Infrastructure, Data analysis | Linux, 2-3 heads/PC, 10 PCs at least |

6. Channel list

a. 16kHz (total 64ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| Laser | Output laser power[W] | 1 |  |
|  | IFO Input laser power[W] | 1 |  |
| MC | REFL | 1 |  |
|  | MC length feedback | 1 |  |
|  | MC frequency feedback | 1 |  |
| LSC | I&Q dor DARM, CARM, MICH, PRC, SRC, etc. | 10 |  |
|  | error, feedback | 10 |  |
| SUS | length * 10 suspensions | 10 |  |

b. 2kHz (total 256ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| ASC | WFS | 5xpitch, yaw=50 |  |
|  | Oplev | 10xpitch,yaw=100 |  |

c. 64Hz Long term monitor (total 512ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| Temperature[deg] | room | 10 | center, end, arm |
|  | table | 10 | laser, REFL, AS, pickoff, end |
|  | suspensions | 50 | Low temperature |
|  | mirrors | 50 | Low temperature |
| Humidity[%] | rooms | 10 | center, end, arm |
| Dust | rooms | 10 | center, end, arm |
| Laser | crystal temperature[degree] and etc. | 10 |  |
|  | Master laser power[W] | 2 |  |
|  | Output laser power[W] | 2 |  |
|  | IFO Input laser power[W] | 2 |  |
| Seismic | Room, outside, 3-axis | 30 |  |
| Sound | Room, outside, table |  |  |

7. Saved parameter list

Gain, switch, offset, filter bank, filter on/off, matrix components and all other parameters on Epics channnel