Interface Control Document

of the LCGT Project

| Subgroup Name | Data Acquisition System |
| --- | --- |
| Subgroup Leader | Daisuke Tatsumi National astronomical observatory of Japan |

Glossary

| GPS | Global Positioning system |
| --- | --- |
| DAQ | Data Acquisition System |
| ADC | Analog to Digital Converter |
| bps | bit per second (a unit to indicate data flow capability) |

1. Definition of subsystem

This subsystem should collect data from an interferometric detector.

Data storage, distribution and pre-procession for GW search are also provided for collaborators.

2. Task area

| No. | Function | Hardware, software |
| --- | --- | --- |
| 1 | Main DAQ system | Analog Digital Converter, Signal conditioning filter (whitening filter) |
| 2 | Frame Maker | Computer: Real time operation system to storage data with GW FRAME FORMAT. |
| 3 | Detector Diagnosis | Computer: Online data analysis soft for detector diagnosis and trend-data archive |
| 4 | Environment Monitor | Computer: Environmental data monitoring soft, display for user interface. |
| 5 | Time Keeper and Global Positioning System | GPS, GPS signal transmission system, GPS time server with Rubidium atomic clock, sampling clock distribution system for ADC and DAC. |
| 6 | Raw Data Archive | Computer, tape archive system and data storage system: Archived data database and its human interface. |
| 7 | Pre Analysis Server | Computer: Data re-formatting for GW signal search |
| 8 | Data Distribution | Computer and high-speed network: Data distribution system for collaborator's demands |

2. Required specifications

| No. | Function | Described section (**) | Related sub-system | Modified | To be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Main DAQ system | 17.1 | Data analysis, Digital system |  |  |
| 2 | Frame Maker | 17.2 | Digital system |  |  |
| 3 | Detector Diagnosis | 17.3 | Digital system |  |  |
| 4 | Environment Monitor | 17.4 | Digital system |  |  |
| 5 | Time Keeper and Global Positioning System | 17.5 | Digital system |  |  |
| 6 | Raw Data Archive | 17.6 | Digital system |  |  |
| 7 | Pre Analysis Server | 17.7 | Data analysis |  |  |
| 8 | Data Distribution | 17.8 | Data analysis |  |  |

** Section in LCGT design document of version 2

3. Interface between systems

|  | Item | Related sub-system | Requirement | Confirmation |
| --- | --- | --- | --- | --- |
|  | Observation band | Data analysis | 10 Hz - 10 kHz | by DAS |
|  | ADC bit resolution | Data analysis | > 16 bits | by DAS |
|  | Number of channels for GW search | Data analysis | 32 channels | by DAS |
|  | Pre-processed data formats | Data analysis | TBD | not yet |
|  | Acceptable delay time to distribute observation data for collaborators | Data analysis | TBD | not yet |
|  | Data storage capability | Data analysis | TBD | not yet |
|  | Accuracy of time | Data analysis | < 1us | not yet |
|  | Computational capability for GW searches | Data analysis | TBD | not yet |
| * | Network capability | Infrastructure | 10Gbps spec network switches Each 16 ports for 8 DAQ stations | not yet |
| * | Power consumption | Infrastructure | TBD | not yet |
| * | Waist heat | Infrastructure | TBD | not yet |
| * | Location and space | Infrastructure | TBD | not yet |
|  | Installation schedule | ??? | TBD | not yet |
|  | Budget allocation | ??? | TBD | not yet |
|  | Man power allocation | ??? | TBD | not yet |

* This mark adds the items, if this subsystem to be specified the requirement.