Interface Control Document

of the LCGT Project

2010/4/19 (ver 1.23)

LCGT Project

Foreword

This document, Interface Control Document (ICD), defines the interfaces among the subsystems constituting the LCGT (Large scale Cryogenic Gravitational wave Telescope). LCGT project is now in the phase of detailed design which includes finalizing the detailed parameters. That means the interfaces are changing literally day by day; which explains why this document is being updated frequently – every 2 weeks or so. This process of updating the interface will continue until the completion of the LCGT or even beyond. The authorization of the parameter changes will be given at the LCGT collaboration meeting which is held every two weeks.

An Interface Control Document generally defines only the interface between the whole system and its users, but we have chosen a different way to minimize the number of documents thus reducing our workload. As a result, this ICD also includes a brief description of the subsystem and the requirements for each of the subsystems, because we intend to expand this document, in the near future, into covering the Configuration Control Document as well.

This ICD currently is for providing each of the subsystem members of the LCGT  project with the knowledge of other subsystem’s interface parameters and requirements, but it will, as mentioned above, hopefully play in the future the role of describing the design parameters of the whole system.

One may refer to the “LCGT Design Document” for clarifying the premises and the process of determining the parameters given in this ICD which includes only the result of designing, not its process.

Finally let me express my sincere respect and appreciation for all the LCGT members who have contributed to this document and will continuously update it in the future. Let me specifically emphasize that Dr. Osamu Miyakawa has done a great job for providing the computer tool and also for editing this document.

Ichiro Nakatani

Project Manager of LCGT,

Institute for Cosmic Ray Research

The University of Tokyo

Index

- Laser Source Subsystem					5

2. Input Output Optics Subsystem				9

- Interferometer Sensing And Control Subsystem	17

- Digital Control Subsystem					25

- Interferometer Support Subsystem			31

  - Scattered Light Control					32

  - 60Hz Control						36

  - Thermal Lensing Control					40

  - Clean Environment					44

- Vibration Isolation Subsystem				49

- Cryocooler Subsystem					57

- Cryostat Subsystem						63

- Vacuum Subsystem						71

- Data Acquisition Subsystem				75

- Analysis Center Subsystem				79

- Data Analysis Subsystem					83

| Subgroup Name | Laser Source Subsystem |
| --- | --- |
| Subgroup Leader | Norikatsu Mio The University of Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 |  |  |

  - ① サブシステム：レーザー光源

レーザー光源サブシステムは、光源本体、電源、冷却系、制御系、モニター系、インターロックシステム（安全管理用）からなる。また、光源全体は、クリーン環境下におかれる。

②　システムの所掌範囲

光源本体は、半導体レーザー励起Nd:YAGレーザーをベースにした、注入同期レーザーシステムと光増幅器からなる。電源は、商用交流電源から励起LDを駆動する安定化電源、制御系を駆動する安定化電源からなる。冷却系は、励起LDとレーザー結晶を水冷する。制御系は、機械的・光学的な制御素子と制御用電気回路群からなる。モニター系は、レーザー装置の状態を見るための測定器類を総合して言う。インターロックシステムは、緊急事態に備えて、レーザー発振の安全な停止を行なうシステムである。

他のシステムとの接続

- 出力光→入射光学系		光

- 干渉計→制御信号系		電気信号

- モニター系→データ収録系		電気信号

- 施設→電源				商用電源

- 施設→冷却水系			水

- 施設→インターロック系		電気信号

- 施設→光源全体			クリーンルームの設置

- 干渉計→インターロック系		電気信号

③ サブシステムへの要求仕様の整理

  - 出力：150 W

  - 波長：1064 nm

  - 周波数雑音＠100Hz,

  - 強度雑音＠100Hz，

  - 周波数制御帯域	＞1 MHz

  - 入力端子：周波数制御、強度制御、インターロック

  - 出力信号：出力、制御信号レベル、温度、発振モード、内部情報

  - 電源：単相200 V、150A（例起用LD、冷却装置）

  - 電源：単相100 V、100A（制御装置、モニター装置等）

  - クリーン度：クラス100

  - 1次冷却水：15度、流量：TBD

④関連するサブシステム間のインターフェースの定義：

- 出力光→入射光学系

  - 入射光学系の光学モードに合わせて、レーザービームの光学軸の位置・角度（アラインメント）、ビーム半径の調整。

  - アラインメント調整用のミラー角度はデジタル制御可能なマウントを用いる。

- 干渉計→制御信号系

  - 周波数制御信号：アナログ信号、帯域１MHz

  - 強度制御信号：アナログ信号、大域1MHz

  - インターロック：デジタル信号（DC付近）

  - アラインメント制御：デジタル信号（DC付近）

- モニター系→データ収録系

  - 出力：アナログ信号（高速10kHz）、デジタル信号（DC付近）

  - 制御信号レベル：アナログ信号（高速10kHz）、デジタル信号（DC付近）

  - 温度：デジタル信号（DC付近）

  - 発振モード：TBD

  - 内部情報：TBD

- 施設→電源

  - 単相200 V、150A

  - 単相100 V、100A

- 施設→冷却水系

  - 1次冷却水：15度、流量：TBD

- 施設→インターロック系	電気信号

  - 非常事態通報：デジタル信号

- 施設→光源全体	クリーンルームの設置

  - 光源全体は、独立したクリーンルーム内に設置

  - 出入り口のセンサーでインターロックを行なう

  - 干渉計を収納する真空タンクにつながる入射窓フランジは、クリーンルーム内に設置

- 干渉計→インターロック系	電気信号

  - 非常事態通報：デジタル信号

  - アンロック信号：デジタル信号

Interface Control Document

of the LCGT Project

| Subgroup Name | Input-Output Optics Subystem (入射・射出光学系サブシステム) |
| --- | --- |
| Subgroup Leader | Shigenori Moriwaki The University of Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-1 | 2010-04-18 | Kick-off draft |

APPROVAL AUTHORITIES

用語集 / Glossary

| AM | Amplitude modulation |
| --- | --- |
| MC | Mode cleaner |
| MMT | Mode matching telescope |
| FI | Faraday isolator |
| FN | Frequency noise |
| HWP | Half wave plate |
| PBS | Polarizing beam splitter |
| MZM | Mach-Zehnder modulator |
| PM | Phase modulation |
| PRM | Power recycling mirror |
| RIN | Relative intensity noise |
| SEM | Signal extraction mirror |
| WFS | Wave front sensing |

1. 各サブシステムの簡単な定義 / Concise definition of Input-Output Optics Subsystem

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | ハードウェア・ソフトウェア / Hardware, software |
| --- | --- | --- |
| 1 | Mode and RF Sideband Cleaner (MC1) | Suspended triangular ring cavity with 10m baseline in vacuum |
| 2 | Mode Cleaner (MC2) | Suspended triangular ring cavity with 15m baseline in vacuum |
| 3 | Phase Modulator for MC1(PMMC1) | Electro-Optic Modulator for 8MHz (TBD) on the input table |
| 4 | Faraday Isolator for MC1 (FI1) | Faraday rotator and polarizing beamsplitter in vacuum |
| 5 | Mode Matching Telescope for MC1 input (MMT1) | A pair of convex/concave mirrors mounted on the input table |
| 6 | Mode Matching Telescope between MC1 and MZM (MMT2) | A pair of convex/concave mirrors suspended in vacuum |
| 7 | Mach-Zehnder Modulator(MZM) | Mach-Zehnder interferometer which contains electro-optic modulators for 11.25MHz phase and 45MHz amplitude modulations |
| 8 | Faraday Isolator for MC2 (FI2) | Suspended Faraday rotator and polarizing beamsplitter in vacuum |
| 9 | Mode Matching Telescope for MC2 input (MMT3) | A pair of convex/concave mirrors suspended in vacuum |
| 10 | Mode Matching Telescope between MC2 and PRM (MMT4) | A pair of convex/concave mirrors suspended in vacuum |
| 11 | Output mode cleaner (OMC) | Rigid-body ring cavity which excludes deformed component of the anti-symmetric port beam |
| 12 | Mode Matching Telescope between SEM and OMC (MMT5) | A pair of convex/concave mirrors suspended in vacuum |
| 13 | Photo Detectors (PDs) | Length and wave front sensing photodetectors at the Dark Port, the Bright Port and the Pick-off Port |

2. 要求仕様 / Required specifications for Input-Output Optics Subsystem

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Related sub-system(s) | 変更有り/modified | 変更の可能性有り/to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Mode and RF Sideband Cleaner (MC1) | 7.2, 7.3 | Laser |  |  |
| 2 | Mode Cleaner (MC2) | 7.2, 7.3 | ISC |  |  |
| 3 | Phase Modulator for MC1(PMMC1) | 7.3 | Laser, ISC |  |  |
| 4 | Faraday Isolator for MC1 (FI1) | 7.9 | ISC |  |  |
| 5 | Mode Matching Telescope for MC1 input (MMT1) | Not yet | ISC |  |  |
| 6 | Mode Matching Telescope between MC1 and MZM (MMT2) | 7.5 | ISC |  |  |
| 7 | Mach-Zehnder Modulator(MZM) | 7.7 | ISC |  |  |
| 8 | Faraday Isolator for MC2 (FI2) | 7.9 | ISC |  |  |
| 9 | Mode Matching Telescope for MC2 input (MMT3) | 7.5 | ISC |  |  |
| 10 | Mode Matching Telescope between MC2 and PRM (MMT4) | 7.5 | ISC |  |  |
| 11 | Output mode cleaner (OMC) | 7.4 | ISC |  |  |
| 12 | Mode Matching Telescope between SEM and OMC (MMT5) | 7.9 | ISC |  |  |
| 13 | Photo Detectors (PDs) | 7.8 | ISC, Digital System |  |  |

** Section in LCGT Design Document , Version 2

3. インターフェース / Interface of the Input-Output Optics Subsystem

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

この欄は、人ではなくsubsystem 名か↓

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | MC2 output power | ISC | 75W | ISC |
|  | MC2 output spatial mode | ISC, Bandwidth | TEM00, M2<1.1 (waist size and location: TBD) | Not yet |
|  | MC2 output polarization | ISC | S-pol, Is/Ip<0.01 | Not yet |
|  | MC2 output frequency noise | ISC | FN<4x10^-8Hz/rtHz at 100Hz | ISC |
|  | MC2 output intensity noise | ISC | RIN<2x10^-8/rtHz at 100Hz | ISC |
|  | MC2 output beam jitter | ISC | TBD | Not yet |
|  | MC2 output phase modulation | ISC | PM m>(TBD) at f1=11.25MHz, AM g>(TBD) at f2=45MHz, PM m>(TBD) at f_WFS=(TBD). | Not yet |
|  | MC2 output frequency tuning range | ISC | TBD | Not yet |
|  | MC2 output intensity attenuation range | ISC | TBD | Not yet |
|  | MC1 input power | Laser | 150W | ISC |
|  | MC1 input spatial mode | Laser | TEM00, M2<1.2 (waist size and location: TBD) | Not yet |
| * | Power consumption | 坑内施設 | TBD | not yet |
| * | Waist heat | 坑内施設 | TBD | not yet |
| * | Location and space | 坑内施設 | TBD | not yet |
|  | Installation schedule | ??? | TBD | Not yet |
|  | Budget allocation | ??? | TBD | Not yet |
|  | Man power allocation | ??? | TBD | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

Infrastructure (vacuum chambers, beam tubes and opyical benches) for the Input-Output Optics Subsystem:

Locations of the centers and diameters of the vacuum chambers in the center area. The origin of the coordinate is at the center of beamsplitter chamber (BS).

| #name | #description | #posx(m) | #posy(m) | #diameter(m) |
| --- | --- | --- | --- | --- |
| BS | Beamsplitter chamber | 0 | 0 | 2 |
| PRM | Power recycling mirror chamber | -5 | 0 | 2 |
| MC2F | Front chamber for second mode clener | -11 | 0 | 2 |
| MC2E | End chamber for second mode cleaner | -11 | 13.3 | 2 |
| MZM | Mach-Zehnder modulator chamber | -16 | 0 | 1 |
| MC1F | Front chamber for first mode cleaner | -16 | -5 | 2 |
| MC1E | End chamber for first mode cleaner | -6 | -5 | 1 |
| SEM | Signal extraction mirror chamber | 0 | -10 | 2 |
| PD | Photo detection chamber | 0 | -14 | 1 |

Locations and sizes of the optical benches in the center area.

| #name | #description | #posx(m) | #posy(m) | #sizex(m) | #sizey(m) |
| --- | --- | --- | --- | --- | --- |
| benchBSmain | BS main bench | 2 | 2 | 1.5 | 1.5 |
| benchBSInline | BS bench at the inline arm side | 1.8 | -2.2 | 1.5 | 1.5 |
| benchBSPerp | BS bench at the perp. arm side | -1.8 | 2.2 | 1.5 | 1.5 |
| benchDark | Dark port bench | 1.8 | -14 | 1.8 | 2.4 |
| benchSEM | SEM bench | 2 | -10 | 1.5 | 1.5 |
| benchPRM | PRM bench | -5 | -2 | 1.5 | 1.5 |
| benchMC1E | MC1 end bench | -4.2 | -5 | 1.5 | 1.5 |
| benchMC2F | MC2 front bench | -9 | 2 | 1.5 | 1.5 |
| benchMC2E | MC2 end bench | -11 | 15.3 | 1.5 | 1.5 |
| benchBright | Bright port bench | -11 | -2 | 2.4 | 1.8 |
| benchMZM | MZM bench | -16 | 1.8 | 1.5 | 1.5 |
| benchInput | Input bench | -16 | -7.2 | 2.4 | 1.8 |
| benchLaser | Laser bench | -13.2 | -7.2 | 2.4 | 1.8 |

0. サブシステムの現状 / Current status of the Input-Output Optics Subsystem

a) Conceptual design (サブシステムの定義) は確定しましたか？		確定 / 未定

* 未定な部分がある場合、検討項目を簡単に記述して下さい。

* Conceptual design の変更に伴い、予想される影響（検討事項）と関連 sub-group。

b) Alternative design は残っていますか？		残っている / いない

* Alternative design の採用により生じると予想される影響（検討項目）と 関連sub-group。

DCリードアウト導入への対応が保留中。

各光学素子のAR面の残反射光の処理経路、MCに用いる鏡のウエッジ角の大きさが未検討。

Faradayアイソレータの真空内防振・水冷系のデザイン。水冷系の導入で万一破綻した場合、電気光学位相変調アイソレータのデザイン。

熱変形に対するモード補償の機能をMMTや MC1, MC2 に持たせるかどうか。

関連 sub-group: ISC (干渉計制御 sub-group)

c) 今年予算承認されたとした場合、年度内に決定すべき項目と関連 sub-group。

実験室内の配置、消費電力、廃熱量について坑内施設と打ち合わせる必要がある。

| Subgroup Name | Interferometer Sensing And Control Subsystem |
| --- | --- |
| Subgroup Leader | Yoichi Aso The University of Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 |  |  |

## Preface

This is a draft of the ICD for the LCGT-ISC sub-system.

## Sub-System Definition

The role of the Interferometer Sensing and Control (ISC) sub-system is to keep the interferometer at its optimal operation point and extract the gravitational wave signal with low noise. This sub-system can be functionally broken into two parts: Sensing and Control.

### Sensing

In order to control the interferometer, we have to know the state of the interferometer. Sensing part of this sub-system defines the methods to extract information about the state of the interferometer. We sort the degrees of freedom (DOFs) of an interferometer into three categories.

#### Length Sensing

The word "length" here means the distances between the mirrors. In addition to the geometric lengths, a change in the laser frequency also appears as an apparent change in the lengths for an interferometer. Therefore, the laser frequency is counted as a length here. There are 5 length DOFs to be controlled for a Dual-Recycled Fabry-Perot Michelson Interferometer (DRFPMI).

| Name | Notation | Description |
| --- | --- | --- |
| Michelson(MICH) | l- | Differential change of the Michelson arm lengths |
| Power Recycling Cavity Length (PRCL) | l+ | Length of the power recycling cavity |
| Signal Recycling Cavity Length (SRCL) | ls | Length of the signal recycling cavity |
| Differential Arm Length (DARM) | L- | Differential change of the arm cavity lengths |
| Common Arm Length (CARM) | L+ | Common change of the arm cavity lengths |

Out of those DOFs, MICH, PRCL and SRCL are called "central part", "short DOFs" or "スモール系". DARM and CARM are called "arm DOFs", "long DOFs" or "ラージ系". CARM is often regarded as being equivalent to the laser frequency variation. DARM contains the gravitational wave signal, so it is the most important DOF.

#### Alignment Sensing

In order for a laser beam to properly resonate inside the interferometer, the beam and the mirrors of the interferometer must be aligned well. Alignment sensing is a mechanism to monitor errors in the alignment. A mirror has three rotational degrees of freedom, out of which only two (pitch and yaw) are important for an interferometer. For each of pitch and yaw, there are 6 alignment DOFs in an interferometer.

| Name | Description |
| --- | --- |
| Common Stable (CS) |  |
| Common Unstable (CU) |  |
| Differential Stable (DS) |  |
| Differential Unstable (DU) |  |
| Power Recycling Mirror (PRM) |  |
| Signal Recycling Mirror (SRM) |  |

CS, CU, DS, DU are the DOFs of the arms in the Sidles-Sigg basis [ref].

#### Auxiliary Signals

There are other signals which may have to be monitored (and possibly corrected for by feedbacks) during the operation of an interferometer.

| Name | Description |
| --- | --- |
| Thermal lensing | Heat deposited on the mirrors by the laser beam can create a lensing effect. This lens mainly manifests itself as a mismatch of the spatial modes between the recombined beams at the dark port. |
| AS_I | If we use RF readout for the DARM, we may have to monitor the I-phase signal of the AS-port PD, which does not contain any GW signal but comes from junk light at the AS-port. AS-I could saturate the AS-PD in RF and reduce the dynamic range for the GW signal channel (AS-Q). If so, we can feedback the AS-I into the AS-PD current to cancel it. |
| SPOB | SPOB is Sideband Picked Off at Beam-splitter. The light picked off inside the PRC is demodulated at twice the frequency of the sidebands to serve as a measure of the sideband power in the PRC. |

### Control

Once the information about the state of the interferometer is obtained, we feedback the information to keep the interferometer at the optimal operation point. Feedback has to be strong enough to keep the error signals in linear regions so that up-conversion and other noises related to the non-linearity are well suppressed.

The control part consists of two successive components: Filtering and Actuation.

#### Filtering

| Type | Description | Related Subsystems |
| --- | --- | --- |
| Digital | Most of the ISC feedback filters will be implemented as digital filters. | Digital |
| Analog | Analog electronics are used where a wide feedback bandwidth is required.This will be the case mainly for the laser stabilization loops i.e. the frequency and intensity stabilization servos. | IFO support |

#### Actuator

Actuators change the state of an interferometer.

| Name | Description | Related Subsystems |
| --- | --- | --- |
| Suspension actuators | These actuators move the mirrors. This is the realm of the suspension sub-system.ISC group will set requirements for the suspension actuators | Suspension |
| Laser actuators | Laser intensity and frequency has to be controllable with a high bandwidth. | IOO |
| Thermal | If necessary, the thermal deformations of the mirrors have to be compensated by some way, such as illuminating the mirrors with CO2 lasers. | IFO Support |

## Requirements

The requirements for the ISC system ultimately come from the target sensitivity. Again the requirements for the ISC subsystem are divided into Sensing and Control.

### Requirements for Sensing

| DARM | The DARM sensing noise should be below the target sensitivity. |
| --- | --- |
| Other DOFs | The noises in the DOFs other than DARM affect the sensitivity through feedback. The sensing noises should be small enough to allow descent feedback gains for the auxiliary loops. |

### Requirements for Control

| DARM | DARM actuator noise directly appears in the DARM noise spectrum. This has to be kept below the target sensitivity. |
| --- | --- |
| Other DOFs | Actuator noises in the DOFs other than DARM appear in the DARM signal through various couplings. The couplings have to be modeled and estimated to set the requirements for the actuator noises. |

## Interface with Other Sub-Systems

The ISC sub-system is realized by connecting hardware components provided by other sub-systems. So establishing good interface with the related sub-systems is imperative. Since the ISC requirements are set directly from the target sensitivity, ISC sets the requirements for other sub-systems in most cases.

| Issues | Description | Numbers | Related Subsystems | Consensus |
| --- | --- | --- | --- | --- |
| Laser Power |  |  | IOO |  |
| Laser Frequency Noise |  |  | IOO |  |
| Laser Frequency Control |  |  | IOO |  |
| Laser Intensity Noise |  |  | IOO |  |
| Laser Intensity Control |  |  | IOO |  |
| Modulation | 11.15MHz PM & 45MHz AM |  | IOO¦ |  |
| Input Mode Clearner |  |  | IOO |  |
| Output Mode Cleaner | 13.3m | 13.3m | IOO |  |
| Seismic RMS |  |  | Suspension |  |
| Mirror actuators |  |  | Suspension |  |
| Mirror Loss | 45ppm per reflection | 45ppm | Mirror |  |
| Mirror Transmittance |  |  | Mirror |  |
| Mirror Coating |  |  | Mirror |  |
| Folding RCs |  |  | IOO, Mirror, Suspension, Vacuum |  |
| Vacuum Layout | Optical layout of the interferometer determines the layout of the vacuum tubes and chambers. |  | Vacuum |  |
| Vacuum Pressure |  |  | Vacuum |  |
| PD | Requirements for power handling, quantum efficiency, noise, bandwidth etc |  | IOO |  |
| Analog Electronics Standards |  |  | IFO support |  |

| Subgroup Name | Digital Subsystem |
| --- | --- |
| Subgroup Leader | Osamu Miyakawa ICRR U-Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-06-2 | Kick-off draft written in wiki format |
| Rev. A-1 | 2009-08-07 | Converted to MS-Word format |
| Rev. A-2 | 2010-04-15 | Fixed several parameters by the experience at CLIO digital system |

Glossary

| ADC | Analog to Digital Converter |
| --- | --- |
| DAC | Digital to Analog Converter |
| AA | Anti aliasing |
| AI | Anti imaging |
| UGF | unity gain frequency |
| IFO | interfoemter |

- Definition of subsystem

This system provides the functions which digitalize analog sensing signals extracted from interferometers, produce signals in computers for controlling the interferometers and data acquisitions, and re-produce analog signals to actuate the interferometer.

- Task area

| No. | Function | Description, equipments |
| --- | --- | --- |
| 1 | Digital control system | Main system. PC, ADC/DAC, AA/AI filter, whitening/dewhitening filter, real time OS, control software, monitor software, data storage. |
| 2 | Detector tuning system | Adjusts interferometer parameters. Tuning software. |
| 3 | Detector diagnosis system | Interferometer self diagnosis. Diagnosis software. |
| 4 | Long term monitor | Monitor software, data storage |
| 5 | Auto lock / auto alignment sequencer | Real time lock code (fast), auto lock and alignment scripts (slow). |
| 6 | Detector operation system for GW observation | Operators, operation scheduling, auto lock scripts. |
| 7 | GW search data calibration | Real time calibration shown in the control room. Projectors, calibration signals, real time calibration software |
| 8 | Real time data analysis | Real time data analysis shown in the control room. Projectors, real time data analysis software |

3. Required specifications

| Item | Requirements | Comment |
| --- | --- | --- |
| Sampling rate | >16kHz |  |
| Dynamic range of input | >+/-15V | Half on differential |
| Dynamic range of output | >+/-10V | Half on differential |
| ADC noise | <3uV/rHz |  |
| DAC noise | <3uV/rHz |  |
| time delay | <100usec | To realize 300Hz UGF |
| Input channel numbers | >1024ch | (16kHz:>128ch, 2kzHz:>256ch, 64Hz>512ch) |
| Output channel numbers | >256ch | for suspensions, PZTs |
| Stored channel | 16kHz:>64ch, 2kzHz:>256ch, 64Hz>512ch |  |

4. Interface between systems

|  | Item | Related sub-system | Requirements | Agreement |
| --- | --- | --- | --- | --- |
| * | Sampling rate | Data acquisition, Data analysis, IFO control | 16384Hz(sampeled at 65536Hz and decimated to 16384Hz) option:up to 65536Hz for limited number of channels | not yet |
|  | Number of channels | Data acquisition, Data analysis, IFO control | 16kHz:64ch, 2kHz:256ch, 64Hz:512ch 16Hz:2048 epics channels (see channel list) | not yet |
| * | Data bit resolution | Data acquisition | 24bit = 4 Byte integer | not yet |
|  | Data transfer rate | Data acquisition | 4MB/sec for 16kHz, 2MB/sec for 2kHz, 128kB/sec for 64Hz 128kB/sec for 16Hz | not yet |
|  | Saved parameters (using conlog) | Data analysis, IFO control | See parameter list | not yet |
| * | ADC dynamic range | IFO control | Full differential +/-10V = effective range +/-20V | not yet |
| * | DAC dynamic range | IFO control | Full differential +/-5V = effective range +/-10V | not yet |
| * | through delay | IFO control | 80usec | not yet |
| * | ADC noise level | IFO control | 2uV/rHz | not yet |
| * | DAC noise level | IFO control | 1.5uV/rHz | not yet |
| * | AA filter noise level | IFO control | 0.1u V/rHz | not yet |
| * | AI filter noise level | IFO control | 0.1u V/rHz | not yet |
| * | whitening filter noise level | IFO control | 1n V/rHz | not yet |
| * | dewhitening filter noise level | IFO control | 1n V/rHz | not yet |
| * | whitening filter input impedance | IFO control | TBD | not yet |
| * | dewhitening filter output impedance | IFO control | TBD | not yet |
|  | Connector shape | IFO control | D-SUB9 @ AA and AI BNC or SMA (or LEMO) for single 2pin LEMO for differential @ whitening / dewhitening and binary switch | not yet |
| * | Power consumption | Infrastructure | TBD | not yet |
| * | Waste heat and cooling | Infrastructure | TBD | not yet |
|  | Network capability | Infrastructure | 10Gbps ethernet | not yet |
| * | Optical fiber cable capability for real time PC, clock timing system | Infrastructure | TBD | not yet |
|  | GPS antenna | Infrastructure, Data acquisition | TBD |  |
|  | Location and space | Infrastructure, Data acquisition, IFO control | 3 racks at center room, 1 rack at X end room, 1 rack at Y end room for control system 10 racks at data center | not yet |
| * | Remote control switch | Vacuum, Infrasturucture | TTL(0V-5V) | not yet |
|  | Wireless LAN (digital system on laptop PC) | Infrastructure | IEEE802.11n(300Mbps) | not yet |

↑ Mark * on items which this subsystem needs to define.

5. Other related subsystems

| No. | Function | Related sub-system | Description, equipments |
| --- | --- | --- | --- |
| 1 | CCD monitor | IFO support |  |
| 2 | Inter lock | Infrastructure, IFO support |  |
| 3 | Entrance monitor system | Infrastructure |  |
| 4 | Real time monitors at control room | Infrastructure, IFO support, Data acquisition, Data analysis |  |
| 5 | Control PCs at control room | Infrastructure, Data analysis | Linux, 2-3 heads/PC, 10 PCs at least |

6. Channel list

a. 16kHz (total 64ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| Laser | Output laser power[W] | 1 |  |
|  | IFO Input laser power[W] | 1 |  |
| MC | REFL | 1 |  |
|  | MC length feedback | 1 |  |
|  | MC frequency feedback | 1 |  |
| LSC | I&Q dor DARM, CARM, MICH, PRC, SRC, etc. | 10 |  |
|  | error, feedback | 10 |  |
| SUS | length * 10 suspensions | 10 |  |

b. 2kHz (total 256ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| ASC | WFS | 5xpitch, yaw=50 |  |
|  | Oplev | 10xpitch,yaw=100 |  |

c. 64Hz Long term monitor (total 512ch)

| Part | Channel point | Channel number | Description |
| --- | --- | --- | --- |
| Temperature[deg] | room | 10 | center, end, arm |
|  | table | 10 | laser, REFL, AS, pickoff, end |
|  | suspensions | 50 | Low temperature |
|  | mirrors | 50 | Low temperature |
| Humidity[%] | rooms | 10 | center, end, arm |
| Dust | rooms | 10 | center, end, arm |
| Laser | crystal temperature[degree] and etc. | 10 |  |
|  | Master laser power[W] | 2 |  |
|  | Output laser power[W] | 2 |  |
|  | IFO Input laser power[W] | 2 |  |
| Seismic | Room, outside, 3-axis | 30 |  |
| Sound | Room, outside, table |  |  |

7. Saved parameter list

Gain, switch, offset, filter bank, filter on/off, matrix components and all other parameters on Epics channnel

| Subgroup Name | Interferometer Support Subsystem |
| --- | --- |
| Subgroup Leader | Shinji Miyoki ICRR, The University of Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 |  |  |

. '''干渉計サポート'''

* （１）散乱光

おもに、クライオスタットに侵入する300K領域からの輻射の散乱光に起因する熱流量対策について設計する。

ただし、CLIOにおいて、内山君、都丸君による、理論的見積もりの修正、その実験的検証、及び、対策案の実験的結果があるので、それを基本に設計する。

* （２）６０Ｈｚ

鉱山内という岩板環境におけるグラウンドの取り回しと、ハム（60Hz）の低減（撲滅）に関して指針を定める。

* （３）熱レンズ

おもに、溶融石英製のBSにおける熱レンズ効果についてその見積もり、シミュレーション、対策を考える。 ただし、すでにLIGOにより、別レーザーによる光学素子の二次元加熱法が進行しているので、その方法を基本に考える。

その後、LIGOの山本さんが、「高品質な溶融石英が得られれば、BSの熱レンズは考えなくていいのでは」という提案を頂き、その線で行くことにしました。

* （４）クリーン環境

振動源にならないクリーン環境の設置を考える。

| Subgroup Name | Scattered Light Control |
| --- | --- |
| Subgroup Leader | Shinji Miyoki ICRR, UT |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-31 | Kick-off draft |

Glossary

| SLC | Scattered Light Control |
| --- | --- |
| DLC | Diamond Liked Carbon ( coating ) |
| NIP | Nickel Phosphorus ( coating ) |

1. 各サブシステムの簡単な定義 / Concise definition of Scattered Light Control

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するための基本的対策。

| No. | 機能 / Function | 基本的対策 / Policy |
| --- | --- | --- |
| 1 | SLC for Main 3km Duct | - Diamond Liked Carbon (DLC) or NIP Coated Baffles |
| 2 | SLC for Radiation Shield Duct | Diamond Liked Carbon (DLC) or NIP Coated Baffles Radiation Protector coated by DLC or NIP around Mirrors in the inner shield. |
| 3 | SLC for Main IFO Optics | Proper wedge angle Low reflection low scattered loss AR coating Optical dumping set for the high intensity AR reflected light Optical dumping set for the high angle scattered light |
| 4 | SLC for Input Output Optics | HR mirrors are desirable Back side should be polished and AR coated Proper wedge Optical dumping set for the transmitted light |
| 5 | SLC for Vacuum Windows | Proper edge Double AR coated Optical dumping set for the high intensity AR reflected light |
| 6 | SLC for Photo Detectors | Housed in NIP coated box Optical dumping set for the high intensity AR reflected light Optical dumping set for the reflected light fro PDs |
| 7 | SLC for non-Linear Optics | Optical dumping set for the high intensity AR reflected light Brewster angle cutting |
| 8 | SLC for Beam Axes | Iris NIP coated meshed metal tube beam guide |

2. 要求仕様 / Required specifications Scattered Light Control

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Required value | modified | to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | SLC for Main 3km Duct | 14.2 | Less than 1/10 of the targeted Sensitivity (2*10^-21 is designed) |  |  |
| 2 | SLC for Radiation Shield Duct | New | Less than 1/30 of the designed heat for one mirror (~ 300mW) Practical baffles design is proven in CLIK (Tomaru) Practical mirror shield is proven in CLIO (Uchiyama) |  |  |
| 3 | SLC for Main IFO Optics | New | Damp 10ppm loss from one mirror |  |  |
| 4 | SLC for Input Output Optics | New | Not fixed |  |  |
| 5 | SLC for Vacuum Windows | New | Not fixed |  |  |
| 6 | SLC for Photo Detectors | New | Not fixed |  |  |
| 7 | SLC for non-Linear Optics | New | Not fixed |  |  |
| 8 | SLC for Beam Axes | New | Not fixed |  |  |

** Section in LCGT Design Document

3. インターフェース / Interface of the Scattered Light Control

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | SLC for Main 3km Duct | Vacuum SPI | Outgas level | By Vacuum for DLC, not NIP |
| * | SLC for Radiation Shield Duct | Vacuum Cryostat Refrigerator | Refrigerator power to evacuate the heat load from 300K area. | By Cryostat system |
|  | SLC for Main IFO Optics | Vacuum ISC Mirror Coating | Position Scattered light level, angle | Not yet |
| * | SLC for Input Output Optics | Vacuum | Housed in vacuum? | Not yet |
| * | SLC for Vacuum Windows |  |  | not yet |
| * | SLC for Photo Detectors | Clean Environment Sound Environment | Clean air introduction Box material | not yet |
| * | SLC for non-Linear Optics | Input optics | Scattered light level | not yet |
| * | SLC for Beam Axes | Input Optics Design | Layout | not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

| Subgroup Name | 60Hz Control |
| --- | --- |
| Subgroup Leader | Shinji Miyoki ICRR, UT |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-31 | Kick-off draft |

1. 各サブシステムの簡単な定義 / Concise definition of the 60Hz Control

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するための基本的対策。

| No. | 機能 / Function | 基本的対策 / Policy |
| --- | --- | --- |
| 1 | Primary Power Source | Grounding AC line purity enhancement |
| 2 | Secondary Power Source | Noise cut trance introduction AC-AC or AC-DC? conversion |
| 3 | Grounding Control for Instruments | Common ground bar Electro conductive concrete introduction |
| 4 | Signal Cross Talk control | Categorization (RF, AM, AC, DC, Network) Electrical shield introduction Separation between categories |
| 5 | Special Treatment for Specific Instruments | Battery with the auto charge system |
| 6 | Signal Transfer | AM : Differential amp, Isolation amp, Optical coupler RF : Ground cutting using transfer |

2. 要求仕様 / Required specifications of the 60Hz Control

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Required value | modified | to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Primary power source | New | Obey the manufacturer level |  |  |
| 2 | Secondary power source | New | TBD |  |  |
| 3 | Grounding control for instruments | New | Grounding Copper Bar Introduction |  |  |
| 4 | Signal cross talk control | New | TBD |  |  |
| 5 | Special treatment for specific instruments | New | TBD |  |  |
| 6 | Signal transfer | New | TBD |  |  |

** Section in LCGT Design Document

3. インターフェース / Interface of the 60Hz Control

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
| 1 | Primary power source and grounding | Facility | TBD | Not yet |
| 2 | Secondary power source | Facility | TBD | Not yet |
| 3 | Grounding control for instruments | Facility | TBD | Not yet |
| 4 | Signal cross talk control | Facility | TBD | Not yet |
| 5 | Special treatment for specific instruments | Data taking Data analysis Facility | TBD | not yet |
| 6 | Signal transfer | Data taking Data analysis Facility | TBD | not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

| Subgroup Name | Thermal Lensing Control |
| --- | --- |
| Subgroup Leader | Shinji Miyoki ICRR, UT |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-31 | Kick-off draft |

1. 各サブシステムの簡単な定義 / Concise definition of the Thermal Lensing Control

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するための基本的対策。

| No. | 機能 / Function | 基本的対策 / Policy |
| --- | --- | --- |
| 1 | Beam Splitter | Prepare super low absorption loss SiO2 ( < 0.1ppm/cm, possibly 0.02 ppm/cm), which will be prepared in Ad-LIGO, then minimize thermal lensing problem For the worst case, the thermal compensation method used in LIGO will be introduced. |
| 2 | Non-Linear Optics | Apply beam profile design accounting for the thermal lensing. Wider beam introduction into the EOMs and Faraday Isolators. |
| 3 | Mode Cleaner | Design to set the wider beam size on the mirrors |
| 4 | Input Test Mass (option) | Prepare super low absorption loss SiO2 ( < 0.1ppm/cm) which will be prepared in Ad-LIGO, then minimize thermal lensing problem |

2. 要求仕様 / Required specifications  the Thermal Lensing Control

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Required value | modified | to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Beam Splitter | New | Absorption loss < 0.1ppm/cm for SiO2 Coating Absorption loss < 0.5 ppm? |  |  |
| 2 | Non-Linear Optics | 7.7 7.9 | TBD |  |  |
| 3 | Mode Cleaner | 7.2 | Absorption loss : no problem Coating Absorption loss < 0.5 ppm? |  |  |
| 4 | Input Test Mass (option) | New | Absorption loss < 0.1ppm/cm for SiO2 |  |  |

** Section in LCGT Design Document

3. インターフェース / Interface of the Thermal Lensing Control

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
| * | Beam Splitter |  |  | Not yet |
| * | Non-Linear Optics | Input Optical System Design | Adjustable optical layout | Not yet |
| * | Mode Cleaner | Input Optical System Design | Adjustable optical layout | Not yet |
| * | Input Test Mass (option) | Mirror | Absorption loss < 0.1ppm/cm for SiO2 | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

| Subgroup Name | Clean Environment |
| --- | --- |
| Subgroup Leader | Shinji Miyoki ICRR, UT |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-31 | Kick-off draft |

1. 各サブシステムの簡単な定義 / Concise definition of the Clean Environment Control

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するための基本対策。

| No. | 機能 / Function | 基本対策 / Policy |
| --- | --- | --- |
| 1 | Primary Clean Air (C class) | Production at out of the tunnel Class 10000 Transfer the air to secondary clean air production |
| 2 | Secondary Clean Air (B class) | Production at the access tunnel area. Class 1000 For a part of 3km tunnel near cryostat, Center, End stations, for cleaning before mechanics and electronics installing A part of the air directly introduced to (A, S class) air production instruments |
| 3 | Special Clean Air (A class) | Optics assembly area (Working bench, Cryostat area) Class 100 |
| 4 | Super Clean Air (S Class) | Mirror assembly area Class <100 |

2. 要求仕様 / Required specifications for the Clean Environment Control

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Required value | modified | to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Primary Clean Air (C class) | New | Class 10000 |  |  |
| 2 | Secondary Clean Air (B class) | New | Class 1000 |  |  |
| 3 | Special Clean Air (A class) | New | Class 100 |  |  |
| 4 | Super Clean Air (S Class) | New | < Class 100 |  |  |

** Section in LCGT Design Document

3. インターフェース / Interface of the Clean Environment Control

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
| * | Primary Clean Air (C class) | Facility | Space Cost | Not yet |
| * | Secondary Clean Air (B class) | Facility | Space Cost Tunnel design Meshed floor | Not yet |
| * | Special Clean Air (A class) | Facility | Cost Meshed floor | Not yet |
| * | Super Clean Air (S Class) | Facility | Cost Meshed floor | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

Interface Control Document of LCGT

| Subgroup Name | Vibration Isolation System |
| --- | --- |
| Subgroup Leader | Ryutaro Takahashi National Astronomical Observatory of Japan |
| Sub-leader | Takashi Uchiyama Institute for Cosmic Ray Research |
| Sub-leader | Shinji Miyoki Institute for Cosmic Ray Research |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-2 | 2010-04-15 | Reviced draft |

APPROVAL AUTHORITIES

Concise definition of vibration isolation system

System requirement

Displacement of the test mass mirrors must be less than 6x10-18m/Hz1/2 at 5Hz where the seismic noise and the radiation pressure noise are crossed. RMS motion must be less than 0.1m. The test mass mirrors are cooled to 20K through heat links.

SAS

Core optics are suspended by SASs. Two kinds of SASs are used in LCGT. Type-A SAS consists of an IP, three stage MGAS filters and a cryogenic mirror suspension. Type-B SAS consists of an IP, two stage MGAS filters and a mirror suspension. Type-A SASs are used for FM1, FM2, EM1 and EM2. Type-B SASs are used for BS, PRM, SEM, MC2F and MC2E.

Stack

Three stage stacks are used for BS, PRM, SEM, MC2F, MC2E, MC1F, MC1E, MMT and PD. Rubbers are enclosed by welded bellows. Some optics are placed on the stage 0.

Glossary

| SAS | Seismic Attenuation System |
| --- | --- |
| IP | Inverted Pendulum |
| MGAS | Monolithic Geometric Anti Spring |
| PF | Platform |
| IM | Intermediate Mass |
| MB | Magnet Box |
| TM | Test Mass |
| RM | Recoil Mass |
| ACC | Accelerometer |
| LVDT | Linear Variable Differential Transformer |
| FM | Front Mirror |
| EM | End Mirror |
| BS | Beam Splitter |
| PRM | Power Recycling Mirror |
| SEM | Signal Extraction Mirror |
| MC | Mode Cleaner |
| MMT | Mode Matching Telescope |
| PD | Photo Detector |

Figure: Schematic drawing of the vibration isolation system.

Table: Specification of the vibration isolation system

|  |  |  |  | # |  | Electric | Interface |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type-A SAS |  | 4 |  |  | Vacuum |
|  | Inverted pendulum (IP) |  |  |  |  |  |
|  |  | Leg | 30mHz | 3 |  |  |  |
|  |  | ACC | <10-10m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | LVDT | <10-8m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | Actuator | 10mm/V | 3 |  | DC15V | Control |
|  |  | Moter slider | H | 3 |  | DC12V | Control |
|  | Filter0 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | H-LVDT | <10-8m/Hz1/2@1Hz | 1 |  | DC15V | Control |
|  | Filter1 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | H-LVDT | <10-8m/Hz1/2@1Hz | 1 |  | DC15V | Control |
|  | Filter2 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.5Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | H-LVDT | <10-8m/Hz1/2@1Hz | 1 |  | DC15V | Control |
|  |  | Piezo-moter | Yaw | 1 |  | ? | Control |
|  | Platform (PF) | 120kg, 14K |  |  |  |  |
|  |  | mini-GAS | V: 0.7Hz | 4 |  |  |  |
|  |  | Piezo-moter | V | 4 |  | ? | Control |
|  |  | Moter slider | H | 2 |  | DC12V | Control |
|  |  | Position Sensor | <10-9m/Hz1/2@1Hz | 8 |  | DC15V | Control |
|  |  | Actuator | 1mm/V | 8 |  | DC15V | Control |
|  |  | Heat link | H: 14mHz, V: 8mHz, 1W |  |  |  | Cryostat |
|  | Intermediate mass (IM) | 60kg, 15K |  |  |  |  |
|  |  | Heat link | 1W |  |  |  | Cryostat |
|  | Magnet block (MB) | 60kg, 14K |  |  |  |  |
|  |  | Position Sensor | <10-9m/Hz1/2@1Hz | 6 |  | DC15V | Control |
|  |  | Actuator | 0.1mm/V | 6 |  | DC15V | Control |
|  | Test mass (TM) | 30kg, 20K |  |  |  | Optics |
|  | Recoil mass (RM) | 30kg, 15K |  |  |  |  |
|  |  | Actuator | 0.01mm/V | 4 |  | DC15V | Control |

|  |  |  |  | # |  | Electric | Interface |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type-B SAS |  | 5 |  |  | Vacuum |
|  | Inverted pendulum (IP) |  |  |  |  |  |
|  |  | Leg | 30mHz | 3 |  |  |  |
|  |  | ACC | <10-10m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | LVDT | <10-8m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | Actuator | 10mm/V | 3 |  | DC15V | Control |
|  |  | Moter slider | H | 3 |  | DC12V | Control |
|  | Filter0 | 60kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | H-LVDT | <10-8m/Hz1/2@1Hz | 1 |  | DC15V | Control |
|  | Filter1 | 60kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | H-LVDT | <10-8m/Hz1/2@1Hz | 1 |  | DC15V | Control |
|  |  | Piezo-moter | Yaw | 1 |  | ? | Control |
|  | Platform (PF) | 60kg |  |  |  |  |
|  |  | mini-GAS | V: 2Hz | 4 |  |  |  |
|  |  | Piezo-moter | V | 4 |  | ? | Control |
|  |  | Moter slider | H | 2 |  | DC12V | Control |
|  |  | Position Sensor | <10-9m/Hz1/2@1Hz | 8 |  | DC15V | Control |
|  |  | Actuator | 1mm/V | 8 |  | DC15V | Control |
|  | Intermediate mass (IM) | 30kg |  |  |  |  |
|  | Magnet block (MB) | 30kg |  |  |  |  |
|  |  | Position Sensor | <10-9m/Hz1/2@1Hz | 6 |  | DC15V | Control |
|  |  | Actuator | 0.1mm/V | 6 |  | DC15V | Control |
|  | Test mass (TM) | 16kg |  |  |  | Optics |
|  | Recoil mass (RM) | 16kg |  |  |  |  |
|  |  | Actuator | 0.1mm/V | 4 |  | DC15V | Control |

|  |  |  |  | # |  | Electric | Interface |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Stack |  | H: 2Hz | 9 |  |  | Vacuum |
|  | Stage 0 |  |  |  |  |  |
|  |  | Breadboard | 200kg | 1 |  |  |  |
|  |  | Bellows |  | 3 |  |  |  |
|  |  | Rubber |  | 3 |  |  |  |
|  | Stage 1 |  |  |  |  |  |
|  |  | Block | 200kg | 3 |  |  |  |
|  |  | Bellows |  | 9 |  |  |  |
|  |  | Rubber |  | 9 |  |  |  |
|  | Stage 2 |  |  |  |  |  |
|  |  | Block | 200kg | 3 |  |  |  |
|  |  | Bellows |  | 9 |  |  |  |
|  |  | Rubber |  | 9 |  |  |  |
| General requirement |  |  |  | Band | Interface |
|  | PSD displacement | 6x10-18m/Hz1/2 |  |  | 5Hz |  |
|  | RMS displacement | 0.1m |  |  | 0.1-4Hz | Control |
|  | RMS velocity | 0.1m/s |  |  | DC-4Hz | Control |
|  | RMS pitch | 10nrad |  |  | 1-10Hz | Control |
|  | RMS pitch | 1rad |  |  | 0.1-1Hz | Control |
|  | RMS yaw | 10nrad |  |  | 1-10HZ | Control |
|  | RMS yaw | 1rad |  |  | 0.1-1Hz | Control |

| Subgroup Name | Cryocooler System |
| --- | --- |
| Subgroup Leader Subleader | Toshikazu Suzuki High Energy Accelerator Research Organization Tomiyoshi Haruyama High Energy Accelerator Research Organization |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. 1 | 2010-04-16 |  |

APPROVAL AUTHORITIES

略語集 / Acronyms and Abbrebiations

| PTC | Pulse Tube Crycooler |
| --- | --- |
| VRS | Vibration Reduction Stage |

基本的構成はCLIOで使用している低振動冷凍機システムを踏襲する。上図の如く、パルス管冷凍機に防振対策を施し、他の機器への振動伝搬を防ぐ。この防振方式での低振動化の限界は設置された床面の振動レベルであると考えられる。

1. 各サブシステムの簡単な定義 / Concise definition of Cryocooler System

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | ハードウェア・ソフトウェア / Hardware, software |
| --- | --- | --- |
| 1 | Generation of low temperature | Pulse Tube Cryocooler with 2 stages. Rotary valve unit must be separable. |
| 2 | Anchoring Cold Head of cryocooler on the floor | Rigid frame for PTC cold head. |
| 3 | Vibration reduction stage | Rigid support with small thermal conductance. Flexible heat link. |
| 4 | Anchoring valve unit on the floor | Rigid support for valve unit and rigid piping to the PTC cold head. |
| 5 | Circulating pressured He gas. | Helium gas compressor with low acoustic noise. Flexible tube connections to the valve unit. |
| 6 | Heat transport path from Cryostat | Heat conductor, thermal insulator and mechanical support. Flexible connection for heat conductor. Rigid support for heat conductor. |
| 7 | Floor for rigid anchoring | Stable and rigid ground. |
| 8 |  |  |

2. 要求仕様 / Required specifications for Cryocooler System

１で示した機能に対する要求仕様が記述されている LCGT design document version 3(2009年11月) での section 番号、関連 sub-system、Design document version 3 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Related sub-systems | 変更有り modified | 変更の可能性有り to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Generation of low temperature | 11.2.1 | Laser power, mirror absorption, cryostat thermal insulation, efficiency of heat transport. |  |  |
| 2 | Anchoring Cold Head of cryocooler on the floor | 11.2.2 |  |  |  |
| 3 | Vibration reduction stage | 11.2.2 | Cryocooler, heat transport, anchoring structure. |  |  |
| 4 | Anchoring valve unit on the floor | 11.2.2 |  |  |  |
| 5 | Circulating pressured He gas. |  | Electric line, cooling wwater. |  |  |
| 6 | Heat transport path from Cryostat | 11.1、11.2.3、10.2, (14.3), | High purity metal (bar or wires), termination/connection of thin wire bundle, mechanical support (material, structure) |  |  |
| 7 | Floor for rigid anchoring | 11.2.2、19.4 |  |  |  |
| 8 |  |  |  |  |  |

** Section in LCGT Design Document , Version 3

3. インターフェース / Interface of the Cryocooler System

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | Cooling power at Cryostat connection | Cryostat, Suspension design |  |  |
|  | Vibration at Cryostat connection | Cryostat, Suspension design |  |  |
|  | Cooling water. Available flow rate, temperature. | Construction, Facilities |  |  |
|  | Power consumption of compressor | Construction, Facilities |  |  |
|  | Tolerance of vibration and acoustic noise environment. | Vibration isolator, other equipments |  |  |
|  | Location of cryostat. Configuration of cryocooler systems. | Optics, Construction, Facilities |  |  |
|  | Working space around cryostat. | Construction, Facilities |  |  |
|  | Installation schedule |  |  |  |
|  | Budget allocation |  |  |  |
|  | Man power allocation |  |  |  |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

0. サブシステムの現状 / Current status of the Cryocooler System

a) Conceptual design (サブシステムの定義) は確定しましたか？		確定 / 未定

* 未定な部分がある場合、検討項目を簡単に記述して下さい。

b) Alternative design は残っていますか？		残っている / いない

* Alternative design の採用により生じると予想される影響（検討項目）と 関連sub-group。

CLIOでは使えた低振動化技術がLCGTでは不十分であった場合：方針は同じで撚り徹底した対策を行う事になるだろう。別方法での冷凍機防振はアイデア段階では存在するが、CLIO方式のレベルまでには達していない。CLIO方式の低振動冷凍機で手がつけられていない数10Hz以上の音響域での冷凍機騒音も含めた振動が問題になった場合は新たな対策を講じる必要がある。

冷凍機の選択：使用する冷凍機の台数を少なく抑えるには、1台当たりの冷凍能力の大きい機種が望ましい。想定している防振方法により低振動化の期待出来る機種は、国産品ではCLIOに使用しているのと同じ4Kで0.5W出るが、外国製品まで含めると4K　1.5Wが存在する。外国製品の場合問題になる可能性があるのは科学的・技術的な点ではなく、法律的な面で、これまでに使用前例も明確な法適用判断も無いのでこの点は不明のまま残っている。

クライオスタットの断熱性能によっては、冷凍機台数の増加を見込まなければならない。

関連 sub-group:

c) 今年予算承認されたとした場合、年度内に決定すべき項目と関連 sub-group。

冷凍機機種決定。法的判断も含めて使用可能な冷凍機を選定し、防振仕様への改造のための具体的設計。

鏡懸架、低温部中間質量、クライオスタット内ヒートリンク、常温防振部との結合、熱輸送路仕様（熱的、機械的）、VRS寒冷端での熱と振動の受渡限界の設定。

光学計設計、真空系

| Subgroup Name | Cryostat System |
| --- | --- |
| Subgroup Leader Subleader | Toshikazu Suzuki KEK Yoshio Saitoh KEK Ryutaro Takahashi NAOJ Shinji Miyoki ICRR Takashi Uchiyama ICRR Nobuhiro Kimura KEK |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. 0 | 2010-04-16 | Kick-off draft |

APPROVAL AUTHORITIES

略語集 / Acronyms and Abbrebiations

| MLI or SI | Multi Layer Insulator or Super Insulator |
| --- | --- |
| e | Emissivity |
| SUS | Stainless Steel |
| ECB | Electro Chemical Buffing |
| MCP | Mechano Chemical-Polish |
| DLC | Diamond Like Carbon |

1. 各サブシステムの簡単な定義 / Concise definition of Cryostat System

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | ハードウェア・ソフトウェア / Hardware, software |
| --- | --- | --- |
| 1 | Vacuum for thermal insulation | Vacuum tank |
| 2 | Thermal insulation | Metal shields or MLI or SI |
| 3 | Support for cryogenic parts | Cryogenic wall with stable temperature and with sufficient low vibration. |
| 4 | Heat transport to cooling unit | Heat links. Thermal conductor. Thermal insulator. Supporting mechanism. |
| 5 | Install and tune for experiments. | Access hole or door. Space for works. Avoid contamination. |
| 6 | Cooling down and warming up | Design for releasing thermal stress. Heat switch. |
| 7 | Floor for mechanical anchoring | Stable and rigid ground. |
| 8 | Avoid thermal radiation from vacuum duct | Shield pipe along duct. Cryogenic baffles. |
| 9 | Avoid molecular drift from vacuum duct | Shield pipe along duct. Cryogenic baffles. Defrost mechanism for cryogenic mirror. |

2. 要求仕様 / Required specifications for Cryostat System

１で示した機能に対する要求仕様が記述されている LCGT design document version 3 での section 番号、関連 sub-system、Design document version 3 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Related sub-systems | 変更有り modified | 変更の可能性有り to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Vacuum for thermal insulation | 10 |  |  |  |
| 2 | Thermal insulation | 10, 11.1.1 |  |  |  |
| 3 | Support for cryogenic parts | 10 |  |  |  |
| 4 | Heat transport to cooling unit | 10 |  |  |  |
| 5 | Install and tune for experiments. |  |  |  |  |
| 6 | Cooling down and warming up |  |  |  |  |
| 7 | Floor for mechanical anchoring | 10, 11.2.2、19.3 |  |  |  |
| 8 | Baffle for radiation | Appendix B, 15.4 |  |  |  |
| 9 | Baffle or trap for gas molecule |  |  |  |  |

** Section in LCGT Design Document , Version 3

3. インターフェース / Interface of the Cryostat System

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | Vacuum | Vacuum system, degassing rate, influence for optics |  |  |
|  | Thermal insulation | Thermal insulator. Support. Cryocooler for shield. |  |  |
|  | Support for cryogenic parts | Temperature, vibration level. |  |  |
|  | Access hole or door | Size, structure, numbers, |  |  |
|  | Time of cooling down and warming up | Cryocooler. Adopt or omit heat switch. |  |  |
|  | Location of cryostat. Configuration of cryocooler systems. | Optics, Construction, Facilities |  |  |
|  | Working space around cryostat. | Construction, Facilities |  |  |
|  | Installation schedule |  |  |  |
|  | Budget allocation |  |  |  |
|  | Man power allocation |  |  |  |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

0. サブシステムの現状 / Current status of the Cryocooler System

a) Conceptual design (サブシステムの定義) は確定しましたか？		確定 / 未定

* 未定な部分がある場合、検討項目を簡単に記述して下さい。

断熱方式：MLI（SI）はコンパクトかつ高性能な断熱方法である一方、常温で超高真空を要求する部品と同じ空間に置くことは問題がある。その為、MLIに代わる断熱法が可能か急遽検討中である。候補の一つは300Kからの熱輻射を比較的少数の金属板層で遮る方法で、使用する金属表面は赤外域も含む高反射率が要求される。測定装置と試料の準備を進めている。予備実験として波長2mm~22mmでの放射率e（＝1-反射率）を放射計で測定した結果を最終ページ表1に載せる。

上記金属板層での断熱が可能になった場合、伝導による熱侵入推定、金属板層の支持方法、振動対策。

クライオスタット内のヒートリンク構造。

常温防振装置との結合。

b) Alternative design は残っていますか？		残っている / いない

* Alternative design の採用により生じると予想される影響（検討項目）と 関連sub-group。

a)で記述した断熱法が使用できないと判断された場合、MLIと超高真空をどのように両立させるか。この問題に対しての具体的なデザインはまだない。構造的に複雑化は免れないが、クライオスタット組み立て作業、実験との干渉についての検討も未着手。

関連 sub-group:

c) 今年予算承認されたとした場合、年度内に決定すべき項目と関連 sub-group。

断熱方式の見極め。それによる予算への影響。

[表.1] 表面放射率の測定結果

| 測定器 | ジャパンセンサーTSS-5X | e=0.06標準面にてオフセット調節後、e=0.94標準面にてゲイン調節。黒体炉からの放射が被測定物の温度上昇を引き起こすため、時間をかけた測定ではeの値が動くので注意。 |
| --- | --- | --- |
| 室温 | 17℃ |  |
| 材料 | 放射率 e | 備考 |
| Cu | 0.08 | 無酸素銅＝フライス加工＋化学研磨＋クロメート処理 |
| Al | 0.07 | 圧延材、厚さ1mm。ピカール磨き面。 |
| Al | 0.08 | 圧延材、厚さ1mm。そのままの面。 |
| Al | 0.06 | 調理用フォイル。厚さ20micron。 |
| アルピカ | 0.07 | A5052 アルピカ/機械加工(Ra=0.86μm：レーザー顕微鏡） |
| SUS | 0.13 | 圧延材、厚さ1mm。ピカール磨き面。 |
| SUS | 0.14 | 圧延材、厚さ1mm。そのままの面。 |
| SUS | 0.11 | ステンレス鋼＝SUS316L＋ECB（electrochemical-buffing）処理 |
| SUS+ECB+DLC | 0.33 | DLCは1micron吸収用の厚さ。 |
| Ti | 0.17 | チタンJIS-2種＝MCP（mechanochemical-polish)処理 |
| Cu95%+Al5% | 0.08 | GRAILの素材。 http://www.minigrail.nl/ ピカール磨き面。 |
| M2052+ECB | 0.15 | 加工＋ＥＣＢ |
| M2052そのまま | 0.35 | 酸化物被覆表面。 |
| Super Insulator | 0.06 | Al蒸着面。 |
| Super Insulator | 0.14 | Mylar（デュポン：ポリエステル）面。 |
| Si | 0.56 | 研磨面。結晶方位不明。 |
| Sapphire | 0.59 | HEM法。厚さ2mm。研磨c面。Al箔の上に置いて測定。 |
| Sapphire | 0.6 | Kyropoulos法。厚さ5mm。研磨面。方位不詳。Al箔の上に置いて測定。 |
| G10 | 0.83 | 厚さ15mm。繊維に平行な面。 |
| Polyethylene_H | 0.85 | Eccostock CPE、高密度ポリエチレン。 |
| Polyethylene_L | 0.78 | 厚さ2mm、低密度ポリエチレン。 |
| ニトリルゴム | 0.81 | 厚さ10mm。 |
| シリコンゴム | 0.91 | 厚さ1mm。 |
| ポバール | 0.85 | 洗濯糊ゴーセンをヨードチンキで着色後乾燥。 |
| 紙 | 0.91 | オゾンR(再生紙) |
| Kaptonテープ | 0.81 | 厚さ70micron。Al板に貼り付け。Kapton（デュポン：ポリイミド） |
| TSS-5X ： | 定温度放射源からのIRの反射量検出。測定波長域 2micron ~ 22micron |
| ECB ： | ElectroChemical-Buffing 電界複合研磨 |
| MCP ： | MechanoChemical-Polish |
| DLC ： | Diamond Lile Carbon coating |
| M2052 ： | Mn73%、Cu20%、Ni5%、Fe2%、の合金。常温から低温まで低Q値の制振材。 |
| G10 ： | ガラス繊維強化エポキシ樹脂 |
| Eccostock CPE ： | マイクロ波透過用素材（Emerson & Cuming） |
| 2010.4.6 | ULVAC超材料研 稲吉氏の協力により測定。 |
|  | 斎藤、高橋、鈴木。 |

| Subgroup Name | Vacuum subsystem |
| --- | --- |
| Subgroup Leader | Yoshio Saito KEK-High Energy Accelerator Research Organization |
| Sub-leader | Ryutaro Takahashi National Astronomical Observatory of Japan |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-28 | Kick-off draft |

Concise definition of vacuum system

Beam tube

Two 3-km vacuum tubes are kept in 2x10-7Pa of vacuum pressure so as to reduce scattering-effects due to residual gas molecules.

The stainless-steel material SUS304L or SUS316 is among the most available for use as long tubes of 3km long and 1m in diameter. Since baking over the entire system of long tubes is not easy, further requiring a large electric power supply, some kinds of surface processing methods for reducing outgas are necessary to be applied to the unit tubes before installation in the tunnel. The ECB method is practically advantageous for large-chamber applications, because it can be performed without any large liquid reservoir or large coating system.

Baffles are characteristic of the beam tubes. The scattered light from the surface of tubes is blocked by the baffle. The surface of the baffle is treated with DLC coatings.

Chamber

Four kinds of vacuum chambers are used in LCGT. The size of each type is dependent in the structure of vibration isolation system for mirrors which are placed in the chamber; SAS + cryogenic mirror suspension in Type A chamber, SAS + mirror suspension in Type B chamber, and stack + mirror suspension in Type C chamber. The stainless-steel material SUS304 is among the most available for use as also large chambers of 1-2m in diameter.

Thirteen chambers are connected by the beam tubes with gate valves of DN1000 or DN400 each other.

Pumping system

From atmospheric pressure to several tens of Pa, a mechanical pump is first operated. A dry pump of the roots type equipped with multi-stages, recently being developed to reach a lower ultimate pressure of several Pa, is available.

To evacuate the system, 67 pumping units are placed at each chamber and every 100m along the 3-km tubes. After the tube pressure is reduced to be on the order of 10-5Pa by operating turbo-molecular pumps, Spatter ion pumps are considered to be most convenient for further pumping and keeping the vacuum.

Glossary

| SAS | Seismic Attenuation System |
| --- | --- |
| ECB | Electro-Chemical Buffing |
| DLC | Diamond-Like Carbon |
| TMP | Turbo Molecular Pump |
| SIP | Spatter Ion Pump |

Figure: Schematic drawing of the vacuum-system design.

Table: Specification of the vacuum system

| Subgroup Name | Data Acquisition System |
| --- | --- |
| Subgroup Leader | Daisuke Tatsumi National astronomical observatory of Japan |

Glossary

| GPS | Global Positioning system |
| --- | --- |
| DAQ | Data Acquisition System |
| ADC | Analog to Digital Converter |
| bps | bit per second (a unit to indicate data flow capability) |

1. Definition of subsystem

This subsystem should collect data from an interferometric detector.

Data storage, distribution and pre-procession for GW search are also provided for collaborators.

2. Task area

| No. | Function | Hardware, software |
| --- | --- | --- |
| 1 | Main DAQ system | Analog Digital Converter, Signal conditioning filter (whitening filter) |
| 2 | Frame Maker | Computer: Real time operation system to storage data with GW FRAME FORMAT. |
| 3 | Detector Diagnosis | Computer: Online data analysis soft for detector diagnosis and trend-data archive |
| 4 | Environment Monitor | Computer: Environmental data monitoring soft, display for user interface. |
| 5 | Time Keeper and Global Positioning System | GPS, GPS signal transmission system, GPS time server with Rubidium atomic clock, sampling clock distribution system for ADC and DAC. |
| 6 | Raw Data Archive | Computer, tape archive system and data storage system: Archived data database and its human interface. |
| 7 | Pre Analysis Server | Computer: Data re-formatting for GW signal search |
| 8 | Data Distribution | Computer and high-speed network: Data distribution system for collaborator's demands |

2. Required specifications

|  | Item | Requirements |
| --- | --- | --- |
| Main DAQ | Sampling rate | 32768 Hz (down-sample from 65536 Hz) |
|  | Number of channels | 32 |
|  | Bit resolution | 24 bit (4 byte integer) |
|  | Anti-alias filter | 10 kHz cut-off |
|  | Data rate | 4 MB/sec |
|  | Frame length | 1 second (32768 samples) |
| Frame builder | Operation system | UNIX |
|  | (minimum) Hard disk | 14.4 GB/hour x 70 hours = 1 TB |
|  | Network interface | Gigabit Ethernet with optical fiber |
| Detector diagnosis | Sampling rate | 16384 Hz (down-sample from 65536 Hz) |
|  | Number of channels | 512 CH = 64 CH x 8 stations |
|  | Bit resolution | 16 bit (2 byte integer) |
|  | Anti-alias filter | 5 kHz cut-off |
|  | Data rate | 2 MB/sec x 8 stations |
| Environmental monitor | Sampling rate | 32 Hz (down-sample from 65536 Hz) |
|  | Number of channels | 512 CH = 64 CH x 8 stations |
|  | Bit resolution | 16 bit (2 byte integer) |
|  | Anti-alias filter | 10 Hz cut-off |
|  | Data rate | 2 kB/sec x 8 stations |
| Timing system and Global Positioning System | Time accuracy | < 1 micro sec |
| Raw data archive | from Main DAQ | 4 MB/sec | = 14.1 GB/hour |
|  | from Diagnosis | 2 MB/sec x 8 | = 56.3 GB/hour |
|  | from Environmental | 2 kB/sec x 8 | = 0.05 GB/hour |
|  | Total data rate | 20 MB/sec | = 70.4 GB/hour |
|  | Total data storage | 100 TB in minimum |
| Pre analysis server | Computing power | 300G Flops in minimum |
| Data Distribution | Network interface | Gigabit Ethernet with optical fiber |

3. Interface between systems

| Item | Related sub-system | Requirement | Confirmation |
| --- | --- | --- | --- |
| Observation band | Data analysis | 10 Hz - 10 kHz | by DAS |
| ADC bit resolution | Data analysis | > 16 bits | by DAS |
| Number of channels for GW search | Data analysis | 32 channels | by DAS |
| Pre-processed data formats | Data analysis | TBD | not yet |
| Acceptable delay time to distribute observation data for collaborators | Data analysis | < 1 hour | not yet |
| Data storage capability | Data analysis | 100T bytes in minimum | not yet |
| Accuracy of time | Data analysis | < 1us | not yet |
| Computational capability for GW searches | Data analysis | 300G Flops in minimum | not yet |
| Network capability | Infrastructure | 10Gbps spec network switches Each 16 ports for 8 DAQ stations | not yet |
| Power consumption | Infrastructure | 100 kW | not yet |
| Waist heat | Infrastructure | 90 kW | not yet |
| Location and space | Infrastructure | 24 m2 + 8 Racks | not yet |
| Installation schedule | Management | until 4th year end | not yet |
| Budget allocation | Management | 50,000,000 Jpn Yen | not yet |
| Man power allocation | Management | 2 person x 5 years | not yet |

| Subgroup Name | Analysis Center Subsystem |
| --- | --- |
| Subgroup Leader | Hirotaka Takahashi Nagaoka University of Technology |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-06-02 | Kick-off draft |

Glossary

| GW | Gravitational Wave |
| --- | --- |
| DAQ | Data Acquisition Subsystem |
| ACS | Analysis Center Subsystem |
| grid | The application of several computers to a single problem at the same time |
| GRB | Gamma Ray Bursts |
| SN | Supernovae |
| Processed data | Calibrated data in strain h, including detector information which need for analysis |

1. 各サブシステムの簡単な定義 / Concise definition of Data Analysis

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | Hardware, Software |
| --- | --- | --- |
| 1 | Computing power and software for event searches | Main Server, Network infrastructure, C, Matlab, etc. |
| 2 | Interface for grid computing as an international GW detector network | GRID server for distributed computing environment, Network infrastructure |
| 3 | Interface for LCGT collaborators as data center including document control | Main Server, Network infrastructure, Library management software (e.g. CVS) |
| 4 | Calibration Routine | Software and parameter table for calibration |
| 5 | Interface for external triggers such as GRB and SNs. | Main Server, Network infrastructure, C, Matlab, etc. |
| 6 | GW alert system | Main Server, Network infrastructure, C, Matlab, etc. |
| 7 | Interface for distributed computing system based on BOINIC (*) | Main Server, Network infrastructure, BOINIC |
| 8 | Processed data server | Mass storage for processed (calibrated) data sharing and distribution |

* http://boinc.oocp.org/indexj.php : Software platform for Einstein@home

2. 要求仕様 / Required specifications for Data Analysis

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Related sub-system(s) | 変更有り modified | 変更の可能性有り to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Computing Power |  | Data Analysis Subsystem |  |  |
| 2 | Data storage and archive |  | Data Analysis Subsystem Data Acquisition Subsystem |  |  |
| 3 | Commercially available software and libraries |  | Data Analysis Subsystem |  |  |
| 4 | Grid system |  | Data Analysis Subsystem |  |  |
| 5 | Database for stored data |  | Data Analysis Subsystem |  |  |
| 6 | Document control and archive |  | Data Analysis Subsystem |  |  |
| 7 | Interface for external trigger |  | Data Analysis Subsystem |  |  |
| 8 | GW alert system |  | Data Analysis Subsystem Data Acquisition Subsystem |  |  |
| 9 | Interface for BOINIC |  | Data Analysis Subsystem |  |  |

** Section in LCGT Design Document, Version 2

3. インターフェース / Interface of the Data Analysis

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
| * | Computing power | DAS | TBD | Not yet |
| * | Amount of data storage | DAS | TBD | Not yet |
| * | Data archive system | DAS, DAQ | TBD | Not yet |
|  | Commercial software | DAS | TBD | Not yet |
|  | Commercial libraries | DAS | TBD | Not yet |
| * | Database for stored data | DAS | TBD | Not yet |
| * | Document control and archive | DAS | TBD | Not yet |
|  | External triggers | DAS | TBD | Not yet |
|  | GW alert system | DAS, DAQ | TBD | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

| Subgroup Name | Data Analysis |
| --- | --- |
| Subgroup Leader | Hideyuki Tagoshi Osaka University |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-0 | 2009-05-27 | Kick-off draft |
| Rev. A-0 | 2009-06-02 | Modified by Tagoshi |
| Rev. A-0 | 2009-06-03 | Submitted to Kuroda |
| Rev. A-0 | 2010-04-15 | Modified by Tagoshi |

APPROVAL AUTHORITIES

用語集 / Glossary

| NS | Neutron Star |
| --- | --- |
| BH | Black Hole |
| SN | Supernovae |
| SNR, S/N | Signal-to-Noise Ratio |
| GW | Gravitational Wave |
| inspiral | The inspiral of the coalescing compact binaries |
| CBC | Compact Binary Coalescence |
| DAQ | Data Acquisition Subsystem |
| ACS | Analysis Center Subsystem |

1. 各サブシステムの簡単な定義 / Concise definition of Data Analysis

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | GW sources / Search Methods |
| --- | --- | --- |
| 1 | International network GW searches | Compact Binary Coalescences, Stochastic backgrounds, Bursts, All sky pulsar searches |
| 2 | LCGT standalone GW searches | External triggered search for CBC and Burst sources, Known pulsars searches, new search method developments, novel GW source searches |
| 3 | Astrophysical interpretation of GW search results |  |

2. 要求仕様 / Required specifications for Data Analysis

１で示した機能に対する要求仕様が記述されている LCGT design document version 3 での section 番号、関連 sub-system、Design document version 3 からの変更の有無と可能性。

フォームの始まり

| No. | 機能 / Function | Described section (**) | Related sub-system(s) | 変更有り modified | 変更の可能性有り to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | CBC search | 2.1, 2.4, 18.2.1, 18.4 | Analysis Center Subsystem |  |  |
| 2 | Burst search | 2.3, 2.4, 2.5, 18.2.2, 18.4 | Analysis Center Subsystem |  |  |
| 3 | Periodic source search | 2.2, 18.2.3, 18.4 | Analysis Center Subsystem |  |  |
| 4 | BH ringdown search | 2.1.2, 2.3, 2.4, 18.4 | Analysis Center Subsystem |  |  |
| 5 | Stochastic GW search | 2.5, 2.6 | Analysis Center Subsystem |  |  |
| 6 | Data quality and character check | 17.4 | Data Acquisition Subsystem Analysis Center Subsystem |  |  |
| 7 | International collaboration | 18.3 | Analysis Center Subsystem |  |  |
| 8 |  |  |  |  |  |
| 9 |  |  |  |  |  |

フォームの終わり

** Section in LCGT Design Document, Version 3

3. インターフェース / Interface of the Data Analysis

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | Observable frequency range | DAQ | 10 Hz - 10 kHz |  |
|  | ADC bit resolution | DAQ | > 16 bits |  |
|  | Search task data format | DAQ | TBD | Not yet |
|  | Calibration code and data | DAQ | TBD | Not yet |
|  | Data distribution method | DAQ, ACS | TBD | Not yet |
| * | Analysis computer system | DAQ, ACS | TBD | Not yet |
| * | CBC search code | ACS | TBD | Not yet |
| * | Burst search code | ACS | TBD | Not yet |
| * | Periodic source search code | ACS | TBD | Not yet |
| * | BH Ringdown search code | ACS | TBD | Not yet |
| * | Stochastic GW search code | ACS | TBD | Not yet |
| * | Data quality and character check code | ACS | TBD | Not yet |
|  | human resource management | ACS | TBD | Not yet |
|  | International collaboration | ACS | TBD | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

0. サブシステムの現状 / Current status of the Data Analysis

a) Conceptual design (サブシステムの定義) は確定しましたか？		確定 / 未定

* 未定な部分がある場合、検討項目を簡単に記述して下さい。

データ解析を行う人員の確保の手段（誰がどの財源を用いて行うか）が未定である．

国際共同データ解析のための具体的体制・手段・人員が未定である．

* Conceptual design の変更に伴い、予想される影響（検討事項）と関連 sub-group。

データ解析人員確保が十分出来ない場合には，各探査項目の優先度について検討する必要がある．

b) Alternative design は残っていますか？		残っている / いない

* Alternative design の採用により生じると予想される影響（検討項目）と 関連sub-group。

データ解析センターが実現した場合には，データ解析コンピュータシステムはセンターにかなり集約するという可能性ができる．

関連 sub-group: Analysis Center Subsystem

c) 今年予算承認されたとした場合、年度内に決定すべき項目と関連 sub-group。

データアーカイブシステム，データ配布システム，データ解析コンピュータシステム（@国内主要拠点）の仕様の決定．