Interface Control Document

of the LCGT Project

| Subgroup Name | Input-Output Optics Subystem (入射・射出光学系サブシステム) |
| --- | --- |
| Subgroup Leader | Shigenori Moriwaki The University of Tokyo |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-1 | 2010-04-18 | Kick-off draft |

APPROVAL AUTHORITIES

用語集 / Glossary

| AM | Amplitude modulation |
| --- | --- |
| MC | Mode cleaner |
| MMT | Mode matching telescope |
| FI | Faraday isolator |
| FN | Frequency noise |
| HWP | Half wave plate |
| PBS | Polarizing beam splitter |
| MZM | Mach-Zehnder modulator |
| PM | Phase modulation |
| PRM | Power recycling mirror |
| RIN | Relative intensity noise |
| SEM | Signal extraction mirror |
| WFS | Wave front sensing |

1. 各サブシステムの簡単な定義 / Concise definition of Input-Output Optics Subsystem

LCGT建設完了までに各サブグループが責任を持って提供すべき機能と、それを実現するためのハードウェア、ソフトウェア。

| No. | 機能 / Function | ハードウェア・ソフトウェア / Hardware, software |
| --- | --- | --- |
| 1 | Mode and RF Sideband Cleaner (MC1) | Suspended triangular ring cavity with 10m baseline in vacuum |
| 2 | Mode Cleaner (MC2) | Suspended triangular ring cavity with 15m baseline in vacuum |
| 3 | Phase Modulator for MC1(PMMC1) | Electro-Optic Modulator for 8MHz (TBD) on the input table |
| 4 | Faraday Isolator for MC1 (FI1) | Faraday rotator and polarizing beamsplitter in vacuum |
| 5 | Mode Matching Telescope for MC1 input (MMT1) | A pair of convex/concave mirrors mounted on the input table |
| 6 | Mode Matching Telescope between MC1 and MZM (MMT2) | A pair of convex/concave mirrors suspended in vacuum |
| 7 | Mach-Zehnder Modulator(MZM) | Mach-Zehnder interferometer which contains electro-optic modulators for 10MHz phase and 60MHz amplitude modulations |
| 8 | Faraday Isolator for MC2 (FI2) | Suspended Faraday rotator and polarizing beamsplitter in vacuum |
| 9 | Mode Matching Telescope for MC2 input (MMT3) | A pair of convex/concave mirrors suspended in vacuum |
| 10 | Mode Matching Telescope between MC2 and PRM (MMT4) | A pair of convex/concave mirrors suspended in vacuum |
| 11 | Output mode cleaner (OMC) | Rigid-body ring cavity which excludes deformed component of the anti-symmetric port beam |
| 12 | Mode Matching Telescope between SEM and OMC (MMT5) | A pair of convex/concave mirrors suspended in vacuum |
| 13 | Photo Detectors (PDs) | Length and wave front sensing photodetectors at the Dark Port, the Bright Port and the Pick-off Port |

2. 要求仕様 / Required specifications for Input-Output Optics Subsystem

１で示した機能に対する要求仕様が記述されている LCGT design document version 2 での section 番号、関連 sub-system、Design document version 2 からの変更の有無と可能性。

| No. | 機能 / Function | Described section (**) | Related sub-system(s) | 変更有り/modified | 変更の可能性有り/to be modified |
| --- | --- | --- | --- | --- | --- |
| 1 | Mode and RF Sideband Cleaner (MC1) | 7.2, 7.3 | Laser |  |  |
| 2 | Mode Cleaner (MC2) | 7.2, 7.3 | ISC |  |  |
| 3 | Phase Modulator for MC1(PMMC1) | 7.3 | Laser, ISC |  |  |
| 4 | Faraday Isolator for MC1 (FI1) | 7.9 | ISC |  |  |
| 5 | Mode Matching Telescope for MC1 input (MMT1) | Not yet | ISC |  |  |
| 6 | Mode Matching Telescope between MC1 and MZM (MMT2) | 7.5 | ISC |  |  |
| 7 | Mach-Zehnder Modulator(MZM) | 7.7 | ISC |  |  |
| 8 | Faraday Isolator for MC2 (FI2) | 7.9 | ISC |  |  |
| 9 | Mode Matching Telescope for MC2 input (MMT3) | 7.5 | ISC |  |  |
| 10 | Mode Matching Telescope between MC2 and PRM (MMT4) | 7.5 | ISC |  |  |
| 11 | Output mode cleaner (OMC) | 7.4 | ISC |  |  |
| 12 | Mode Matching Telescope between SEM and OMC (MMT5) | 7.9 | ISC |  |  |
| 13 | Photo Detectors (PDs) | 7.8 | ISC, Digital System |  |  |

** Section in LCGT Design Document , Version 2

3. インターフェース / Interface of the Input-Output Optics Subsystem

各サブシステムの詳細設計を行うにあたり、決定しなければならない仕様、他のサブシステムで決めて欲しい仕様、もしくは合意されている仕様

* 実際に建設が始まったら決まっていないと困ること、建設完了までに決まっていないといけないこと。

この欄は、人ではなくsubsystem 名か↓

|  | 事項 / Item | 関連サブシステム / Related sub-system | 要求値 / Value | 合意済 / Confirmed |
| --- | --- | --- | --- | --- |
|  | MC2 output power | ISC | 75W | ISC |
|  | MC2 output spatial mode | ISC, Bandwidth | TEM00, M2<1.1 (waist size and location: TBD) | Not yet |
|  | MC2 output polarization | ISC | S-pol, Is/Ip<0.01 | Not yet |
|  | MC2 output frequency noise | ISC | FN<4x10^-8Hz/rtHz at 100Hz | ISC |
|  | MC2 output intensity noise | ISC | RIN<2x10^-8/rtHz at 100Hz | ISC |
|  | MC2 output beam jitter | ISC | TBD | Not yet |
|  | MC2 output phase modulation | ISC | PM m>(TBD) at f1=11.25MHz, AM g>(TBD) at f2=45MHz, PM m>(TBD) at f_WFS=(TBD). | Not yet |
|  | MC2 output frequency tuning range | ISC | TBD | Not yet |
|  | MC2 output intensity attenuation range | ISC | TBD | Not yet |
|  | MC1 input power | Laser | 150W | ISC |
|  | MC1 input spatial mode | Laser | TEM00, M2<1.2 (waist size and location: TBD) | Not yet |
| * | Power consumption | 坑内施設 | TBD | not yet |
| * | Waist heat | 坑内施設 | TBD | not yet |
| * | Location and space | 坑内施設 | TBD | not yet |
|  | Installation schedule | ??? | TBD | Not yet |
|  | Budget allocation | ??? | TBD | Not yet |
|  | Man power allocation | ??? | TBD | Not yet |

↑ 当該サブシステムが決めないといけないことには * 印を付けること。

Infrastructure (vacuum chambers, beam tubes and opyical benches) for the Input-Output Optics Subsystem:

Locations of the centers and diameters of the vacuum chambers in the center area. The origin of the coordinate is at the center of beamsplitter chamber (BS).

| #name | #description | #posx(m) | #posy(m) | #diameter(m) |
| --- | --- | --- | --- | --- |
| BS | Beamsplitter chamber | 0 | 0 | 2 |
| PRM | Power recycling mirror chamber | -5 | 0 | 2 |
| MC2F | Front chamber for second mode clener | -11 | 0 | 2 |
| MC2E | End chamber for second mode cleaner | -11 | 13.3 | 2 |
| MZM | Mach-Zehnder modulator chamber | -16 | 0 | 1 |
| MC1F | Front chamber for first mode cleaner | -16 | -5 | 2 |
| MC1E | End chamber for first mode cleaner | -6 | -5 | 1 |
| SEM | Signal extraction mirror chamber | 0 | -10 | 2 |
| PD | Photo detection chamber | 0 | -14 | 1 |

Locations and sizes of the optical benches in the center area.

| #name | #description | #posx(m) | #posy(m) | #sizex(m) | #sizey(m) |
| --- | --- | --- | --- | --- | --- |
| benchBSmain | BS main bench | 2 | 2 | 1.5 | 1.5 |
| benchBSInline | BS bench at the inline arm side | 1.8 | -2.2 | 1.5 | 1.5 |
| benchBSPerp | BS bench at the perp. arm side | -1.8 | 2.2 | 1.5 | 1.5 |
| benchDark | Dark port bench | 1.8 | -14 | 1.8 | 2.4 |
| benchSEM | SEM bench | 2 | -10 | 1.5 | 1.5 |
| benchPRM | PRM bench | -5 | -2 | 1.5 | 1.5 |
| benchMC1E | MC1 end bench | -4.2 | -5 | 1.5 | 1.5 |
| benchMC2F | MC2 front bench | -9 | 2 | 1.5 | 1.5 |
| benchMC2E | MC2 end bench | -11 | 15.3 | 1.5 | 1.5 |
| benchBright | Bright port bench | -11 | -2 | 2.4 | 1.8 |
| benchMZM | MZM bench | -16 | 1.8 | 1.5 | 1.5 |
| benchInput | Input bench | -16 | -7.2 | 2.4 | 1.8 |
| benchLaser | Laser bench | -13.2 | -7.2 | 2.4 | 1.8 |

0. サブシステムの現状 / Current status of the Input-Output Optics Subsystem

a) Conceptual design (サブシステムの定義) は確定しましたか？		確定 / 未定

* 未定な部分がある場合、検討項目を簡単に記述して下さい。

* Conceptual design の変更に伴い、予想される影響（検討事項）と関連 sub-group。

b) Alternative design は残っていますか？		残っている / いない

* Alternative design の採用により生じると予想される影響（検討項目）と 関連sub-group。

DCリードアウト導入への対応が保留中。

各光学素子のAR面の残反射光の処理経路、MCに用いる鏡のウエッジ角の大きさが未検討。

Faradayアイソレータの真空内防振・水冷系のデザイン。水冷系の導入で万一破綻した場合、電気光学位相変調アイソレータのデザイン。

熱変形に対するモード補償の機能をMMTや MC1, MC2 に持たせるかどうか。

関連 sub-group: ISC (干渉計制御 sub-group)

c) 今年予算承認されたとした場合、年度内に決定すべき項目と関連 sub-group。

実験室内の配置、消費電力、廃熱量について坑内施設と打ち合わせる必要がある。