Current Issues of LCGT Interferometer Design
2010/8/2, Y. Aso
Purpose of the document
I will try to summarize the current status and the issues of the
interferometer design (not limited to the control schemes) of LCGT.
The scope of this document is limited to the main interferometer part.
The input optics subsystem is supposed to deliver an appropriately
shaped laser beam with enough power and necessary sidebands.

---
What do we have to design ?
3rd year and final design
We have to design both 3rd year IFO and the final IFO.
In the first half of this document, I will focus on the final IFO.
The 3rd year configuration should be designed reflecting the final IFO configuration.
Therefore, we have to decide on the final design first.
Parameters necessary for
mirror order and tunneling
We also have to design:
Length sensing and control scheme
Alignment sensing and control scheme
Arm cavity parameters
Finesse
g-factor (Mirror ROCs)
Mirror Size
AR wedge
Error specs
Recycling Cavity Designs
RM reflectivities
Lengths
Folding design
Beam splitter design
Size
Wedge
There are many factors to consider to decide
on the parameters and the scheme.

---
Arm Cavity Parameters
Finesse: 1550 (already decided by the IFOBW WG)
Issues
1550 could be too high. Need more investigations on what could go wrong.
Mirror loss: 45ppm per reflection. Is it possible ?
sqrt(1/3) --> L=3000m, ROC=7098.08m (Conventional number)
-sqrt(1/3) --> L=3000m, ROC=1901.92m (Alternative)
g-factor:
Beam Size: 3.5cm for both cases
HOM degeneration: the same for both cases
Angular instability:
Two eigen-frequencies are 1.66Hz and 0.86Hz for a sapphire mirror
(Moment of inertia = 0.173 [kg*m^2])
For positive g, 1.66Hz becomes unstable while it is 0.86 for negative g.
Parametric Instability:
There are preferred regions in the g factor space from the view point of PI.
The regions are the same for positive and negative g.
However, dg/dR is different by a factor of 13 (negative g is larger).
Therefore, negative g is more sensitive to the ROC error (not limited
to the PI actually).

---
PI calculation by K. Yamamoto
Negative g-factor
Positive g-factor
The error requirement on the mirror ROC is stricter for the negative g-factor.

---
Mirror Size
Factors to consider
It is desirable to have as few as possible variations of size and weight of the mirrors
from the view point of SAS
Especially, changing the weight is costly.
What is the maximum possible mirror size ?
Main Cavity Mirrors
Diameter=25cm, Thickness=15cm is the default
Weight is 16kg for Silica and 30kg for Sapphire
The beam diameter on the mirrors is 7cm. 25cm is larger than the 3*sigma diameter.
Compound mirror ? (see the next next page)
Recycling and Folding Mirrors
Diameter=25cm, Thickness=15cm, 16kg is the default
These mirrors can be smaller, but increasing mirror size variation is considered
more costly at this moment (discussion needed).
Beam Splitter
Diameter=37cm, Thickness=6.85cm, 16kg is the default.
These numbers are chosen based on the H. Yamamoto's calculation
shown on the next page.
The thickness is adjusted to have the same weight as the RMs.

---
Optical Loss in the PRC by BS size effect by H. Yamamoto

---
Compound Mirror Idea
by M. Ando (compiled by Y. Aso)
The 3rd year IFO does not necessarily have an extremely good thermal noise
By attaching a ring of heavy metal around a small fused silica mirror, we may
make a 25cm mirror with the same weight as the final sapphire one.
We can use Type-A SAS from the beginning (no replacement required)
Thermal noise has to be checked.
Fused Silica
25cm
Metal Ring
Example:
Using Copper.
Silica diameter = 18.9cm.
Copper ring outer diameter = 25cm, inner diameter = 19.9cm
Total Weight = 30kg

---
Wedge
Functions of wedge
To avoid forming an Etalon between the AR and HR surfaces
To separate secondary reflections from the main beam
ITMs & PRM
These are now curved mirrors --> no Etalon formed.
Wedge is still needed for picking up the secondary reflections
 (no pick-off mirror is planned to be installed at this moment)
BS
Wedge is necessary to separate the secondary reflection
from the main beam.
Issues
Is it possible to make wedge on a sapphire mirror ?
When the mirror substrate is changed, the wedge angle
must be changed because the deflection angle depends
on the refraction index.
Other Mirror Specs
0.25deg wedge
AR reflectivity
Error tolerances for various parameters

---
Recycling Cavity Design
Background
A straight recycling cavity would be marginally stable for the LCGT parameter.
This can introduce many unwanted side-effects.
A solution to this is to stabilize it by adding extra Gouy phase shift inside.
For the moment, the Gouy phase shift in the RCs are designed to be 20deg
one-way. This is a rough number taken from aLIGO's design.
Folding Cavity Design
The RCs are folded by two additional curved mirrors to add extra Gouy phase shift.
Issues
Mode matching between the RC and the arm cavities depends strongly on the
distance between the two folding mirrors.
We need a mechanism to adjust the position of the folding mirrors.
Is it possible to polish a large mirror to a small ROC ?
Scattered light by the folding mirrors
The scattered light power was estimated by D. Tatsumi
We have to convert this to actual contamination of the error signals.

---
Recycling Cavity Design continued
What is the optimal Gouy phase shift ?
A very stable PRC would suppress the WFS signal from the arm cavities.
We have to hit a balance between the RC stability and the WFS signal strength.
20deg is probably not a bad number but most likely not the optimal one.
We need the ASC calculation and the GW signal loss estimation by MIST (or Finesse)
to answer the above question.
For the moment, if we decide to fold the RCs, the locations of the folding mirrors are
fixed by the geometric constraints coming from the minimization of the astigmatism.
Fine adjustment of the Gouy phase can be done by changing the ROC of the folding
mirrors.

---
IFO Length Sensing and Control
A basic scheme is found
Not sure it is the optimum one
Needs a cross check
Alignment Sensing and Control
What is the status, Agatsuma-kun ?

---
Lock Acquisition
Basic ideas for green laser lock
Green Lasers are injected from PR3 for X-arm, and SR3 for Y-arm
PR3, SR3 and BS are transparent to green.
ITMs and ETMs are dichroic mirrors
Each green laser is locked to the main laser through a PLL
Additional AOM could be inserted between the green lasers and PLL
 to provide fast frequency actuation
Main Laser
PRM
PR2
AOM
Green1
PLL1
PR3
SR2
PDH1
Lock procedure
Each arm is locked to the green laser by
 frequency feedback to the PLLs and AOMs.
Common signal of the two arms is fed back
 to the main laser (high freq.) and CARM (low freq.)
Differential signal is fed back to DARM
Scan the PLL1 and PLL2 to find the resonance
 of the main laser
SR3
SRM
PDH2
PLL2
Green2
AOM

---
Interfaces with other subsystems
Suspension
We need:
Realistic seismic attenuation performance including alignment
We provide:
Actuator requirements (noise, strength)
Local sensor requirements
Optical Layout
Input & Output Optics
We provide:
Requirements for the laser power
Sideband frequencies and power
Input mode shape
Intensity and frequency noise requirements
Digital & Analog Electronics
We provide:
Number of signal ports & actuation points
Electric noise requirements
RF noise requirements

---
Interfaces with other subsystems continued
Vacuum and Cryogenic System
We provide:
Strongly request to make view ports
Optical Layout
Mirror Group
We need:
Producible mirror sizes
Realizable accuracy of ROC
Realizable loss (including absorption and scatter)
We provide:
Mirror Size (as soon as possible)
Detailed mirror specs including error tolerance

---
Risks and Concerns
A draft list by Somiya and Miyakawa
(1) ロスのインバランスが小さすぎてHD位相が90度に固定されてしまう
   ～ aLIGOではBAEをしないのでLCGT特有という意味でリスキー
(2) DRSEにしたときにf1にインバランスができて誤差信号にオフセット
   ～ PD出力がサチる、非線形雑音など、aLIGOが避けたリスクを負う
(3) 入射光学系でAMを作ったりMZを入れたりすると変な雑音が乗る
   ～ これもaLIGOが避けた問題
(4) f1とf2の比が近いのがなんとなく危険
   ～ aLIGOより比が小さい
(5) DDMのPDは作れるのか
   ～ aLIGOはSDMのみ
(6) OMC-REFLから信号がきれいにとれるのか(LA問題、高次モードなど)
   ～ aLIGOでは使わない
(7) 折り返しの散乱光vs折り返さない場合のSBモード縮退
   ～ 折り返すならaLIGOと同じリスク、折り返さないなら特有リスク
(8) フィネスが高い→(1)と逆にHD位相が0度に近くなる可能性
   ～ aLIGOでは下げている
(9) VRSEにするためにlsとl-が下がる
   →(6)が失敗するときつい
   →DRSEだとFFがとれないかもしれないので厳しくなる
(10) PM-PMのときのLA方法が確立されていない
(11) OMCの共振は大丈夫か
(12) サファイアITMは作れるか
(13) サファイア鏡とファイバーはくっつくか

---
Risks and Concerns continued
(14) 1.8mm径のファイバーが作れるか
(15) サファイアで45ppmの光損失は可能か
(16) (15)はコーティングの機械損失が低温で上がるかという意味だったかも
(17) 7kmもしくは1.9kmのROCが実現できるか
(18) RM2のROC→なんでしたっけ、これ