LCGT LSC Design
and other practical interferometer details
Yoichi Aso
2010/12/7

---
Basic Ideas behind the LSC scheme of LCGT
DOFs to be controlled: DARM, CARM, MICH, PRCL, SRCL
Signals are extracted using the beat between the carrier and RF sidebands
except for DARM (DC readout).
CARM is sensed at REFL by the beat between the carrier, which sees
the arm cavity and one of the RF sidebands, which are insensitive to the arms.
 This signal is usually huge.
Two RF sidebands are resonated in the PRC and SRC in different ways:
One sideband, called f2, is perfectly reflected by the MICH so that it sees
only PRC.
The other sideband (f1) resonates in the coupled PRC-SRC cavity.
So it carries both the information of PRC and SRC.
These two sidebands are PM so that these can be used for WFS.
Additional sideband, which is non-resonant to the PRC, can be used to provide
a local oscillator for the PRC, SRC, MICH sensing. This sideband is AM.
MICH signal is generated in the Q-phase by the imbalance of the upper and
 lower sidebands of f1 beating against the carrier or the non-resonant sideband.

---
Sideband Resonant Conditions and Signal Ports
ETMY
f1 sideband resonates in PRC-SRC
f2 sideband resonates only in PRC
f3 sideband does not enter the interferometer at all
ITMY
REFL
PRM
PR2
ITMX
ETMX
POP
BS
PR3
SR2
SR3
SRM
Carrier
ASPO
f1 sideband (PM 11.25MHz)
f2 sideband (PM 45MHz)
OMCREFL
f3 sideband (AM 39.375MHz)
AS_DC

---
Macroscopic Length and modulation frequencies
Important requirement: The SRC finesse for f1 has to be moderate.
        --> Allow 3.5deg detuning of SRC.
The MICH reflectivity for f1 has to be close to PRM reflectivity to make the
combined mirror of PRM+MICH has a low reflectivity.
f2 frequency was chosen to be not too high but not too low.
  --> 45MHz
MICH asymmetry (Las) was set to perfectly reflect the f2 sidebands.
 --> 3.33m (smallest possible)
PRC length (Lp) is chosen to make f2 resonant in the PRC.
There are actually many choices for Lp. We preferred to make it about 80m.
25m is taken by the cold pipe for radiation shield between BS and ITMs.
The rest is for folding.
--> 73.2826m
f1 frequency is chosen to be resonant in the PRC and also to have an appropriate
 MICH reflectivity. Also, the MC FSR has to be small enough to make the MC length
 practical.
--> 11.25MHz (f2/4).
SRC length (Ls) is chosen to make f1 resonant in the PRC-SRC coupled cavity.
We also want to make this about 80m for the same reasons for Lp.
--> 73.2826m

---
Resonance curves of f1 sideband to the SRC

---
Signal Extraction Scheme

---
Optickle Simulation
Optickle: A frequency domain simulation tool for interferometers (by M. Evans)
It can ...
Generate optical gain transfer functions from optics to signal ports.
DC offset at each port.
Quantum noise (shot noise and radiation pressure noise).
Incorporate mechanical TFs of optics.
A New Optickle Model of LCGT
Full LCGT IFO including MZ, folding mirrors and OMC
New version of Optickle
Vacuum fluctuations are injected automatically at every
open or lossy port.
Loop noise calculation.
Displacement noise coupling
All Optickle simulations are done with ...
Up to 3rd order harmonics of RF sidebands included.
1% mirror reflectivity imbalance between the two arms.
+/-10ppm arm loss imbalance.

---
Move from AM-PM to PM-PM scheme
Original Scheme:
f1: AM, f2: PM
f1 is the only available sideband at the AS port
However, it is AM. Not good for WFS.
No RF DARM available.
WFS and AM
WFS signal can be obtained using AM sidebands
Gouy phase difference between TEM00(f1) and TEM01(carrier) transforms AM
sidebands to PM at certain locations.
However, residual TEM00 carrier creates strong beat against f1 TEM00.
Any QPD mis-centering would see this residual beat.
Using OMC REFL, we could in principle eliminate carrier TEM00
This has a potential of contaminating the WFS signal with the OMC alignment noise

---
Signal Ports and Naming Convention
How to decipher a signal name ?
REFL_1I
Reflection port demodulated at f1 freq.
in I-phase.
Demodulation Phase
Detection Port Name
Demodulation Frequency
REFL_1DmI
Reflection port demodulated at
f3-f1 freq. in I-phase.
Demodulation Phase
Detection Port Name
Demodulation Frequency
1Dm: f3 - f1
1Dp: f3 + f1
2Dm: f3 - f2
2Dp: f3 + f2
DC Power at each port
REFL: ~ 200mW
AS: ~ 10mW
POP: ~ 400mW

---
CARM, PRCL, SRCL
These signals are mixed
CARM signal can be extracted from the beat between the carrier and
   the f1 or f2 sidebands at the REFL port.
PRCL and SRCL information is also embedded in the same signal.
PRCL is obtained from f2 demodulation, which contains no SRCL
information.
f1 demodulation is a mixture of SRCL, PRCL and CARM
How do we solve the signal mixing problem ?
Gain Hierarchy: iLIGO and aLIGO way
CARM feedback is much faster than any other DOFs because we can use
  the laser frequency actuators. (UGF ~ 50kHz).
Therefore, we can expect a good suppression of CARM signal at UGFs of
 PRCL and SRCL (~100Hz).
Examples of signal extraction ports
CARM: REFL_2I
PRCL: POP_2I
SRCL: POP_1I

---
Sensing Matrix with Single Demodulation
(BRSE, measured at 100Hz)
[W/m]

---
Alternative: Non-Resonant Sidebands (NRS)
CARM signal is mixed with PRCL and SRCL because we used
the carrier for signal generation.
If we use a sideband which does not enter the interferometer at all
 as a local oscillator for f1 and f2, PRCL and SRCL can be
Now MC length is doubled. FSR is 11.25/2.
We can use,
f3: AM at 39.375MHz
This should in principle be insensitive to any arm motion.
No it is not unless we use Mach Zehnder.
Serial Modulation
f1
f2
f2
f3
Generates sidebands of sidebands (sub-sidebands)
For example, (f3-f2) sub-sidebands beating against the carrier create
some signal of CARM at the (f3 - f2) frequency.

---
Sensing Matrix with NRS
(BRSE, no MZ, measured at 100Hz)
Signals are still mixed
(but a bit less)
[W/m]

---
Mach Zehnder
To MC
Pros:
Able to avoid generation of sub-sidebands
Cleaner signal separation
Cons:
Waste half of the sideband power
Additional phase noise
f2
f3
Laser
f1

---
Sensing Matrix with NRS
(BRSE, with MZ, measured at 100Hz)
Clean signal separation
[W/m]

---
Loop Noise

---
Shot Noise Coupling
So far, we've been concerned only with the signal separation ...
This is by no means sufficient.
Auxiliary DOFs in general have worse shot noise than DARM
MICH is particularly problematic one.
MICH unavoidably couples to DARM (1/finesse)
MICH signal is weak
Driving MICH with this bad signal ---> Noise coupling to DARM
How the MICH signal at REFL_Q is generated ?
SY Port
MICH signal
+
+
-
Q-phase
Sideband imbalance --> Weak signal

---
Loop Noise
Formulation used here:
Canonical IFO DOFs
Mirror displacement
size 20 {vec n_{nitalic s} }
Shot Noise
Calibrated
Output
Displacement
noise
Detector
Sensing
Calibration
+
D
S
C
size 20 {vec x_{nitalic c} }
size 20 {vec n_{nitalic d} }
+
+
-
Actuator
Filter
F
A
+
F'
Feed forward
size 26 {vec x_{nitalic c} = (I+G)^{-1} cdot S cdot vec n_{nitalic s} + (I+G)^{-1} cdot SD cdot vec n_{nitalic d}}
size 26 {G equiv S cdot D cdot A cdot (F+F')}
D: Optical Gain Transfer Function calculated by Optickle
A: Mechanical TFs of the mirror suspensions + optical spring stiffness
F: Feedback filters
F': Feed forward matrix
S: Sensing matrix (here I just used identity matrix)

---
Default UGFs
DARM: 200Hz
CARM: 10kHz
MICH: 50Hz
PRCL: 50Hz
SRCL: 50Hz
At Kamioka, we may be able to reduce
them further (~10Hz ?)
Feed forward used for MICH and SRCL

---
So, the shot noise coupling kills the sensitivity
BRSE, SDM, no feed forward

---
With the Feed Forward
Feed Forward TF error = 1% (random error added)

---
Other Configurations
BRSE DDM no MZ
MICH: REFL_1DmQ
PRCL: REFL_2DmI
SRCL: REFL_1DmI
BRSE DDM with MZ
DRSE SDM
DRSE DDM no MZ
DRSE DDM with MZ

---
BRSE DDM no MZ
Feed forward accuracy = 3%

---
BRSE DDM with MZ
Feed forward accuracy = 3%

---
DRSE SDM
Feed forward accuracy = 1%
A large optical spring peak around 40Hz ruins the sensitivity

---
DRSE SDM
Feed forward accuracy = 1%
Reduced MICH UGF to 10Hz

---
DRSE DDM no MZ
Feed forward accuracy = 1%
MICH UGF = 10Hz

---
DRSE DDM with MZ
Feed forward accuracy = 1%
MICH UGF = 10Hz

---
Check DC Offset
Offset amount in meters
	DARM	CARM	MICH	PRCL	SRCL
BRSE SDM	7.64e-13	7.17e-15	4.04e-12	7.49e-12	2.8e-11
BRSE DDM no MZ	7.64e-13	6.99e-15	3.74e-11	4.19e-11	1.9e-11
BRSE DDM with MZ	7.64e-13	7.28e-15	6.12e-13	7.17e-11	7.99e-14
DRSE SDM	7.64e-13	1.15e-14	4.96e-09	8.23e-12	1.22e-08
DRSE DDM no MZ	7.64e-13	1.15e-14	1.72e-09	3.48e-11	1.23e-08
DRSE with MZ	7.64e-13	1.08e-13	1.75e-09	8.01e-11	1.23e-08
Problem ?
Caused by the f1 sideband rotation by the SRC detuning
(f1 no longer acts as pure PM but somewhere between AM and PM)

---
Displacement Noise Requirement
Feed forward increases displacement noise coupling from aux. mirrors to DARM
BRSE, no MZ, Feed Forward 3%

---
Displacement Noise Requirement
Feed forward increases displacement noise coupling from aux. mirrors to DARM
DRSE, no MZ, Feed Forward 1%, MICH UGF=10Hz

---
Summary of the Length Sensing Schemes
For BRSE, Non-Resonant Sideband Method without MZ seems OK.
No MZ makes the setup simple and robust
Moderate feed forward gain (30) is enough.
MICH UGF can be as high as 50Hz.
For DRSE, Non-Resonant Sideband Method with MZ seems the best choice.
MZ noise could be a problem.
High feed forward gain (100) is required.
MICH UGF has to be below 10Hz.
A large MICH offset can be a problem.
We don't have to make a choice now !
These sensing schemes can be switchable at a later time.
No in vacuum work necessary to switch
MZ <--> no-MZ change may require some work,
 but still doable on an optical bench.
Important thing is: There are schemes which seem to work.

---
Lock Acquisition
Lock Acquisition Procedure
First, lock the central part then lock the arms
When the central part is locked, this lock should not be disturbed by the arms
It is desirable to use signals insensitive to the arms
e.g. 3rd Harmonics demodulation
NRS DDM with MZ is insensitive to the arms
Alternatively, the arms can be pre-locked to an aux. laser
The Default Plan for LCGT Lock Acquisition is Green Pre-Lock

---
Green Pre-Lock
Basic ideas for green laser lock
Green Lasers are injected from PR3 for X-arm, and SR3 for Y-arm
PR3, SR3 and BS are transparent to green.
ITMs and ETMs are dichroic mirrors
Each green laser is locked to the main laser through a PLL
Additional AOM could be inserted between the green lasers and PLL
 to provide fast frequency actuation
Two green beams have orthogonal polarizations.
Optionally, they can have ~ 100MHz frequency shift to avoid the mixture
 of the signals from the arms.
Main Laser
PRM
PR2
AOM
Green1
PLL1
PR3
P-pol
SR2
PDH1
Lock procedure
Each arm is locked to the green laser by
 frequency feedback to the PLLs and AOMs.
Common signal of the two arms is fed back
 to the main laser (high freq.) and CARM (low freq.)
Differential signal is fed back to DARM
Scan the PLL1 and PLL2 to find the resonance
 of the main laser
SR3
SRM
PDH2
PLL2
Green2
AOM
S-pol

---
Mirror Requirements for Green
Several Dichroic Mirrors are necessary
Specs for 532nm
PR3: T>99%, Polarization: P
SR3: T>99%, Polarization: S
BS: T>99% for both Polarization
ITMX: R=80%, Polarization: P
ITMY: R=80%, Polarization: S
ETMX: R=90%, Polarization: P
ETMY: R=90%, Polarization: S
Arm finesse = 20
Injection Port Considerations
At PR3, the beam size is large (3.5cm)
Requires either a large optical window or an in-vacuum telescope
At PR2, the beam size is small. Much easier to handle.
Probably we want to separate the output port for POP (large 1064nm leak)
 and the injection port for green.
Dispersion between 1064nm and 532nm separates 1064nm and 532nm beams
 by 2mm on PR3. Not enough to separate beams.
PR2 injection seems better because PR3 POP won't be contaminated by green.

---
Alignment Sensing and Control (ASC)
There are several ways to reduce alignment fluctuation
Passive attenuation by the suspension system @ detection band.
Optical Lever @ Resonant frequencies
WFS @ DC and Resonant frequencies
WFS senses the mismatch between the incident beam and the cavity axis.
This is why WFS is used for DC.
WFS does not guarantee beam centering. We may need something else.
WFS signals
DARM: AS
CARM: REFL
PRC: REFL_2D
SRC: REFL_1D
Possible Detection Ports
Optickle Simulation is needed.
We are working on it now...

---
Folding Cavity and Alignment Control
Sideband Modes are Unstable
GW sidebands can be reduced
WFS signals may not make sense
Straight RCs: Almost degenerated
Increase the Gouy phase shift in the RCs
Focus the beam in the RCs
Folding the RCs
If the Cavity is Too Stable
Arm misalignment scatter the TEM00 carrier to TEM01 or TEM10
TEM01 or TEM10 are suppressed in the RCs --> No WFS signal.
A Compromise between the Stability and he WFS signal
One-way Gouy Phase shift of 20 deg.

---
Folding configuration by D. Tatsumi

---
Effect of the ROC errors in the folding mirrors
We have to be able to adjust the folding mirror positions by +/-5cm or so.

---
Folding Mirrors and Alignment
How do we get the alignment information of the folding mirrors ?
PRM
PR2
BS
PR3
ITMX
Even if it is folded, there is only one cavity axis
There are 2 DOF per rotation axis, translation and tilt.
WFS senses the translation and tilt with respect to the incident beam.
But there are 4 mirrors to be controlled
Any motion of the 4 mirrors can in principle be canceled by moving
two mirrors ?
More investigations on the cavity geometry needed

---
Arm Cavity g-factor
sqrt(1/3) --> L=3000m, ROC=7098.08m (Conventional number)
-sqrt(1/3) --> L=3000m, ROC=1901.92m (Alternative)
Beam Size: 3.5cm for both cases
HOM degeneration: the same for both cases
Angular instability:
Two eigen-frequencies are 1.66Hz and 0.86Hz for a sapphire mirror
(Moment of inertia = 0.173 [kg*m^2])
For positive g, 1.66Hz becomes unstable while it is 0.86 for negative g.
Parametric Instability:
There are preferred regions in the g factor space from the view point of PI.
The regions are the same for positive and negative g.
However, dg/dR is different by a factor of 13 (negative g is larger).
Therefore, negative g is more sensitive to the ROC error (not limited
to the PI actually).

---
PI calculation by K. Yamamoto
Negative g-factor
Positive g-factor
The error requirement on the mirror ROC is stricter for the negative g-factor.
by
size 22 {(R_{nitalic p} / R_{nitalic n})^2}
Mirror sag is proportional to 1/ROC.
So required machining precision may be independent on the ROC ?
If so, we should employ the negative g-factor

---
RF Sideband Higher Order Mode in the Arm Cavity
Arm Cavity FSR = 50kHz
RF Sidebands >10MHz
Accidental resonances of HOM RF sideband may happen

---
Only a small arm length change can drastically change
the RF sideband power in the arms.
Arm length tuning range of +/-10cm would be necessary

---
Optical Layout
Necessary to decide how to handle stray light and signal ports
Tool
A python module to automatically compute the propagation, reflection,
 deflection of Gaussian beams.
Programmatic design of the IFO optical layout to satisfy various quantitative
 requirements at the same time

---
Vacuum Chamber Spacing
With the current design, the spacing between the chamber centers is 3m.
PRM
PR2
25m
ITMX
BS
PR3
Keep this distance
This is not a good working environment
for the suspension commissioners.
SR2
To reduce astigmatism, we want to keep the distance between PR2 and PR3.
The total length of the RCs are fixed by the LSC scheme.
Can we reduce the BS-ITM distance by 2m and give it to the BS-PR3 and
  PR2-PRM spacings ?
Interface between: ISC, Cryo, Vacuum and Suspension

---
Output Telescopes
At some output ports, beam size is large (3.5cm).
We have to reduce the size of the beams first --> Output Telescopes
Port	Beam Size
REFL	5mm
POP	3.5cm or 5mm
Green	3.5cm or 5mm
POX, POY	3.5cm
AS (Before OMC)	5mm
TRX, TRY	3.5cm
In vacuum telescopes ?
Suspended ?
Reflective or transmissive ?
Interface with Input Output Optics Group

---
Radiation Baffles and PO Beams
Pick-off beams from the ITMs are separated from the main beam
in the BS tank.
POY Beam
POX Beam
The current configuration will interfere with the radiation shield baffles.
Interface with Cryo-Group

---
Input Steering Mirrors
The current design uses the mode matching telescope as the input beam
steering mirror.
MT1
from MC
PRM
MT2
We should check if the telescope can produce both beam translation and tilt
with enough actuation range.
Output Mode Cleaner
No design so far ?
4 mirror cavity ?
How to lock it ?
How to align it ?
Interface with Input Output Optics Group

---
Summary
LSC scheme has been studied in detail
There are at least several feasible candidates for LSC scheme.
ASC scheme is the big missing stuff in LCGT
I personally recommend negative g-factor
Folding cavity design and the HOM resonance issue both require
 the suspensions be movable by +/- 10cm. (ETMs and folding mirrors)
A rough plan for Green-Lock exists
A draft optical layout exits
Needs more discussions with other sub-systems

---
TO DO
LSC
Check the Optickle results with Finesse
 ASC
Find a reasonable signal extraction scheme with Optickle
Check noise coupling from ASC to LSC
 Optical Layout
Finalize the main optics layout
Need to decide on the vacuum chamber spacing
Auxiliary beam handling
Output telescope
 Green Lock
Detailed optical configuration
Noise estimates
Issues, Risks, Worries
MZ noise coupling
PRM matching with arm may be poor --> increased REFL shot noise for DDM
Is feed forward accuracy of 1% possible ? Adaptive Filtering ?
Is it possible to align the folded cavity with WFS ?
PRM thermal lensing