Main Interferometer Meeting
2011/2/9
Agenda
SRC Folding, Yes or No ?
Decide on the Arm cavity g-factor
Dynamic range
f1 frequency. Is 11.25MHz really OK ?
ASC status
Green lock design
Mirror specs
Task assignment

---
SRC Folding
Reason for PRC Folding
If straight: PRC g-factor = 0.9996 -> Transverse mode spacing = FSR/158
PRC Finesse = 57 ---> Up to 3rd order HOMs are well within the cavity resonance.
Unpredictable spatial mode of RF SBs in the PRC
How about SRC Folding
Straight SRC is equally unstable to the PRC
f1 SB resonates in the PRC-SRC coupled cavity
HOMs not resonating in PRC won't resonate in the coupled cavity
SRC could be unstable for f1 in principle.
Yi Pan and others suggested the GW SBs may be lost by the unstable SRC.

---
Cavity g-factor
Relevant Issues
Beam spot size --> Mirror Thermal Noise
Angular radiation pressure (Sidles-Sigg Instability)
Parametric Instability
Proposed g-factors from Detector Configuration Group
g1 = 0.87, g2 = 0.6 --> R1 = 23km, R2 = 7.7km
        or
g1 = -0.87, g2 = -0.6 --> R1 = 1.6km, R2 = 1.9km
Possible ?
Old g-factors
g1 = g2 = 0.586 --> R1 = R2 = 7.2km
        or
g1 = g2 = -0.586 --> R1 = R2 = 1.9km

---
Sidles-Sigg Stiffness Matrix
Angular Optical Spring Constant k [N*m/rad]
New g-factors
4.59, -29.2 (g1 = 0.87, g2 = 0.6)
-4.59, 29.2 (g1 = -0.87, g2 = -0.6)
Old g-factors
5.0, -19.33 (g1 = g2 = 0.586)
-5.0, 19.33 (g1 = g2 = - 0.586)
Suspension
Angle [rad]
Torque [N*m]
+
H
+
-
k
Optical angular spring constant
Open Loop Gain: G = k*H
Check Stability

---
Suspension TF (by Sekiguchi-kun)
Yaw Torque -> Yaw Angle
This is H

---
1.5Hz
Open Loop TF
New g-factor, positive
Stable
Unstable
2.5Hz
Unstable frequency
Positive g-factor: 2.5Hz
Negative g-factor: 1.5Hz

---
1.6Hz
Open Loop TF
Old g-factor, positive
Stable
Unstable
2.2Hz
Unstable frequency
Positive g-factor: 2.2Hz
Negative g-factor: 1.6Hz
No big difference in terms of
the Sidles-Sigg instability

---
Parametric Instability
There are dangerous regions to avoid in the g-factor space
Negative g-factor
Positive g-factor
The error requirement on the mirror ROC is stricter for the negative g-factor.
by
size 22 {(R_{nitalic p} / R_{nitalic n})}
Negative g-factor is about 3.7 times more
severe to ROC error in terms of PI
Negative g-factor: R ~ 1.9km
Positive g-factor: R > 7km
10m ROC errror for 1.9km mirror -> 0.5% error
100m ROC errror for 7km mirror -> 1.5% error

---
Conclusion on g-factor
Please vote !
		Thermal Noise (IR) / DRSE/BRSE [Mpc]	Optical Spring / Unstable Freq.	PI	Other
(a)	g1=0.87 / g2=0.6	273/245	2.5Hz	Easy	ROC=23km / may not be possible
(b)	g1=-0.87 / g2=-0.6	273/245	1.5Hz	Severe
(c)	g1=0.586 / g2=0.586	266/241	2.2Hz	Easy	iLIGO mirrors can / be used.
(d)	g1=-0.586 / g2=-0.586	266/241	1.6Hz	Severe

---
Modulation Frequencies
Concerns about 11.25MHz scheme
f1:f2 = 1:4 prohibits the use of 3rd harmonics demodulation
f3 = 7/2*f1 --> f2 -f3 ~ 5.6MHz too low ?
MICH reflectivity for f1 is about 50%, SRC resonance is not sharp
--> MICH signal may be too small.
Test other frequencies
(a) 11.25MHz - 45MHz: Lmc = 26.6m, Lprc = Lsrc = 73.3m, Las = 3.3m, Rmi=50%
(b) 9MHz - 45MHz: Lmc = 33.3m, Lprc=Lsrc=74.9m, Las = 6.6m, Rmi=10%
(c) 12.857MHz - 45MHz: Lmc=23.3m, Lprc=Lsrc=81.6m, Las=6.6m, Rmi=5%
(d) 13.5MHz - 45MHz: Lmc = 33.3m, Lprc=Lsrc=83.3m, Las=3.3m, Rmi = 34%

---
SRC Detuning
(a) 11.25MHz-45MHz
(b) 9MHz-45MHz

---
Loop Noise: BRSE 11.25MHz DDM with NRS
Feed forward gain = 100, MICH UGF=50Hz

---
Loop Noise: BRSE 11.25MHz SDM
Feed forward gain = 100, MICH UGF=50Hz

---
Loop Noise: DRSE 11.25MHz DDM with NRS
Feed forward gain = 100, MICH UGF=10Hz

---
Loop Noise: DRSE 11.25MHz SDM
Feed forward gain = 100, MICH UGF=10Hz

---
Loop Noise: BRSE 9MHz DDM with NRS
Feed forward gain = 100, MICH UGF=50Hz

---
Loop Noise: BRSE 9MHz SDM
Feed forward gain = 100, MICH UGF=50Hz

---
Loop Noise: DRSE 9MHz DDM with NRS
Feed forward gain = 100, MICH UGF=10Hz

---
Loop Noise: DRSE 9MHz SDM
Feed forward gain = 100, MICH UGF=10Hz

---
Change the modulation frequencies ?
9MHz seems better than 11.25MHz
f3 = 7/2 * 9MHz = 31.5MHz, f3-f1 = 22.5MHz, f2-f3 = 13.5MHz
Lmc and Las are a bit longer
(d) is not much different from (a)
(c) is not as good as (b) (have to check why)
We have to decide Now !

---
Green Lock Scheme
We need to have mirror specs for 532nm soon.
Where to inject green ?
PR2 or PR3
GreenY1
PR2: Beam size is smaller
PR3: No 532nm coating for PR2
PRM
PR2
GreenX1
GreenX2
PR3
SR2
End injection ?
How tolerant are the green coating requirements ?
How much is the power necessary ?
SR3
SRM
GreenY2

---
Mirror Specs
We have to provide more detailed mirror specs to Mio-san as soon as possible.
TM Specs (Draft)
HR@1064nm=99.6%+/-0.01%(ITM), >99.9945% (ETM)
HR@1064nm imbalance between X and Y: ???
HR@532nm = 80%+/-10% (R_ITM < R_ETM)
HR loss@1064nm < 45ppm (loss imbalance: ???)
HR loss@532nm < 1%
AR@1064nm=200ppm+100/-0ppm
AR@532nm<5%
ROC = 7177m +50/-20m
Wedge angle = 0.25deg (+/-0.01deg?)
POX, POY
~ 100mW

---
BS Specs (Draft)
HR@1064nm=50%+/-0.1%
HR@532nm = 10%
HR loss@1064nm: 0.01%? Set from thermal lens
HR loss@532nm < 10%
AR@1064nm < 50ppm
AR@532nm < 10%
ROC = flat (how flat ?)
Wedge angle = 0.48deg (+/-0.01deg?)
PRM Specs (Draft)
HR@1064nm=90%+0/-0.1%
HR loss@1064nm: < 100ppm
AR@1064nm < 50ppm
ROC = 316m +/-1m
Wedge angle = 2deg (LIGO mirror)

---
SRM Specs (Draft)
HR@1064nm=84.64%+/-0.01%??
HR loss@1064nm: < 100ppm
AR@1064nm < 50ppm
ROC = 316m +/-1m
Wedge angle = 2deg (LIGO mirror)
PR3/SR3 Specs (Draft)
PR2/SR2 Specs (Draft)
HR@1064nm > 99.95%
HR@532nm > 80%
HR loss@1064nm: < 100ppm
HR loss@532nm: < 1%
AR@1064nm < 1000ppm
AR@532nm < 10%
ROC = 32.1m +/-10cm
Wedge angle = 2deg (LIGO mirror)
HR@1064nm = 99.95%+/-0.01%
HR@532nm < 10%
HR loss@1064nm: < 100ppm
HR loss@532nm: < 1%
AR@1064nm < 500ppm
AR@532nm < 10%
ROC = -3.964m +/-1cm
Wedge angle = 2deg (LIGO mirror)

---
Task Assignment
LSC: Aso + ...
ASC: Michimura, Agatsuma
ISC Check: Somiya, Miyakawa + ...
Optical Layout: Aso --> Manual check by some student
Mirror Specs: Aso -> ....
Green Lock: Akutsu, Izumi