LCGT Main Interferometer Subsystem
Type B Review
2011/3/1@ICRR
Y. Aso on behalf of the LCGT MIF Working Group

---
Members
Y. Aso (U-Tokyo, Chair)
K. Somiya (Waseda)
O. Miyakawa (ICRR)
D. Tatsumi (NAOJ)
T. Akutsu (NAOJ)
K. Yamaoto (INFN)
K. Agatsuma (NAOJ)
M. Ando (Kyoto-U)
Y. Michimura (U-Tokyo)
E. Nishida (NAOJ)
C. Dan (NAOJ)
K. Izumi (NAOJ)
H. Yamamoto
K. Arai
K. Kawabe

---
Definition of the Subsystem
Main Interferometer
FP arms, PRC, SRC, Michelson, (OMC)
Length Control, Alignment Control, Lock Acquisition
Commissioning
No Hardware Manufacturing
Design and Commissioning

---
Requirements
Design an interferometer which can achieve the target sensitivity of bLCGT
Switchable between BRSE and DRSE
Robust operation
Efficient commissioning
bLCGT Target Sensitivity

---
Interfaces with Other Subsystems
Input/Output Optics
Mirror
Mirror specs
Input beam parameters
Modulation
Laser noises
OMC design
Seismic noise
Actuator dynamic range
Local sensors
MIF
Vibration Isolation
Optical layout
View ports
Vacuum
Sampling Frequencies
ADC dynamic range
Number of ports
Digital
Optical layout
View ports
PD specs
Modulation freq.
High speed servo
Cryogenic
Analog Electronics

---
Contents
Design of bLCGT Main Interferometer
iLCGT design
Activity plan during the tunnel excavation period
Commissioning Schedule
Risk Assessment

---
Main Interferometer Design
Arm Cavity Design
Angular Instability
Parametric Instability
Higher Order Spatial Modes
Recycling Cavities
Modulation Frequencies
Length Sensing Schemes
Folding
Alignment Sensing
Lock Acquisition Strategy
Green laser pre-lock
3rd Harmonics Demodulation
Non-Resonant Sideband
Optical Layout

---
Overview
Dual Recycled Fabry-Perot Michelson Interferometer in RSE mode.
ETMY
Larm
ITMY
PRM
PR2
From MC
Lp1
Lmy
ITMX
ETMX
Larm
Lp2
Lmx
Lp3
BS
PR3
SR2
Ls3
Lmi = (Lmx + Lmy)/2
Las = Lmy - Lmx
Lprc = Lp1+Lp2+Lp3+Lmi
Lsrc = Ls1+Ls2+Ls3+Lmi
Ls2
Ls1
SR3
SRM

---
Arm Cavity Design
Parameters
Length: 3000.00m
Finesse: 1546
g-factor : g1=1, g2=0.572
Prefixed
Arm Cavity g-factor
Spatial Mode Stability
Beam Spot Size => Thermal Noise
Angular Radiation Pressure Instability (Sidles-Sigg effect)
Parametric Instability
Beam Spot Size
Larger is Better for Thermal Noise
4.53cm@ETM => 0.6ppm diffraction loss
3.43cm@ITM
ITM coating is thinner than ETM
No problem for Thermal Noise

---
Angular Instability
Sidles-Sigg Stiffness Matrix
Angular Optical Spring Constant k [N*m/rad]
Large Beam (ITM=3.5cm, ETM=4.5 or 4.2cm)
4.4, -33.8 (g1 = 1, g2 = 0.572)
-4.6, 29.2 (g1 = -0.87, g2 = -0.6)
Small Beam (ITM=ETM=3.5cm)
5.0, -19.3 (g1 = g2 = 0.586)
-5.0, 19.3 (g1 = g2 = - 0.586)
Suspension
Torque [N*m]
Angle [rad]
+
H
+
-
k
Optical angular spring constant
Open Loop Gain: G = k*H
Check Stability

---
Suspension TF
Yaw Torque -> Yaw Angle
This is H

---
Small beam, positive (g1=g2=0.586)
Stable Eigenmode
2.2Hz
Unstable Eigenmode

---
Small beam, negative (g1=g2=-0.586)
Stable Eigenmode
1.6Hz
Unstable Eigenmode

---
Large beam, negative (g1=-0.87,g2=-0.6)
Stable Eigenmode
1.6Hz
Unstable Eigenmode

---
Large beam, positive (g1=1,g2=0.572)
Stable Eigenmode
2.65Hz
Unstable Eigenmode
Unstable Frequency
Large Beam
g1 = 1, g2 = 0.572: 2.65Hz
g1 = -0.87, g2 = -0.6: 1.6Hz
Small Beam
g1 = g2 = 0.586: 2.2Hz
g1 = g2 = - 0.586: 1.6Hz

---
Parametric Instability
There are dangerous regions to avoid in the g-factor space
Negative g-factor
Positive g-factor
The error requirement on the mirror ROC is stricter for the negative g-factor.
by
size 22 {(R_{nitalic p} / R_{nitalic n})}
Negative g-factor is about 3.7 times more
severe to ROC error in terms of PI
Negative g-factor: R ~ 1.9km
Positive g-factor: R > 7km
10m ROC errror for 1.9km mirror -> 0.5% error
100m ROC errror for 7km mirror -> 1.5% error

---
g-factor Comparison
		Thermal Noise (IR) / DRSE/BRSE [Mpc]	Optical Spring / Unstable Freq.	PI	ROC
(a)	g1=1 / g2=0.572	275/246	2.6Hz	Easy	ITM: >100km / ETM: 7000m
(b)	g1=-0.87 / g2=-0.6	273/245	1.6Hz	Severe	ITM: 1604m / ETM: 1875m
(c)	g1=0.586 / g2=0.586	266/241	2.2Hz	Easy	ITM: 7246m / ETM: 7246m
(d)	g1=-0.586 / g2=-0.586	266/241	1.6Hz	Severe	ITM: 1892m / ETM: 1892m
Arm Cavity Parameters
Length	3000.00m	ETM ROC	7000m
ITM Reflectivity	99.6%	ETM Beam Size	4.53cm
ITM ROC	flat	g-factor	0.572
ITM Beam Size	3.43cm	Round Trip Loss	<100ppm
ETM Reflectivity	>99.9945%	Finesse	1546

---
Higher Order Modes
TEM00 resonance has to be isolated from higher order modes
Higher order modes are large => Diffraction loss
Resonant curves of LG(l,m) modes

---
Maximum HOM Power, ITM ROC error

---
Maximum HOM Power, ETM ROC error

---
HOM RF Sideband Overlap

---
Recycling Cavity Lengths and Modulation Frequencies
Constraints
Resonate RF sidebands in desired parts of the interferometer
f1 sees both PRC and SRC
f2 is only resonant in PRC
MC length must not be too long (< 30m)
Modulation frequencies should not be too high
PD and QPD response
Modulation frequencies should not be too low
RF laser noise, CARM UGF
Michelson Average Length ~ 25m
Cryogenic radiation shield = 20m (BS <-> ITM)
Schnupp asymmetry
Not too large asymmetry
Room for Folding

---
RF Sideband Resonant Conditions
ETMY
f1 sideband resonates in PRC-SRC
f2 sideband resonates only in PRC
f3 sideband does not enter the interferometer at all
ITMY
REFL
PRM
PR2
ITMX
ETMX
POP
BS
PR3
Carrier
SR2
f1 sideband (PM 16.875MHz)
f2 sideband (PM 45MHz)
f3 sideband (AM 56.25MHz)
SR3
SRM
ASPO
OMCREFL
OMC
AS_DC

---
RC Length Parameter Scan
There are many candidates of Lprc, Lsrc, Las which satisfy the resonant conditions
Parameter selection procedure
Fix f2 to be 45MHz
Not too high, not too low
Choose Las
MICH reflectivity for f2 = 100%
Las = 3.3m or 6.6m
Choose Lprc
Resonate f2
65m< Lprc <85m
Choose f1
Integral (or half integral) multiple of the FSR of PRC
MC length must not be too long (GCD of f1 and f2 is large enough)
Choose Lsrc
f1 is resonant in SRC <= anti-resonant in PRC
f1 is anti-resonant in SRC <= resonant in PRC
65m < Lsrc < 85m
Still there are many candidates
Finesse of PRC-SRC for f1 varies depending on the MICH reflectivity to f1
Choose one with wide enough resonance to allow detuning of SRC by offset

---
Parameter Candidates
It is basically a matter of choosing f1 frequency

---
Final Candidates
	9MHz	11.25MHz	16.875MHz
Lprc	74.95m	73.28m	66.62m
Lsrc	74.95m	73.28m	66.62m
Las	6.66m	3.33m	3.33m
Lmc	33.3m	26.65m	26.65m
f3	13.5MHz(f2*3/10)	61.9MHz(f2*11/8)	56.3MHz (f2*10/8)
DDM freq.	22.5MHz, 31.5MHz	16.9MHz, 50.6MHz	11.25MHz, 39.4MHz
Pros and Cons
Loop noise 11.25MHz < 16.875MHz < 9MHz (worse < better)
9MHz needs a bit longer MC (33m not 27m)
9MHz has a longer asymmetry (6.6m compared to 3.3m)
11.25MHz is incompatible with 3rd harmonics demodulation
9MHz and 16.875MHz have larger SRCL non-linearity

---
Signal Extraction Ports
ETMY
f1 sideband resonates in PRC-SRC
f2 sideband resonates only in PRC
f3 sideband does not enter the interferometer at all
REFL
ITMY
PRM
PR2
ITMX
ETMX
POP
BS
PR3
Carrier
SR2
f1 sideband (PM 16.875MHz)
f2 sideband (PM 45MHz)
f3 sideband (AM 56.25MHz)
SR3
SRM
ASPO
OMCREFL
OMC
AS_DC

---
Modulation Types
PM or AM ?
AM wastes laser power
Low loss method exist [N. Ohmae, Opt. Lett.]
---> complicated
Mach-Zhender may introduce extra noise.
Conventional Scheme
  f1:PM, f2:PM
No MZ
No AM
Conventional Scheme + NRS
   f1:PM, f2:PM, f3:AM
May need MZ
Need AM
AM can be weak if used only for lock acquisition
AM-PM Scheme
 f1: AM, f2:PM
Default:
Conventional Scheme + (NRS)
Need MZ
Need AM
May have a problem with WFS at AS

---
Signal Ports and Naming Convention
How to decipher a signal name ?
REFL_1I
Reflection port demodulated at f1 freq.
in I-phase.
Demodulation Phase
Detection Port Name
Demodulation Frequency
REFL_1DmI
Reflection port demodulated at
f3-f1 freq. in I-phase.
Demodulation Phase
Detection Port Name
Demodulation Frequency
1Dm: f3 - f1
1Dp: f3 + f1
2Dm: f3 - f2
2Dp: f3 + f2
DC Power at PDs
Attenuated to be less than 100mW on each PD

---
Sensing Matrix
BRSE: 16.875MHz - 45MHz
	DARM	CARM	MICH	PRCL	SRCL
AS_DC	1	4.2e-5	1.0e-3	4.8e-6	4.7e-6
REFL_1I	5.4e-3	1	4.3e-5	6.5e-3	4.3e-3
REFL_1Q	5.0e-3	1.3e-2	1	1.02	0.67
POP_2I	2.3e-2	4.3	1.0e-2	1	2.5e-4
POP_1I	8.7e-2	16.23	3.1e-2	2.1	1
Large Coupling from CARM to PRCL & SRCL
Gain hierarchy to suppress CARM
PRCL, SRCL mixed to MICH

---
Sensing Matrix
Use of Non-Resonant Sideband (f3: 56.25MHz)
BRSE: 16.875MHz - 45MHz
	DARM	CARM	MICH	PRCL	SRCL
AS_DC	1	4.1e-5	1.0e-3	4.8e-6	4.7e-6
REFL_1I	5.4e-3	1	3.9e-5	5.4e-3	4.5e-3
REFL_1DmQ	4.8e-3	2.5e-3	1	0.7	1.3
REFL_2DmI	2.3e-2	8.3e-2	0.18	1	0.32
REFL_1DmI	8.7e-2	1.5e-2	2.4e-2	1.7	1
CARM coupling is now small
Shot noise may not be so good.

---
Loop Noise Coupling
Just looking at sensing matrices is not enough
Auxiliary DOFs in general have worse shot noise than DARM
MICH is particularly problematic one.
MICH unavoidably couples to DARM (1/finesse)
MICH signal is weak
Driving MICH with this bad signal ---> Noise coupling to DARM
How the MICH signal at REFL_Q is generated ?
SY Port
MICH signal
+
+
-
Q-phase
Sideband imbalance --> Weak signal

---
Loop Noise Coupling
Formulation used here:
Canonical IFO DOFs
(DARM, CARM, MICH, PRCL, SRCL)
Mirror displacement
size 20 {vec n_{nitalic s} }
Shot Noise
Calibrated
Output
Displacement
noise
Detector
Sensing
Calibration
+
D
S
C
size 20 {vec x_{nitalic c} }
size 20 {vec n_{nitalic d} }
+
+
-
Actuator
Filter
F
A
+
F'
Feed forward
size 26 {vec x_{nitalic c} = (I+G)^{-1} cdot S cdot vec n_{nitalic s} + (I+G)^{-1} cdot SD cdot vec n_{nitalic d}}
size 26 {G equiv S cdot D cdot A cdot (F+F')}
D: Optical Gain Transfer Function calculated by Optickle
A: Mechanical TFs of the mirror suspensions + optical spring stiffness
F: Feedback filters
F': Feed forward matrix
S: Sensing matrix (here I just used identity matrix)

---
Loop Noise Coupling
Formulation used here:
Canonical IFO DOFs
(DARM, CARM, MICH, PRCL, SRCL)
Mirror displacement
size 20 {vec n_{nitalic s} }
Shot Noise
Calibrated
Output
Displacement
noise
Detector
Sensing
Calibration
+
D
S
C
size 20 {vec x_{nitalic c} }
size 20 {vec n_{nitalic d} }
+
+
-
Actuator
Filter
F
A
+
F'
Feed forward
size 26 {vec x_{nitalic c} = (I+G)^{-1} cdot S cdot vec n_{nitalic s} + (I+G)^{-1} cdot SD cdot vec n_{nitalic d}}
size 26 {G equiv S cdot D cdot A cdot (F+F')}
Ideally, G is diagonal (D・A is diagonal), but in practice it is not.
Off diagonal elements of G introduce the shot noise of auxiliary DOFs to DARM
F' is added to diagonalize G (Feed forward)

---
Control Loop Gains
UGFs
	BRSE	DRSE
DARM	200Hz	200Hz
CARM	10kHz	10kHz
MICH	50Hz	10Hz
PRCL	50Hz	50Hz
SRCL	50Hz	50Hz

---
9MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
BRSE: f1=9MHz, Feed forward gain=100

---
9MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
DRSE: f1=9MHz, Feed forward gain=100

---
11.25MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
BRSE: f1=11.25MHz, Feed forward gain=100

---
11.25MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
DRSE: f1=11.25MHz, Feed forward gain=100

---
16.875MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
BRSE: f1=16.875MHz, Feed forward gain=100

---
16.875MHz-45MHz
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1Q
PRCL: POP 2I
SRCL: POP 1I
DRSE: f1=16.875MHz, Feed forward gain=100

---
16.875MHz-45MHz
Double Demodulation with Non-Resonant Sideband
BRSE: f1=16.875MHz, Feed forward gain=100
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1DmQ
PRCL: REFL 2DmI
SRCL: REFL 1DmI

---
16.875MHz-45MHz
Double Demodulation with Non-Resonant Sideband
DRSE: f1=16.875MHz, Feed forward gain=100
DARM: ASDC
CARM: REFL 1I
MICH: REFL 1DmQ
PRCL: REFL 2DmI
SRCL: REFL 1DmI

---
SRCL Non-Linearity
SRC detuning by offset => Error signal non-linearity
Up conversion noise
Formalization
x: mirror displacement [m]
y: error signal [W]
size 25 {y(t) = a x(t) + b x^2(t)}
Calibration
size 25 {x_{nitalic e}(t) = y(t)/a = x(t) + (b/a) x^2(t)}
xe: Displacement equivalent error signal [m]
b/a: dimension is 1/m
Non-linear part
Total frequency conversion noise
[ref. Applied Electronics, Koichi Shimoda]
size 25 {P_{nitalic conv}(f) = (b over a)^2 [int from{0} to{f} P(f - f') P(f') df' + 2 int from{0} to{infinity} P(f + f') P(f') df' ]}
Down Conversion
Up Conversion
P(f): Displacement equivalent noise spectrum [m2/Hz], one sided.

---
SRCL error signal range, f1=9MHz
b/a = 1.3e8 m-1
f1=9MHz

---
SRCL error signal range, f1=11.25MHz
b/a = 2.7e7 m-1
f1=11.25MHz

---
SRCL error signal range, f1=16.875MHz
b/a = 1.05e8 m-1
f1=16.875MHz

---
Up Conversion Noise
Blue Curve: SAS displacement noise + SRCL shot noise
Green Curve: Above noise suppressed by the servo
Red Curve: Non-linear up conversion noise (b/a=1e9)
It does not seem to be a problem

---
PD Dynamic Range
Offsets in MICH and CARM --> Dynamic Range of RFPD circuit
SRC detuned: f1 SB is not at the peak of the resonance
f1 gets some phase rotation at REFL and POP
f1 is no longer pure PM for the carrier
Large offset at PDs for f1 SB
The buffer op-amp of the PD circuit has to handle this large RF signal
Max RF amplitude: ~ 0.1Vpp (?) Slew rate and linearity
Noise of the op-amp: >1nV/rtHz
Dynamic Range ~ 160dB
Actual Numbers
REFL_1 PD gets 55mW of offset RF signal@f1 frequency(16.875MHz) in DRSE
Input power equivalent noise of op-amp is 55mW/1e8/rtHz = 5.5e-10W/rtHz
Sensitivity is 1.64e9 W/m for CARM, 2.0e6 W/m for MICH
Displacement equivalent op-amp noise is 3.4e-19m/rtHz for CARM, 2.7e-16m/rtHz for MICH
POP_1 PD gets 7.2mW of offset RF signal@f1 frequency(16.875MHz) in DRSE
Input power equivalent noise of op-amp is 7.2mW/1e8/rtHz = 7.2e-11W/rtHz
Sensitivity is 3.3e5 W/m for SRCL
Displacement equivalent op-amp noise is 2.2e-16m/rtHz for SRCL

---
Risk: PD Noise Coupling

---
Risk: PD Noise Coupling with Feed Forward

---
Risk: SRCL detuning by Offset
How to deal with the PD dynamic range problem ?
Find a good op-amp with larger dynamic range
Increase the feed forward gain
Current injection to PD to cancel the large
RF signal (like AS_I servo in iLIGO)
Pre-rotate f1 sidebands

---
Conclusion on the Modulation Frequencies
	9MHz	11.25MHz	16.875MHz
Loop Noise	Good	OK	Good
SRCL Non-linearity	OK	OK	OK
3rd Harmonics Demodulation	OK	No	OK
Lprc,Lsrc	74.95m	73.28m	66.62m
Asymmetry	6.66m	3.33m	3.33m
Lmc	33.3m	26.65m	26.65m
f3	13.5MHz(f2*3/10)	61.9MHz(f2*11/8)	56.3MHz (f2*10/8)
DDM freq.	22.5MHz, 31.5MHz	16.9MHz, 50.6MHz	11.25MHz, 39.4MHz

---
Displacement Noise Requirements
Formulation used here:
Canonical IFO DOFs
(DARM, CARM, MICH, PRCL, SRCL)
Mirror displacement
size 20 {vec n_{nitalic s} }
Shot Noise
Calibrated
Output
Displacement
noise
Detector
Sensing
Calibration
+
D
S
C
size 20 {vec x_{nitalic c} }
size 20 {vec n_{nitalic d} }
+
+
-
Actuator
Filter
F
A
+
F'
Feed forward
size 26 {vec x_{nitalic c} = (I+G)^{-1} cdot S cdot vec n_{nitalic s} + (I+G)^{-1} cdot SD cdot vec n_{nitalic d}}
size 26 {G equiv S cdot D cdot A cdot (F+F')}
Safety factor
(I+G)-1SD: transfer function from nd to xc
Require nd's contribution to xc to be 1/10 of DARM shot noise
Requirement on each mirror's displacement noise
(seismic, thermal, etc)

---
Displacement Noise Requirements
BRSE

---
Displacement Noise Requirements
DRSE

---
Folding of Recycling Cavities
Straight Recycling Cavity ==> Nearly Degenerated
How badly degenerated ?
g-factor (g1*g2) = 0.9998
One-way Gouy Phase Shift = 0.7deg.
Transverse Mode Spacing = FSR/257
PRC Finesse = 57 (FWHM = FSR/57)
(PRCL = 42.5m, occupying the same tunnel space)
HG(m,n) modes resonate
up to m+n = 2
LG(p,q) modes resonate
up to 2*p+q = 2
The RFSB spatial modes are unstable (alignment fluctuation, thermal lensing)
Folding the PRC and focusing the beam inside ==> Stable PRC
How about SRC ?
f1 SB resonates in PRC-SRC
If PRC is stable, HOMs cannot resonate in PRC-SRC.
No need to fold SRC ? -> Not so simple
GW sidebands may be scattered to HOMs by mode mismatch
between the arm cavities and SRC.
The loss of GW sidebands is higher for degenerated SRC
(Kip Thorne & Yi Pan)

---
SRC Folding
Yi Pan's report (LIGO-T-060004): ITM ROC error of 0.25% ==> Up to 2% GW Signal Loss
        Loss ∝ (ITM Error)2 ==> 1% error -> 32% signal loss
The situation for LCGT should not be too different from aLIGO
But we should check it anyway
HOM simulation using Finesse
No definitive answer yet
Large (1W) TEM00 leak at AS port if not folded
Seems like non-folded SRC is bad
For the moment, the default design is to fold SRC
Cost increase (two more vacuum tanks, suspensions, mirrors)
Additional control of SR2, SR3 alignment (we have to control PR2, PR3 anyway)
Folded SRC provides a convenient port for green laser injection
The beam size at AS is smaller and easy to handle (4mm)
If necessary, the tunnel can accommodate straight SRC (Lsrc=40m)

---
Folding Design
How Stable ?
HOM isolation ==> Stable is better
Too stable ==> Arm alignment signal is suppressed
Compromise between HOM and ASC ==> One-way Gouy Phase Shift = 20deg.
Not Optimized Yet
How to fold the PRC/SRC ?
PR2
PRM
Lp1
Lp2
Lp3
BS
PR3
Constraints
Minimum vacuum chamber spacing: 2.7m
Astigmatism: Smaller folding angle is better ==> Longer Lp2
Mirror locations are almost uniquely determined
Play with ROCs of PR2 and PR3

---
Beam Propagation in PRC
Beam Width Change in PRC

---
Folding Optimization
Mirror distances: fixed
One-way Gouy phase: 20deg
Small Beam Spot ==> Large Thermal Lensing
Beam Size on the Mirrors vs PR3 focal length

---
Thermal Lens
ITM Lensing
1W heat deposit
on the mirror
ROC=11661km, No Problem
Thanks to the high thermal conductivity of sapphire
1mK Temperature Raise
Calculation by Muzammil A. Arain (UFL)

---
Thermal Lens
PRM, PR2
PR3, BS
Beam Spot Size: 35mm
Incident Power: 800W
Beam Spot Size: 4mm
Power on HR: 800W
	PRM	PR2	PR3	BS
10ppm absorption	18% ROC error	0.2% ROC error	0.3% ROC error	ROC 100km
1ppm absorption	2% ROC error	0.02% ROC error	0.03% ROC error	ROC 1000km

---
ROC Error of PR2, PR3
Very Sensitive to PR3 ROC Error

---
How to Handle PR3 ROC error ?
iLCGT
No SAS. Suspensions can be easily moved by more than 10cm
PR2 and PR3 for iLCGT will be used in bLCGT
PRM is a blank with curvature
bLCGT
PR2 and PR3 position can be changed by more than 10cm at the installation time
After installation, it takes time to move them
Installation and Adjustment Plan
Make PR2 and PR3
Measure the ROCs of PR2 and PR3
Install them to iLCGT
Adjust the location of PR2 and PR3 to form the desired telescope
Remember the optimal location of PR2 and PR3
Measure the ROC of PRM, which match the actually formed PRC.
Order a PRM according to the measured ROC.
Install PR2 and PR3 at the remembered positions for bLCGT
Install the PRM
PRM
PR2
PR3
BS
Lp1
Lp2
Lp3

---
Modulation frequency Fine adjustment
f1 and f2 SBs are not exactly anti-resonant to the arm cavities
f1 and f2 get finite phase shifts from the arm cavities
In general, f1 and f2 cannot fully resonate in the PRC at the same time
Fine adjust the MC length (thus f1, f2 frequencies) to achieve
Φ1:Φ2 = f1:f2 (Φ1: phase shift of f1 by the arm, Φ2: phase shift of f2 by arm)
Lprc and Lsrc are adjusted accordingly
Locations of RF SBs in the FSR of AC

---
Lmc adjustment = -1.37cm
f2 resonance
Adjust Lprc
by 3.7mm
f1 resonance
Adjust Lsrc
by 7.4mm

---
Alignment Sensing and Control
Basic Strategy
Combination of Wave Front Sensing (WFS) and Optical Levers
Arm Cavity Misalignment Modes
Combinations of the ITM, ETM rotation to diagonalize the angular stiffness matrix
Hard - Soft basis
[ Common Hard (CH), Common Soft (CS), Differential Hard (DH), Differential Soft (DS) ]
Folding and ASC
RCs are very stable --> TEM01 and TEM10 modes are suppressed
No ASC signal of TMs
One-way Gouy phase shift in RCs --> about 20 deg.
Needs optimization
What to do with the alignment of folding mirrors ?
Not enough DOF from WFS
Control a linear combination of PRM,PR2,PR3 angles ?
Is it stable ?
Simulations with Optickle (Pickle), work in progress

---
bLCGT ASC Sensing Matrix

---
Lock Acquisition
Principle: Lock acquisition has to be a deterministic process
Lock acquisition steps
Pre-lock the arms at off-resonant positions (Green laser pre-lock)
Lock the central part using the third harmonics demodulation
or non-resonant sideband
Reduce the arm offset to the full resonance
The error signals to low noise ones
Pre-lock here
f1
f1
f1
f2
f2

---
Green Laser Pre-Lock
Basic ideas for green laser lock
Two green lasers (Frequency doubled from 1064nm)
Green lasers are phase locked to the main laser by PLL
Green Lasers are injected from PR2 for X-arm, and SR2 for Y-arm
PR3 and SR3: High reflectivity for green (>90%)
BS is transparent to green
Arm finesse for green is low (~10)
Two green lasers are frequency shifted by ~ 100MHz
Lock the arms independently by the green lasers
Arm cavity length can be finely tuned by sweeping the PLL
PRM
PR2
PR3
SR3
SR2
SRM
GreenX
GreenY
Main Laser

---
Third Harmonics Demodulation
Beat between 2*f1 and f1 (Insensitive to the arms)
Useful for lock acquisition.
Substitutes for NRS. No MZ, no AM necessary -> simple.
Unfortunately, all the f1 candidates cannot use this method in the usual sense,
because 2*f1 resonates in the PRC-SRC.
(f1 frequencies tested: 9MHz, 11.25MHz, 13.5MHz, 16.875MHz, 19.3MHz)
Actually, 3rd harmonics demodulation produces some signal due to difference in the
response of 2*f1 and f1.
However, strong interference from the carrier is present (carrier-3*f1 beat).
@100Hz

---
Third Harmonics Demodulation
PRCL
3rd Harmonics signal during lock acquisition
CARM offset: 2nm -> 0
MICH is affected by CARM
MICH
SRCL

---
Non-Resonant Sideband for Lock Acquisition
NRS serves as a local oscillator
insensitive to the arms
PRCL
NRS signals during the lock acquisition
CARM offset: 2nm -> 0
SRCL
MICH

---
Detailed Optical Layout
Detailed optical layout design is a non-trivial task !
We have to ...
Take into account wedge deflection
Make the two arms at the right angle
Track the optical path length (for SB resonant conditions)
Track the Gaussian mode evolution
Track the Gouy phase evolution
Take into account the dispersion effect for the green beams
Trace secondary beams (AR reflected)
Generate CAD files
A python package to do the above job was developed.
gtrace: A Gaussian ray tracing library
(Validation of the library was done by Chen Dan)

---
iLCGT
iLCGT has to be on the way to bLCGT
Minimum detour from the straight path to bLCGT
Most parameters are the same as bLCGT
Interferometer Configuration
Fabry-Perot Michelson Interferometer (no recycling)
Arm cavity finesse is the same as bLCGT
Mirrors
Test masses are fused silica
All the other mirrors are to be used in bLCGT (BS and the folding mirrors)
PRM is a blank with curvature (for mode matching)
No SRM installed.
LSC
A simple frontal modulation scheme using f1 SB only
ASC
Wave front sensing at REFL and AS

---
iLCGT Sensing Matrices
LSC
ASC (Diagonalized)

---
What to do next ?
ASC and Folding Optimization
One-way Gouy Phase in RCs
HOM in RCs
Folding Design
ASC
Technical Noise Couplings
Laser Noise (frequency, intensity)
Modulator phase noise
Actuator noise (hierarchical control)
PD noise
etc ....
Requirements to
other subsystems
OMC Design (together with the IOO group)
Requirements (HOM reduction ratio)
Control Schemes
Prototype test

---
Simulated IFO plant
Expedite the commissioning
Make effective use of tunnel excavation & vacuum installation period (2 years)
Develop a computer model of the IFO
Connected to the digital control system
Develop the LSC & ASC digital servo system before actual interferometer is available
Once real interferometer is installed, use the pre-developed servo system
Linear Model
IFO
model
REFL_1I
REFL_1Q
POP_1I
POP_2I
AS_DC
Mirror Actuators
Laser Freq.
Laser Intensity
Seismic Motion
etc ...
Model Generation: Optickle
Implementation: Digital System
Non-Linear Model
Time-domain simulation: e2e
Non-realtime
Simulate lock acquisition etc..
Digital Control System

---
Schedule
During the construction period

---
Schedule
Commissioning Period

---
Risks
Arm loss may be higher --> PRC becomes under coupled
Prepare several PRMs with slightly different reflecvitities
Arm loss may be smaller
Shot noise increase of the DDM signals
HD phase depends on the amount of reflectivity mismatch between the arms
DARM offset may have to be very large
HD phase may be almost 90 deg.
SRC detuning by offset
PR3 ROC error
Leave room for moving PRM, PR2, PR3, SRM, SR2 and SR3
ASC design
How to control the folded PRC/SRC ?
OMC design
Control Schemes

---
Summary
Interferometer Design (iLCGT)
Interferometer Design (bLCGT)
RSE interferometer
Variable BRSE/DRSE
66m folded recycling cavities
Fabry-Perot Michelson
No Recycling
Length Control Scheme
16.875MHz-45MHz PM, Single demodulation
Optional Non-Resonant Sideband
Alignment Sensing Scheme
WFS & Optical Lever
Needs more study
Lock Acquisition
Green laser pre-lock
Third harmonics demodulation or NRS
TO DO
Alignment Sensing Schemes
Folding design optimization
OMC design
Technical noise couplings
Simulated IFO plant