Input Mode Matching of LCGT
2012/1/5, Yoichi Aso

---
Baseline layout: bLCGT
Baseline layout: bLCGT
Negative g-factor (R1 = 1.68km, R2 = 1.87km)
Sapphire Test Masses (n = 1.754)
Vacuum chambers are installed so that the mirrors
are centered for the bLCGT layout
Negative g-factor (R1 = 1.68km, R2 = 1.87km)
Sapphire Test Masses (n = 1.754)
Vacuum chambers are installed so that the mirrors
are centered for the bLCGT layout
Several possibilities for iLCGT
Test Mass
(A) New TM from CSIRO (ROCs are the same as bLCGT)
(B) iLIGO Mirror (R1 = Flat, R2 = 7.2 km)
Optimize Folding Part
Tweak the distance between PR2 and PR3 to optimize the mode matching
between the PRC and the arm cavities. Do the same for SRC.
(a) Yes, (b) No
Geometric layout correction method
How the mirrors are moved to compensate for the change of the ITM position
(1) Move PR3, Rotate PR2 and BS
(2) Laterally move ITMs

---
Detailed notes on the iLCGT layout (You can skip this slide)
About the folding part optimization
A good mode matching between the PRC/SRC and the arm cavities is necessary to do power- or
signal-recycling. If we want to do the Silica RSE, this is crucial. (See Appendix A)
On the other hand, for FPMI or DRMI, this mode matching is not that important. What we care
is the mode matching of the input beam to the arm cavities, or DRMI.
Folding part optimization involves moving the PRC/SRC mirrors. We want to avoid this if possible.
About the geometric layout correction
The bLCGT ITMs have a finite wedge angle on the AR side. In order for the incident beam to hit the
 HR surface at right angle, the beam must hit the AR from slightly non-normal angle.
Because of this, when the ITMs are put 26.6m further from the BS in iLCGT, the beam will not
  hit the center of the ITMs.
We have to correct this by either moving the ITMs laterally (option 2) or by tweaking the PRC
  mirrors to correct the incident beam angle and position (option 1). (See Appendix B)
Option 2 is simple because we do not have to move the PRC mirrors between iLCGT and bLCGT.
However, option 2 requires that the arm cavity beam axis be shifted laterally by 7cm. This means that
 the beam does not go through optical windows on the GVs separating the central part and the arm
pipes. It is not good for initial alignment. Therefore, the GVs have to be displaced for iLCGT, which
 is possible according to Saito-san.

---
Default iLCGT: iLCGT-Aa2
CSIRO Mirrors
Optimize the Folding Part
Laterally move ITMs
I will also consider:
iLCGT-Aa1 (CSIRO, Optimize Folding, Move PR3)
iLCGT-Ab1 (CSIRO, No Folding Optimization, Move PR3)
iLCGT-Aa2 (CSIRO, Optimize Folding, Laterally move ITMs)
iLCGT-Ab2 (CSIRO, No Folding Optimization, Laterally move ITMs)
iLCGT-Ba1 (iLIGO, Optimize Folding, Move PR3)
iLCGT-Bb1 (iLIGO, No Folding Optimization, Laterally move ITMs)
iLCGT-Ba2 (iLIGO, Optimize Folding, Move PR3)
iLCGT-Bb2 (iLIGO, No Folding Optimization, Laterally move ITMs)

---
Mode Matching for bLCGT
MC
MMT1
PRM
MMT2
L1, L2 and L3 are given. Optimized RMMT1 and RMMT2.
L1=7.5m, L2=4.5m, L3=4.7m
RMMT1 = -21.579m, RMMT2 = 23.968m
This is the start point. We won't change the ROCs of the MMT mirrors.
We will move MMT1 and MMT2 to adjust the mode matching.
L1
L2
L3

---
iLCGT Input Mode Matching
From the next slide, iLCGT mode matching is shown for many cases.
For each case, the bLCGT layout is transformed with the following procedure
Start from the bLCGT layout
Change the TMs to the silica mirrors: (A) CSIRO Mirrors, (B) iLIGO TMs.
Move ITMs by 26.6m
Do either of the followings to hit the center of ITMs with right angle:
   (1) Rotate PR2 and BS, move PR3 and adjust the ITM wedge angle.
(2) Move the ITMs laterally and adjust the ITM wedge angle.
Do either of the followings:
(a) Adjust the distance between PR2 and PR3 to match the eigen-modes of the PRC
   and the arm cavities.
   (b) Do nothing.
Eigen-modes of the main interferometer
After the layout is adjusted, the eigen-mode of the arm cavity is propagated to the PRM to
obtain the beam parameter, q0, at the AR surface of the PRM. q0 is calculated also for the
case without PRM (just propagating the beam on the PRM HR surface by the thickness of PRM).
Additionally, the eigen-mode of the DRMI is calculated and translated into the beam parameter
at the AR surface of the PRM.
Mode matching with the beam from the input MMT
The beam coming out of the input MMT is propagated to the AR surface of the PRM.
The beam parameter is compared with the ones calculated above to get the mode matching.
This is repeated by sweeping the positions of the MMT mirrors to see if the mode matching
can be recovered by moving those mirrors.

---
iLCGT-Aa1
Without PRM
With PRM
DRMI

---
iLCGT-Ab1
Without PRM
With PRM
DRMI

---
iLCGT-Aa2
Without PRM
With PRM
DRMI

---
iLCGT-Ab2
Without PRM
With PRM
DRMI

---
iLCGT-Ba1
Without PRM
With PRM
DRMI

---
iLCGT-Bb1
Without PRM
With PRM
DRMI Cavity is Unstable

---
iLCGT-Ba2
Without PRM
With PRM
DRMI

---
iLCGT-Bb2
Without PRM
With PRM
DRMI Cavity is Unstable

---
Conclusion
The input mode matching is good (more than 85%) even without the folding part
  optimization (b cases) for CSIRO mirrors.
For iLIGO TMs, the folding part optimization is inevitable.
Absence of PRM does not degrade the mode matching so much.
If silica RSE is not necessary (DRMI test is sufficient), iLCGT-Ab2 is probably best,
  as it provides reasonable mode matching rates for FPMI and DRMI, plus no adjustment
  of auxiliary mirror positions is necessary.
For silica RSE, better mode matching between the RCs and the arm cavities is necessary.
  In this case, iLCGT-Aa2 is best.
If CSIRO mirrors are not available, we should employ iLCGT-Ba2.

---
Appendix A
Procedure for optimizing the folding part of the recycling cavities.

---
1st. step: Optimize the ROCs of PR3 and PR2 for bLCGT
    Target
Gouy phase change from ITMX to PRM is 20 deg.
Beam spot sizes on PR2 and PRM are equal
Method
Propagate a beam matching the arm
 cavity mode from ITMX to PRM
Repeat this with different combinations
of PR3 and PR2 ROCs.
PRM ROC is set to the ROC of the beam
  hitting PRM.
Do the same for SRC
PR2
PRM
ITMX
BS
PR3
PRC/SRC parameters after the optimization
PRM ROC	PR2 ROC	PR3 ROC	PRM Spot Size	PR2 Spot Size	PR3 Spot Size
303.96m	-2.763m	24.574m	4.03mm	4.03mm	36.48mm
SRM ROC	SR2 ROC	SR3 ROC	SRM Spot Size	SR2 Spot Size	SR3 Spot Size
303.96m	-2.776m	24.584m	4.03mm	4.03mm	36.33mm

---
2nd step: Move and Change ITMs
PR2
Move
PRM
ROC
1.5km -> Flat
ITMX
BS
PR3
Need to tweak the positions and orientations of PR2, PR3 and BS
to make the beam normal incidence to ITMs
Test: Is this PRC stable ?
Calculate the round trip (PRM -> ITM -> PRM) ABCD matrix
See if -1 < (A+D)/2 < 1 is satisfied ===> No ! (A+D)/2 = -1.85
We cannot use this configuration.

---
3rd step: Tweak the distance between PR2 and PR3
Move
Move
PR2
PRM
ITMX
BS
PR3
Keep the PRC length unchanged
Find the optimal displacement to match the eigen mode of PRC with the arms
By moving PR2 by 17cm and PRM by 34cm, the two modes match very well
Mode matching between the input beam from MMT and the PRC eigen mode = 99.8%
Mode matching between the PRC eigen mode and the arm cavity eigen mode = 99.99%
(Using the same mirrors and the same MMT, optimized for bLCGT)

---
Appendix B
Geometric layout correction for iLCGT

---
Oblique incidence due to
the ITM wedge
ITM
(bLCGT)
Arm Cavity Axis
From BS
From BS

---
The beam does not hit the center of the ITM if we just move it by 26.6m
ITM
(iLCGT)
ITM
(bLCGT)
From BS
26.6m

---
Adjustment Method 1
Move BS and PR3
Maximum shift ~ 2cm
Also adjust SRC
ITM
(iLCGT)
ITM
(bLCGT)
Change the angle and position of the incident
beam by adjusting the orientations and positions
of PR2, PR3 and BS.
From BS
Change the wedge angle

---
Adjustment Method 2
Laterally move ITM
Do not touch other mirrors
The beam does not go through the optical window on the GV
GV
ITM
(iLCGT)
ITM
(bLCGT)
From BS
Optical Window
Φ10cm
7cm