Internal Review of
Main Interferometer Subsystem
2012/1/27
Yoichi Aso

---
Overview: Definition and scope of the subsystem
MIF includes: Arm cavities, Recycling cavities, Michelson part
Assigned tasks
Parameter selection of the MIF
Length, ROC, etc
Optical layout
Design of the control scheme
LSC, ASC
Lock acquisition scheme
Commissioning
For some reason, detector characterization is a part of MIF
Maybe the Instrument Control will be too

---
Interface with other subsystems
Mirror
Reflectivity, ROC, Loss, other specs.
Suspension
Isolation requirements
Actuator design
Installation procedure
Suspension+AOS
Local sensors
Laser
Power
IOO
Intensity Noise
Frequency Stabilization Path
Input/Output mode matching
Detection ports
OMC
Green lock
AOS
Scattered light
Digital System
Servo model
Analog electronics
PD, QPD, I-Q demodulator, servo
filters, etc
Vacuum
Layout

---
Design Status
IFO params	semi-final	LSC principle	final
ASC principle	preliminary	Servo modeling	TBD
Green Lock Design	preliminary	Optical Layout	final
Frequency Servo	preliminary	Commissioning Plan	TBD
OMC	early stage	Analog Circuits	TBD

---
iLCGT Design
Target Specs
Stably operate Fabry-Perot Michelson Interferometer
No sensitivity requirement
Final(?) Design
Based on bLCGT design
Use Silica TMs
ROCs are the same as bLCGT
Locations of TMs are shifted by 26.6m/30m from bLCGT
ITMs laterally shifted by 7cm
Arm GV is shifted accordingly
No folding part optimization
PRM will not be installed (PR2, PR3 will be)
Tweak the Input MMT to get a reasonable mode matching
SRC is isolated vacuum wise.
Pick-off the AS beam before the GV
Green lock may be tested with X-arm

---
(Virtual) Layout Change in iLCGT
Location of ITMs: Shifted by 26.6m from the bLCGT position
Location of ETMs: Shifted by 30m from the bLCGT position
ITM lateral shift: 7cm
PR2
Move
Move
lateral shift
7cm
PRM
26.6m
30m
ITMX
ETMX
BS
PR3

---
Mode Matching (iLCGT-Ab2)
Without PRM
With PRM
DRMI
JGW-G1200763-v1

---
Vacuum Isolation of SRC
Separate Vacuum
during iLCGT
Pick-off the AS
beam here.

---
Schedule
Task list during tunnel excavation
(to be finished by March 2014)
Intensity noise, frequency noise requirements
LSC/ASC Servo model including hierarchical actuation
Frequency servo topology
Servo model noise analysis
Servo model implementation on RTS
Green lock design
Green injection system assembly
Commissioning planning,
Suspension positioning method
Optical bench layout (with IOO)
Analog electronics list up/Design

---
Installation & Commissioning Scenario

---
Quality assurance
Each component will be tested by corresponding subsystem
(e.g. mirrors, laser, etc)
The quality of MIF is the noise level of the interferometer
It is guaranteed that the quality will not meet the requirement
at first
Thorough and careful planning for the commission is the best
quality assurance

---
Risk Management
Risk factors
StackB is too noisy
=> Strong damping, strong actuators at the expense of noise
Laser frequency noise is too large
=> Spend more time on the frequency stabilization servo
Mirror quality is poor
=> ....
Commissioning takes too long (very likely to happen)
=> Work harder folks !

---
bLCGT

---
Requirements
Operate the interferometer with the following noise level
Duty cycle > 90%(?)

---
Preliminary Design
Interferometer Parameter
Arm Finesse	1550	Arm Length	3km	PRG	10
SRM Reflectivity	85%	Input Laser Power	51W	PRC Length	66.6m
SRC Detuning	3.5°	SRC Length	66.6m	MICH Asym.	3.33m
g1	-0.786	g2	-0.602	g1・g2	0.473
R1	1.68km	R2	1.87km
For details:
http://gwwiki.icrr.u-tokyo.ac.jp/JGWwiki/LCGT/subgroup/ifo/MIF/OptParam

---
g-factor selection
Beam Size
ITM: 3.5cm, ETM:4.0cm
4.0cm is the maximum spot size for 22cm mirror.
3.5cm beam at the central part is easier to handle.
Since ITMs have less coating layers, the thermal noise is not
compromised by 3.5cm beam size on ITMs.
Decided:
size 32 {g_1 cdot g_2 = 0.473}
Candidates
g1=0.786, g2=0.602 (R1=14km, R2=7.5km)
g1=-0.786, g2=-0.602 (R1=1.68km, R2=1.87km)

---
Arm Cavity HOM Resonances
No significant difference between Positive and Negative
See JGW-G1200789
Parametric Instability
Colored area = Unstable mode exists
See JGW-T1200787

---
Sidles-Sigg Instability (ASC)
WFS UFG for Pitch has to be lower than 1Hz
For arm power > 330kW, Pitch instability frequency > 1Hz
for positive g-factor
Negative g-factor never makes Pitch unstable
Current arm power (compromised to deal with high sapphire
absorption) = 250kW --> even positive g-factor is OK
Original (desirable) arm power = 376kW
        --> positive g-factor is not an option
Conclusion
Negative g-factor is better
Positive g-factor limits us to operate only with low power

---
Sideband Resonant Conditions for Signal Extraction
Signal Ports
DARM: AS_DC
CARM: REFL_1I
MICH: REFL_1Q
PRCL: POP_2I
SRCL: POP_1I
Y-arm
ITMY
PRM
REFL
PR2
POX
ITMX
ETMX
Laser Beam
From MC
BS
X-arm
PR3
SR2
AS_DC
OMC
SR3
SRM
Carrier
f1 (PM)
f2 (PM)
f3 (AM)

---
LSC Loop Noise Couplings
UGF DARM: 200Hz, CARM: 10kHz, Others: 50Hz
Feed Forward Gain: 100

---
ASC
WFS+OpLev

---
Total Angular Noise Couplings to DARM

---
Green Lock Setup

---
Arm Cavity Stability after Green Lock
Requirement: 0.3pm RMS

---
Relevant documents
MIF design procedure: JGW-G1100604
LSC design: arXiv:1111.7147
ASC: JGW-G1100608, JGW-G1100533
g-factor selection: JGW-G1200789, JGW-T1200787, JGW-G1200808
Input Mode Matching: JGW-G1200763
Parametric Instability: JGW-T1200787
Recycling Cavity Adjustment: JGW-T1100512
Wedge Angle Error Tolerance: JGW-T1100489
Green Lock: JGW-T1200788

---
Schedule & Installation Scenario

---
Prototype Test
ISC simulation using virtual interferometer on RTS
Green injection table will be tested beforehand
(Kashiwa ? NAOJ ?)
Quality Assurance
Commissioning is QA for MIF

---
Risk Management
Risk factors
Arm cavity loss is too large: PRC under-coupled
=> Prepare a spare PRM with lower reflectivity
Arm cavity reflectivities are so matched that the homodyne phase
cannot be set to around 45°
=> Forget about BAE
Mirror quality is poor
=> ....
Commissioning takes too long (very likely to happen)
=> Work even harder folks !
Lack of man power
 => Get money to hire people

---
Appendix

---
ITMにWedgeが付いているので
斜めから入射する
ITM
(bLCGT)
腕共振器光軸
From BS
From BS

---
そのまま26.6m先にITMを動かすと、中心にビームが当たらない
ITM
(iLCGT)
ITM
(bLCGT)
From BS
26.6m

---
調整方法1
BS, PR3を動かす
最大移動量2cm
SRCも調整
ITM
(iLCGT)
ITM
(bLCGT)
PR3とBSの位置と向きを調節
入射ビームの位置と角度を変える
From BS
Wedge角も変える

---
調整方法2
ITMを横に動かす
他のミラーには触れない
GVの窓を通らない
GV
ITM
(iLCGT)
ITM
(bLCGT)
From BS
窓板
Φ10cm
7cm