## Slide 1: External forces from heat links in cryogenic suspensions
D1, ICRR, Univ. Tokyo
Takanori Sekiguchi
GWADW in Hawaii

## Slide 2: About this Talk
Estimate seismic noise introduced from heat links.
Discuss how to achieve cooling and seismic isolation at the same time.

## Slide 3: Seismic Noise from Heat Links

## Slide 4: Basic Requirement for KAGRA Test Mass Suspension
Attenuate seismic noise
Cool down test masses
Test Mass Displacement
< 3 x 10-20 m/√Hz @ 10 Hz
Mirror Temp. ~ 20 K

## Slide 5: Seismic Attenuation System for KAGRA Test Mass
~14 m
Seismic vibration transmits to the mirror in two different paths
From the top through the attenuation chain
From the wall of the cryostat through heat links
①
②

## Slide 6: Cryogenics
Heat transferred via pure aluminum heat links.
We need Φ1 mm, L=1 m heat links x 7~8
Thermal simulation Done by Y. Sakakibara
(Φ1.6 mm, L=30cm)

## Slide 7: Mechanical Property of Heat Links
A heat link works as a soft spring (f0~10 mHz) with violin modes above ~1 Hz
FEM Simulation Done by Y. Aso, (JGW-G1000108)

## Slide 8: Estimation of Seismic Noise via Heat Links
Simulation Tool: 3-D rigid-body model simulation
T. Sekiguchi, Master Thesis (JGW-P1200770)

## Slide 9: Calculation Result
①
②
Polluting detector sensitivity above 10 Hz !!
* Assuming 1% coupling
from vertical

## Slide 10: To Make Matters Worse ..
There is no guarantee that the wall inside the cryostat is vibrating at the same level as the ground.
???

## Slide 11: Vibration Inside the Cryostat in CLIO
10-100 times larger !!
K. Yamamoto et al, J. Phys.: Conf. Ser. 32 418 (2006)

## Slide 12: In Worse Case
①
②
* Assuming 1% coupling
from vertical
If the attachment point of heat links is vibrating at the same level as cryostat vibration in CLIO..

## Slide 13: Improved Design
Add one more “cushion” between the cryostat and mirror

## Slide 14: Consideration on Cooling
These two masses are thermally well connected by heat links*
* Pure aluminum Φ 3 mm, L=63 cm, Number: 5
(Φ1.6 mm, L=30cm)

## Slide 15: After Improving Wiring

## Slide 16: After Improving Wiring
Several peaks exceed the target sensitivity, but the flour level is OK.

## Slide 17: Possible Ideas of Further Improvement
Suppress the cryostat vibration passively/actively.
Put additional filters between suspension and cryostat.
Add vertical springs for test mass suspension.

## Slide 18: Another Consideration

## Slide 19: Effect on Angular Motion
SAS is very soft in yaw motion (~ 10 mHz).
Low frequency yaw motion can be easily excited.
Single wire suspension

## Slide 20: Effect on Angular Motion
If one employs asymmetric wiring of heat links..
RMS: 2 μrad
Microseismic peak
Yaw resonance
* Eddy current damping for yaw modes is applied
T. Sekiguchi, Master Thesis (JGW-P1200770)

## Slide 21: Symmetric Configuration
Symmetric wiring does not subject any torque.
If you admit 10% thickness difference in two connections  Blue Curve
Φ1.1 mm
Φ1.０ mm
RMS: 0.5 μrad
Not small, but in a controllable level

## Slide 22: Summary

## Slide 23: Summary
Careful wiring of heat links is required, in order to mitigate the seismic noise introduced from them.
Further isolation, or improvement of the suspension design may be necessary.
Yaw excitation by heat links would be not so huge (be in a controllable level).

## Slide 24: Future Works
Transfer function measurement of heat links. (How to ??)
Vibration measurement inside the cryostat.
  L. Naticchioni and D. Chen will start this autumn

## Slide 25
The END

## Slide 27: Appendices

## Slide 28: Requirement for KAGRA Test-Mass Suspensions (1)
Seismic noise should be much lower (at least 10 times smaller) than other noises at the detector observation band (> 10 Hz).
KAGRA Design Sensitivity
Seismic Noise Requirement:
< 3 x 10-20 m/√Hz @ 10 Hz
And rolls off steeper than f-3

## Slide 29: Requirement for KAGRA Test-Mass Suspensions (2)
Mirror temperature should be as low as 20 K to suppress thermal noise.
Substrate thermoelastic noise (∝T2.5) gets lower than coating Brownian noise(∝T0.5) at < 23 K

## Slide 30: Seismic Attenuation System (SAS) for KAGRA
7-stage pendulum + 5-stages vertical spring
~13 m
(horizontal attenuation)
(vertical attenuation)
Last 3 stages are cooled at cryogenic temperature (<20 K) to suppress thermal noise
Cryostat
* Beam splitter and other optics are suspended by smaller vibration isolation systems
Mirror (Test Mass)
Metal cantilever springs
Geometric Anti-Spring (GAS) Filter
f0 ~ 0.3 Hz

## Slide 31: Vibration Isolation System Disposition
Expected Performance

## Slide 32: SAS Status
Prototype Experiment:
Standard filter (GASF): Performance was measured @NIKHEF
Pre-isolator (IP&GASF): Now Measuring @ Kashiwa
Design:
Type-B Payload: Now Designing
Measured
Transfer Function
(Feb. 16th, 2011)

## Slide 33: Cryogenics

## Slide 34: Initial Cooling Time
Thermal simulation with Y. Sakakibara’s Method
* The inner shield and the masses except for the test mass are DLC-coated (ε=0.41).
** Radiation cooling is dominant before 15th day.

## Slide 35: Initial Cooling Time Calculation Diagram
By Y. Sakakibara

## Slide 36: Heat Load
Absorption in mirror
  Coating: 0.4 W (1ppm)
  Substrate: 0.6 W (50 ppm/cm)
  Total: 1.0 W
Inner shield
  Radiation from 80 K: 1.3 W
  Conductance: 0.8 W
  Scattered Light: 5 W (10 ppm)
  Total: 7.1 W

## Slide 37: Heat Extraction Scheme
In the new heat extraction scheme, mirror temperature would not be raised, even if large scattered light attacks the shield.

## Slide 38: Thermal Conductivity of High Pure Aluminum
40,000 W/m/K @ 6K
6N Aluminum
2N Aluminum
~Type A-1070
For inner shield
For outer shield
5N up Al
RRR=3000

## Slide 39: Heat Link TF Calculation
Pure aluminum (E=68 GPa), Φ1 mm
Half-ellipsoid (a=400 mm, b=200 mm)
Loss angle: 10-4
FEM Simulation Done by Y. Aso, (JGW-G1000108)

## Slide 40: Heat Link Transfer Functions

## Slide 41: Heat Link TFs

## Slide 42: Seismic Noise via Heat Links
Couplings from the vertical motion is dominant above 3 Hz.
* Assuming 1% coupling
from vertical

## Slide 43: Heat Links with Half Diameters
How about decreasing the fiber thickness, from Φ1.0 mm to Φ0.5 mm ?
Heat conductivity per link: x 1/4
Necessary number of links: x 4
Spring constant per link: x 1/16
Total stiffness: 1/4
Heat link total mass: Same

## Slide 44: Hot Platform Design
Push heavy Platform to the room temperature part.
Decrease the initial cooling time.
Another vibration shortcut occurs between IM and IRM

## Slide 45: Hot Platform Initial Cooling Time
Current Design
Hot Platform
1 week earlier!!

## Slide 46: Hot Platform Seismic Noise
Due to the vibration shortcut, seismic noise gets larger above 10 Hz in ~1 order of magnitude

## Slide 47: Heat Links with Half Diameters
Only better at 1-3 Hz, not so good above 10 Hz
* Assuming 1% coupling
from vertical

## Slide 48: Torsion Mode Damping
Eddy current damping for yaw modes

## Slide 49: Torsion Mode Damping
Torsion modes of the single wire suspensions would be sufficiently damped by the eddy current damper.
Damping time:
1~2 min.
Mirror yaw angle response to applied torque

## Slide 50: Effect on Angular Motion
RMS: 0.5 μrad