## Slide 1: Cryogenic Suspension for KAGRA and Suspension Thermal Noise Issues
2012/08/21 Thermal Noise Seminar @ Jena
D1, ICRR, U. Tokyo
Takanori Sekiguchi
As a member of vibration isolation system (VIS) subgroup for KAGRA
Notes: I

## Slide 2: Contents
1. Introduction of KAGRA cryogenic suspensions
2. Suspension thermal noise in KAGRA
3. Ideas to reduce suspension thermal noise in KAGRA
4. Summary and discussion
tseki@icrr.u-tokyo.ac.jp

## Slide 3: Contents
1. Introduction of KAGRA cryogenic suspensions
2. Suspension thermal noise in KAGRA
3. Ideas to reduce suspension thermal noise in KAGRA
4. Summary and discussion

## Slide 4: KAGRA Key Features
Cryogenics
Underground
Seismic attenuation system (SAS)
Mirror thermal noise
Expand observation band (~ 10 Hz)
~13 m
Sapphire test mass
23kg, 20K

## Slide 5: KAGRA-SAS Overview
Type-A for test masses
  * SAS technology * Cryogenics
Type-B for recyclers& BS
  * Simpler than Type-A * No cryogenics
Type-C for smaller optics
  * TAMA-stack + simple/double pendulum
Suspension systems for KAGRA core optics

## Slide 6: KAGRA-SAS Key Technologies
Inverted Pendulum stage
GAS filter chain
Control with LVDTs, accelerometers and voice-coil actuators
Developed in TAMA-SAS, HAM-SAS, AEI-SAS, etc.
Cryogenics
Low vibration cryocooler Radiation shields
Still many R&Ds are necessary for this part !!!
Developed in CLIO.
Cryogenic sensors Heat link wiring Sapphire fibers
To be developed

## Slide 7: Cryogenic Suspension for KAGRA
KAGRA Cryogenic Payload Schematic Design
Platform with cryogenic spring (GAS)
Intermediate mass and its recoil mass for alignment control
Sapphire test mass and its recoil mass
Total mass: 300 kg
Preliminary
Sapphire fibers (Φ1.6 mm, L 30 cm)
Aluminum heat links for heat transfer

## Slide 8: Heat Subtraction Scheme
KAGRA Cryogenic Payload Heat Flow

## Slide 9: Cryogenic Suspension Problems [1]
Initial cooling time problem
 Slow down commissioning, reduce duty cycle
~ months to reach target temperature
(Discussed by Y. Sakakibara)

## Slide 10: Cryogenic Suspension Problems [2]
Heat link wiring problem
 Spoil the performance of SAS
Aluminum heat links work as soft mechanical springs (~10 mHz)
Cryostat vibration is transmitted to the mirror via heat links

## Slide 11: Cryogenic Suspension Problems [2]
Close to KAGRA sensitivity!!
More details: GWADW2012 presentation, JGW-G1201037
Cryostat vibration can be larger than seismic vibration

## Slide 12: Cryogenic Suspension Problems [3]
Sapphire fiber problem
Many difficulties in engineering!!
Thick and short sapphire fibers (Φ1.6 mm, L 30 cm).
Rough surface decreases thermal conductivity  Need surface polishing
Sapphire bonding may be necessary??

## Slide 13: Cryogenic Suspension Problems [3]
Sapphire fiber problem
 Pollute detector sensitivity!!
Vertical bounce mode and violin mode peaks at ~100 Hz.
(Even with low Q sapphire fibers, suspension thermal noise gets large because of small dilution factor.)

## Slide 14: Summary
We use cryogenic suspension for thermal noise reduction.
Many difficulties have been found.
  Initial cooling time is quite long.
  Heat links introduce non-negligible seismic noise.
  Thick sapphire fibers introduce non-desired peaks around target frequencies.
Still many R&Ds remain!! (but schedule is tight…)

## Slide 15: Contents
1. Introduction of KAGRA cryogenic suspensions
2. Suspension thermal noise in KAGRA
3. Ideas to reduce suspension thermal noise in KAGRA
4. Summary and discussion

## Slide 16: Suspension Thermal Noise
Thermal fluctuation of mirror displacement due to mechanical loss of suspension system.
Power spectrum can be predicted by fluctuation-dissipation theorem
Imaginary part of force – displacement transfer function

## Slide 17: Suspension Thermal Noise
Thermal fluctuation of simple oscillator
Material loss: structural damping model
Pendulum Q is larger than intrinsic material Q (dissipation dilution)

## Slide 18: Dissipation dilution
In pendulum, most potential energy stored as lossless gravitational potential energy
Ue: Potential energy stored in the bending of fibers Ug: Gravitational potential energy (lossless)
1 / Dilution factor

## Slide 19: Dissipation dilution
Dilution factor gets large for thin and long fibers
L: wire length, d: wire diameter
Initial LIGO dilution factor: ~464
KAGRA dilution factor: ~19
However, thick and short fibers are used in KAGRA for thermal conduction.

## Slide 20: Sapphire Fiber Thermal Noise
Sapphire fiber thermal noise estimation (pendulum mode)
LIGO-G040298

## Slide 21: Violin Modes
For high frequency response, violin modes of fiber should be taken into account.
Eq. of motion of fiber
Eq. of motion of suspended mass

## Slide 22: Sapphire Fiber Thermal Noise
Sapphire fiber thermal noise estimation (pendulum mode + violin modes)
LIGO-G040298
220 Hz

## Slide 23: Vertical Thermal Noise
In KAGRA, we have un-avoidable V-H coupling of 1/300.
Contribution of vertical thermal fluctuation is not negligible.
110 Hz

## Slide 24: Contribution of Upper Stage Losses
Generally, thermal noise from upper stage (and recoil mass) loss is cut off at high frequencies.

## Slide 25: Contribution of Upper Stage Losses
In KAGRA, due to large stiffness of sapphire fibers, vertical thermal noise from upper stage (and recoil mass) loss directly transmits to the mirror.

## Slide 26: Suspension Thermal Noise in KAGRA
Thermal noise simulation including upper stages and recoil mass (with intrinsic material Q of ~104)

## Slide 27: Summary
Thick sapphire fibers introduce resonant peaks of vertical & violin modes around 100 Hz.
Thermal noise from upper stages and recoil mass is not negligible even at high frequencies.
Especially, recoil mass can introduce large vertical thermal fluctuation at 20-200 Hz.

## Slide 28: Contents
1. Introduction of KAGRA cryogenic suspensions
2. Suspension thermal noise in KAGRA
3. Ideas to reduce suspension thermal noise in KAGRA
4. Summary and discussion

## Slide 29: To Reduce Suspension Thermal Noise
Vertical thermal noise
  Reduce V-H coupling (1/300)
  Reduce vertical bounce mode frequency (~100 Hz)
Horizontal thermal noise
  Increase dilution factor (~19)
  Push violin modes to higher frequencies (~200 Hz)
Loss at recoil mass
  Improve recoil mass suspension (Q~104)
  Remove recoil mass

## Slide 30: New Suspension Design
A fresh approach to the design of low thermal noise cryogenic suspension for KAGRA (and ET)
Design development is conducted by R. DeSalvo

## Slide 31: Vertical Thermal Noise
Vertical stiffness of sapphire fiber introduces:
  An annoying peak around 100 Hz
  Large thermal fluctuation from recoil mass stage
  Practically, we cannot equalize tension of four fibers.

## Slide 32: Cantilever Spring
Hold the mirror from cantilever springs
What material should be used?
  High Q
  Large thermal conductivity
 Candidate: silicon cantilever

## Slide 33: Silicon cantilever blades
Etch the bending area
Leave thick section for clamping and for fiber connection
With 0.15 Gpa only limited flexure possible (~25 Hz)
With >1GPa large deflection

## Slide 34: Larger stresses possible?
MEM sensors operating at 1.4 GPa, ~ 10 times higher limit!
Is etching eliminating surface defect and therefore causing the larger strength?
if YES, large bends possible!
Lower frequency bounce modes

## Slide 35: NIKHEF Test
Produce a number of samples
Test and see

## Slide 36: Silicon Cantilever Solution
Thermal noise estimation with cantilever spring (assuming f0 ~10 Hz, Q~10-7)

## Slide 37: Horizontal Thermal Noise
Small dilution factor due to thickness of fibers.
Can we increase dilution factor without spoiling thermal conductivity?
 Fiber with flexure design
Flexure part
For thermal noise reduction
Thick fiber part
For thermal conductivity

## Slide 38: Why Flexure?
Most bending energy concentrates on the fiber ends
Bending energy can be reduced by using soft fiber in the ends

## Slide 39: Flexure Design
Ultra-Sound Machined structure
Etching of the flexure surface
Expected to increase the break point >1GPa

## Slide 40: Ribbons Key features:
Compression joint attachment
Machined-polished Sapphire ribbons
(from bulk, not grown)
High quality sapphire
High quality surface finish (sub-phonon defect size)
= > High thermal conductivity !

## Slide 41: Sapphire Ribbon + Silicon Flexure
Preliminary result (calculated last night…)
Violin mode frequencies can be pushed to high freq region.
The thermal noise is suppressed at low (< 100 Hz) frequencies.
Flour level around 100 Hz get worse

## Slide 42: Flexure Design Pro & Con
10-50 Hz thermal noise will be improved.
50-200 Hz thermal noise will get worse.
We can push the violin modes to higher frequencies.
Good, but not so effective?
Bad
Good

## Slide 43: Can We Remove Recoil Mass ??
Thermal noise from RM suspension loss is quite large.
Can we remove recoil mass??
In Virgo, the actuators on TM are not used during operation!! (thanks to large seismic attenuation)

## Slide 44: No Suspended Recoil Mass
No suspended recoil mass for TM
Actuators only used for damping
Coil should be opened during operation

## Slide 45: No Recoil Mass Case
No peaks at 10-100 Hz!!
Alternative: also employ springs for RM

## Slide 46: Summary
Using low-loss cantilevers, vertical thermal noise is dramatically reduced and annoying peak disappears.
Fibers with flexure design has both profit and demerit.
Removing RM, or employing cantilever for RM?

## Slide 47: Contents
1. Introduction of KAGRA cryogenic suspensions
2. Suspension thermal noise in KAGRA
3. Ideas to reduce suspension thermal noise in KAGRA
4. Discussion

## Slide 48: Discussion

## Slide 49: The END

## Slide 50: Appendices

## Slide 51: Flexure Design
Ultra-Sound Machined structure
Etching of the flexure surface
Expected to increase the break point >1GPa

## Slide 52: Ribbons Key features:
Compression joint attachment
Machined-polished Sapphire ribbons
(from bulk, not grown)
High quality sapphire
High quality surface finish (sub-phonon defect size)
= > High thermal conductivity !

## Slide 53: Why Gallium
Indium proved extremely effective to eliminate friction noise in compression joints (Vladimir Braginsky)
Melts at relatively high temperature
May need heating mirror to more than 160oC for disassembly

## Slide 54: Indium vs. Gallium

## Slide 55: Violin mode elimination
Fiber-fed
Red-shifted
Fabry-Perot
Can cool
violin modes
and bounce modes
to mK level
(Same for Parametric Instabilities ?)

## Slide 56: Conductance budget
Preliminary conductance budget from Sakakibara with 1 W load
Thin ribbon responsible for bulk of loss ! ! !
Plenty of space for parametric optimization

## Slide 57: Chao Shiu laboratory, Taiwan Silicon cantilever with KOH wet etching
4” un-doped double-side polished (001) silicon wafer,
500um thickness etched down to 92 and 52 µm
0.3 10-6 loss measured from residual gas
44.35 mm
10 mm
92 μm or 52 μm
34 mm
0.35mm
500 μm
5.5mm
Frequency=59.04 (Hz)
φmeasurement = 1.4*10-6
Time(sec)
Amplitude
Decay Time = 3940.8 (s)
Silicon cantilever (d=52um)
Amplitude(V)
Original Data
Decay Time = 710.1 (s)
φmeasurement = 4.3*10-6
Frequency = 103.20 (Hz)
Silicon cantilever (d=92um)

## Slide 58: Thermo-elastic limit
@ 59 Hz 0.945 10-6 loss angle predicted (T.E.)
1.3 10-6 measured (-) 0.3 10-6 residual gas
1. 10-6 loss angle measured
=> 100% Thermoelastic limited ! ! !
Frequency=59.04 (Hz)
φmeasurement = 1.4*10-6
Time(sec)
Amplitude
Decay Time = 3940.8 (s)
Silicon cantilever (d=52um)

## Slide 59: Suspension Thermal Noise in KAGRA
Distribution of thermal noise source (H)

## Slide 60: Suspension Thermal Noise in KAGRA
Distribution of thermal noise source (V)

## Slide 61: Mode Shape (Beam Profile)
Pendulum Mode
1st Violin Mode
3rd Violin Mode
2nd Violin Mode