Introduction to the KAGRA Interferometer
Yoichi Aso
University of Tokyo
Japan-Korea Workshop, May 28 2012@ICRR

---
KAGRA Interferometer
ETMY
ITMY
PRM
PR2
Laser
ITMX
ETMX
BS
PR3
SR2
SR3
SRM
Variable RSE, P = 50W, L = 3km
PRG = 10, Arm Finesse = 1500

---
Principle of the gravitational wave detection
Michelson Interferometer
Gravitational Wave
M2
Mirror: Pendulum
M1
Laser
Differential arm length change
→ Intensity variation on the PD
PD

---
Insensitive to the laser frequency noise
M2
M1
Laser
PD

---
Photon Counting Noise = Shot Noise
Photo Detector
size 40 {%delta n = sqrt{n}}
size 36 {"SNR" = sqrt{P_{"in"}} over P_{"in"} = 1 over sqrt{P_"in"}}

---
Where is the best operation point ?
Power on the PD
Dark Fringe
Shot Noise of the Michelson Interferometer
Our Target < 10-23
(Bandwidth 1Hz)
size 26 {h_{nitalic min} approx 2 times 10^{-21}}
Totally insufficient.
What can we do ?
Laser Power = 100W, L = 3km

---
Fabry-Perot Michelson Interferometer
Additional Mirrors
Bouncing the photons many times.
Increase the interaction with GW.
Laser
PD
Shot Noise
Looks good
What else can we do ?
size 26 {h_{nitalic min} approx 2 times 10^{-24}}
Finesse ~ 1000

---
Power Recycling
One more mirror
Reflect back the wasted power
going to the laser
Laser
PD
Shot Noise
Impressive sensitivity
However . . .
size 26 {h_{nitalic min} approx 6 times 10^{-25}}
10 times power increase

---
Multiple bounces of the photons => Signal cancellation
Michelson
Fabry-Perot-Michelson
Narrower observation band

---
Resonant Sideband Extraction (RSE)
Laser
Yet another mirror
PD

---
Gravitational Wave

---
Gravitational Wave
Phase Modulated Sidebands
(= GW Sidebands)

---
Multiple bounces of the photons => Signal cancellation
Michelson
Fabry-Perot-Michelson
GW sidebands are suppressed

---
Resonant Sideband Extraction (RSE)
Laser
Yet another mirror
PD

---
Resonant Sideband Extraction (RSE)
Signal Recycling Cavity
Laser
Yet another mirror
PD

---
Multiple bounces of the photons => Signal cancellation
Michelson
Fabry-Perot-Michelson
Cut off frequency

---
Resonant Sideband Extraction (RSE)
For GW sidebands,
the effective finesse is lowered
Laser
Yet another mirror
PD

---
Comparison of shot noise shapes
Select optimal configuration for given targets
Broadband RSE
Detuned RSE
Power Recycling Only

---
Comparison of shot noise shapes
Seismic Noise
Radiation Pressure Noise
Various other noises at low frequencies
No advantage for pure power recycling
Broadband RSE
Detuned RSE
Power Recycling Only

---
KAGRA Interferometer
ETMY
ITMY
PRM
PR2
Laser
ITMX
ETMX
PR3
SR2
SR3
SRM
Variable RSE, P = 50W, L = 3km
PRG = 10, Arm Finesse = 1500

---
Target Sensitivity of KAGRA
Detectable range of binary NS coalescences ~ 240Mpc

---
Interferometer Control
5 degrees of freedom: Two Arms, Power Recycling,
Signal Recycling + Michelson Fringe
Optimal operation point: Keep the resonances
PRM
PR2
PR3
SR3
SR2
SRM
ITMY
ETMY
ITMX
ETMX
Laser

---
Extremely High Precision Control
< Pico meters
< 0.1 μrad

---
Signal Extraction Scheme for KAGRA
Three RF Sidebands
ETMY
Resonant in different parts of the interferometer
ITMY
REFL
PRM
PR2
ITMX
ETMX
Resonant Conditions
POP
PR3
SR2
SR3
SRM
AS
Three signal extraction ports: AS, REFL, POP
Carrier
f1 sideband (PM 16.875MHz): PRC-SRC
f2 sideband (PM 45MHz): Only PRC
f3 sideband (AM 56.25MHz): Not resonant at all