## Slide 1: Cryogenic Cavity for Ultra Stable Laser
T. Ushiba, A. Shoda, N. Omae, Y. Aso, S. Otsuka S. Hiramatsu, K. Tsubono, ERATO Collaborations

## Slide 2: Contents
Overview of the cryogenic cavity
Detail and current status
Summary

## Slide 3
Overview of the cryogenic cavity

## Slide 4: What is optical lattice clock?
frequency standard
Cs atom clock → definition of second
a candidate of new frequency standard
１. single ion in ion trap
２. group of atoms in laser cooling
３. optical lattice clock
Notes: 9.2GHz

## Slide 5: Motivation
stability of optical lattice clock
Currently limited by the frequency stability of probe laser
Long integral time
We need a stable laser !
    M. Takamoto, T. Takano, and H. Katori, Nat. Photon., 5, 288 (2011)
Develop an ultra stable prove laser using a highly stable optical cavity
Our target
@ 1s
(fractional stability)
Applications in gravitational wave detectors

## Slide 6: Limit of stability of present lasers
limit of stability of major stable lasers
Limited by thermal noise of optical cavity
K. Numata，A. Kemery and J. Camp Phys. Rev. Lett. 93，250602(2004).
Spectrum of NIST laser’s noise
Our strategy
monocrystaline silicon
Cool down to 18K

## Slide 8: Our enemy
Thermal noise
Thermal vibration of atoms
ULE cavity is limited by this.()
Vibration
Elastic deformation of cavity bodies
Need for vibration insensitive support
Thermal variation
Finite CTE (Coefficient of Thermal Expansion)
Cavity length flactuation
Stable laser stable cavity length
Who are disturbing us ?

## Slide 9: Thermal noise
In general:
Proportional to and
Larger beam spot size is better
Noise sources:
Cavity spacer
Mirror substrate
Mirror coatings
What we have to do
Find a material with good quality factor : silicon
Lower the temperature
Larger beam spot size
Mechanical quality factor
(intrinsic to materials)
Most problematic

## Slide 10: Vibration
Vibration insensitive support
Four point support
Vibration sensitivity:
[1/(m/)]
Active vibration isolation
Hexapod stage
Acceleration noise:
4[(m/)/]

## Slide 11: Temperature Variation
Low CTE materials
Temperature control
Sillicon CTE
Zero-cross around 18K
K. G. Lyon，G. L. Salinger，
C. A. Swenson and G. K. White:
J. Appl. Phys. 48，865(1977).

## Slide 12: Design of cryogenic cavity
Material: monocrystaline silicon
Cavity length: 20cm
Mirror ROC: 3m → beam spot size = 0.5mm
Finesse 100,000 → coating thickness = 8um
Wave length: 1396nm
Cooled down to 18K by cryocooler
Helium liquifaction pulsetubecryocooler for low vibration

## Slide 14: Noise budget
Assumption
Vibration sensitivity = [1/(m/)]
Acceleration noise = 4[(m/)/]
Residual CTE = [1/K]
Temperature fluctuation = 20[nK/]

## Slide 15
Detail and current status

## Slide 16: Silicon Cavity
Machining and polishing
spacer : finished
Mirror substrate : under re-polishing
Optical contact test
Contacted by SIGMA KOKI
Notes: あ

## Slide 17: Cooling test of optical contact
Cooling test in liquid nitrogen
6 time thermal cycling
not broken

## Slide 18: Cryostat
Cryocooler: cryomech
Helium liquifaction
1st stage
2nd stage
(4K)
(60K)
He gas entrance

## Slide 19: Cryostat
Cryocooler
Turbo pump
dry pump
He gas
0.8m
Gate valve
Vacuum test
Turbo pump on
Close gate valve
~10 hour

## Slide 20: Cryostat
Cooling test
thermometer

## Slide 21: Active vibration isolation
Hexapod stage
Cryocooler’s vibration isolation

## Slide 22: Summary
We are making monocrystaline silicon cavity for frequency stable laser.
The idea is cooling the cavity made by a high Q material and isolating vibration in a high level.
The experiment has many troubles but proceeds step by step.