## Slide 1: Simulation for KAGRA cryogenic payload: vibration via heat links and thermal noise
Univ. Tokyo, D1
Takanori Sekiguchi

## Slide 2: Introduction
Ligo Livingston
Designing of the cryogenic suspension system for KAGRA is currently in progress.
Several problems/difficulties have been found for cryogenic suspensions:
  Long initial cooling time (~ months)
  Cryogenic compatible sensors/actuators
  Extra vibrations via heat links
  Suspension thermal noise

## Slide 3: Cryogenic Suspension Base-Line Design
Ligo Livingston
Triple pendulum
Cryogenic Spring (GAS)
Pure aluminum heat links for heat extraction
Test mass suspended by four thick and short sapphire fibers (Φ1.6mm, L = 30 cm)

## Slide 4: Today’s Topic
Ligo Livingston
Vibration transmitted through the heat links
Thermal noise of the cryogenic suspension

## Slide 5: Vibration via Heat Links
Ligo Livingston

## Slide 6: Vibration via Heat Links
Ligo Livingston
Heat is subtracted from the recoil mass of intermediate stage (furthest from TM)
Eight Al wires of Φ1mm x 1 m, with round shape
Vertical vibration is filtered by small springs (~5 Hz) and a GAS spring (~0.5 Hz)

## Slide 7: Vibration via Heat Links
Ligo Livingston
The vibration via heat links seems much below the target sensitivity level.
But...

## Slide 8: Larger Vibration of Cryostat ??
Ligo Livingston
Cryostat in CLIO is vibrating at larger level than ground vibration [K. Yamamoto, 2006].
K. Yamamoto et al, J. Phys.: Conf. Ser. 32 418 (2006)
Assuming larger vibration level of the cryostat, there are only little safety margin.

## Slide 9: For Further Isolation (Suggestion)
Ligo Livingston
Additional filter between IRM and cryostat
K. Yamamoto et al, J. Phys.: Conf. Ser. 32 418 (2006)
Vertical springs for test mass suspensions.

## Slide 10: Other Concerns
Ligo Livingston
Shortcut of the vibration via actuators of intermediate mass  No problem at least for pendulum mode ?? (to be investigated more)

## Slide 11: Summary: Vibration via Heat Links
Ligo Livingston
In the current design, vibration via heat links can pollute the detector sensitivity at ~10 Hz.
Additional filter would be necessary for further isolation.
Vibration of the KAGRA cryostat is to be measured.

## Slide 12: Suspension Thermal Noise
Ligo Livingston

## Slide 13: Suspension Thermal Noise Calculation
Ligo Livingston
Rigid-body models used for seismic noise estimation.
In the model, it is possible to introduce loss of the springs/ wires by adding imaginary parts to their spring constants.
Suspension thermal noise can be calculated by taking imaginary part of the force-displacement transfer function.

## Slide 14: Suspension Thermal Noise Calculation
Ligo Livingston
Assumed Q of suspension materials:
  Sapphire fibers: 5 x 106
  Other suspension: 1 x 104
  GAS Filter: 1 x 103
Pendulum Q gets higher than the intrinsic material Q (dissipation dilution)
Thermal noise of sapphire fiber violin modes is calculated separately and added to the rigid-body model calculation.

## Slide 15: Suspension Thermal Noise in KAGRA
Vertical bounce modes of TM & RM suspension fibers exist at 10-100 Hz.
Thermal noise from upper stages/recoil mass is dominant at < 20 Hz.

## Slide 16: To Improve Thermal Noise
Ligo Livingston
Test mass and recoil mass should be suspended by springs.
  Eliminate annoying peaks from observation band
  Improve the vertical thermal noise around 100 Hz
Silicon springs might be used for large thermal conductivity and high Q.

## Slide 17: To Improve Thermal Noise
Ligo Livingston
Fibers with flexures might be useful to push the violin modes to higher frequency.

## Slide 18: Summary: Suspension Thermal Noise
Ligo Livingston
Thermal noise from recoil mass suspension is dominant at 10-100 Hz, and should be improved.
Vertical bounce modes of the suspension fibers produce annoying peaks. Springs should be introduced.

## Slide 19: Thank you for your attention.
Ligo Livingston
Any questions?