JGW- T1301549-v1	KAGRA	21 February 2013

Top filter pre-isolator tuning/performance evaluation

Takanori Sekiguchi, Paolo Radaelli, Luca Malerbi, Maddalena and Riccardo DeSalvo

Distribution of this document:

Public

This is an internal working note of the

### KAGRA Large-scale Cryogenic Graviationai Wave Telescope Project.

http://gwcenter.icrr.u-tokyo.ac.jp/en//

filter B1-1

working point 23.6 mm frequency 0.176 Hz

working mass 274 kg at 22.4oC

compression	15.77 ± 0.17 mm

filter B1-2

working point 24.6 mm frequency 0.186 Hz

working mass 276 kg at 21oC

compression	15.44 ± 0.07 mm

filter B1-3

working point 25.8 mm frequency 0.117 Hz

working mass 276 kg at 20oC

compression	14.9 ± 0.1 mm

filter B2

working point 18.4 mm frequency 0.138 Hz

working mass 301 kg at 23.5oC

compression	15.46 ± 0.25 mm

filter A1

working point 18.2 mm frequency 0.211 Hz

working mass 210 kg at 20.8oC

compression	16.7 ± 0.4 mm

filter A2

working point 25.1 mm frequency 0.168 Hz

working mass 209 kg at 20.8oC

compression	15.68 ± 0.1 mm