## Slide 1: Development Status of Seismic Attenuation System for KAGRA
U. Tokyo, ICRR
Takanori Sekiguchi

## Slide 2: About SAS
SAS [Seismic Attenuation System]
Seismic isolation starting from ultra low frequency
KAGRA
old

## Slide 3: Key Technology of SAS
Development of low frequency oscillator Natural frequency ~ 100 mHz
Inverted Pendulum [IP]
Geometric Anti-Spring (GAS) Filter

## Slide 4: SAS for Gravitational Wave Detectors
TAMA-SAS (JPN)
EIB-SAS (Virgo)
HAM-SAS (LIGO)
AEI-SAS (GER)
Multi-SAS (Virgo)
2000
2005
2010
KAGRA-SAS (JPN)
Collaboration with other GW project

## Slide 5: Contents
Introduction of KAGRA-SAS
Prototype Experiment
Modeling of SAS

## Slide 6: Contents
Introduction of KAGRA-SAS
Prototype Experiment
Modeling of SAS

## Slide 7: KAGRA-SAS Overview
Type-A
Type-B
Type-C
KAGRA Interferometer

## Slide 8: KAGRA-SAS Overview

## Slide 9: Development Status
Standard filter:
Prototype test at Nikhef (2011. 2.)
Production (19 filters) has been already finished.

## Slide 10: Development Status
Standard filter: test at Nikhef
Production (19 filters) has been finished.

## Slide 11: Development Status
Prototype has just been arrived at NAOJ.
Assembly test and performance test should be done.

## Slide 12: Development Status
Pre-isolator :
Prototype test is undergoing at Kashiwa.
Will be delivered to NAOJ for full system test
(summer, this year)
(Today’s Main Topic)

## Slide 13: Contents
Introduction of KAGRA-SAS
Prototype Experiment
Modeling of SAS

## Slide 14: Pre-Isolator
Pre-isolation of seismic noise (< 1 Hz)
Control the position of whole system
Role of Pre-Isolator

## Slide 15: Pre-Isolator Prototype in Kashiwa
Verify the performance of passive isolation
Test bench for active control by the use of new digital system, new sensors and actuators.
Purpose of this work

## Slide 16: Mechanics
IP Leg
Large GAS Filter (Φ ~1200)
Hydraulic Pistons
LVDT & Voice Coil Actuator
Accelerometer
 Geophone
Stepper Motor with soft spring

## Slide 17: Hydraulic Piston
Inclination of the system can be finely tuned:
(~1.5 μrad/Stroke)

## Slide 18: Sensor & Actuator Unit

## Slide 19: LVDT Driver
LVDT driver designed at Nikhef
Sensitivity is limited by ADC noise
Noise level increases with large DC
~ 3 nm/rtHz

## Slide 20: Inertial Sensor (Seismometer)
Geophone L-4C (Sercel)
Passive sensor (No lock)
 stable operation, easy handling
Preamp designed at Nikhef
Noise measurement 

## Slide 21: Digital System
Digital System & Electric Devices
Standalone digital system [LIGO]
16 kHz sampling
ADC 16 bit (65536)
Range: +/- 20 V (differential)
ADC Noise: 2 μV/rtHz

## Slide 22: Study on GAS Filter

## Slide 23: GAS Filter Tuning
Standard Filter Tuning
310 mm

## Slide 24: Large GAS Filter Tuning
645mm
Encounter run-out instability below ~0.15 Hz

## Slide 25: Large GAS Filter Tuning (2)
Real system (Not prototype)
@G&M, Lucca, Italy

## Slide 26: Q-factor Transition of Anti-Spring System
Q factor of GAS filter decreases as its frequency decreases
Energy loss per one cycle: Constant
Kinetic energy of the oscillator ∝ f2
Q ∝ f2
⇒
Q factor transition of TAMA-IP
(A. Takamori)

## Slide 27: Q-factor Transition of GAS (Previous Result)
Deviation from quadratic curve
Different dissipation process??
Avalanche inside material?
Self-Organized Criticality ?
GAS filter Q measurement
@Caltech
Q ∝ f2

## Slide 28: Q-factor Transition of Large GAS (New)
Deviation from quadratic curve
Different dissipation process??
Avalanche inside material?
Self-Organized Criticality ?
Large GAS Filter @Lucca
Q ∝ f2

## Slide 29: Interpretation of New Result
Thermoelastic loss is dominant.

## Slide 30: Future Works
Study working point, instability and Q in more detail
How can we tune GAS filter to lower frequency without encountering instability??
Measure isolation performance of top Filter (tuning of magic wand)

## Slide 31: Inverted Pendulum Control

## Slide 32: IP Prototype System Overview
X
Y
Yaw
Pendulum

## Slide 33: Tuning of IP
Resonant frequency shift due to gravitational anti-spring
Adding mass on the stage
0.1 Hz achieved

## Slide 34: Top Stage Motion (LVDT Signal)
X Y θ
[μm/rtHz]
X, Y, θ motions are reconstructed from 3 LVDT signals

## Slide 35: Top Stage Motion (LVDT Signal)
Wire torsion
(0.043 Hz)
Pendulum
(0.357 Hz)
IP [X,Y]
(0.133 Hz)
IP [θ]
(0.207 Hz)
Pitch
(0.865 Hz)

## Slide 36: Active Damping
[μm/rtHz]
Damped

## Slide 37: Isolation Performance with Active Damping
Put geophone on the top stage
LVDT control re-inject seismic noise above 0.1 Hz
RMS: 3 μm (20 μm for no control)

## Slide 38: Active Damping with Geophone
Velocity damping by the use of geophone signal [for only X-direction]
Noise level above 0.1 Hz is improved
RMS: 1 μm

## Slide 39: Future Plan
Increase the control gain to further decrease RMS [goal: 0.1 μm/sec for lock acquisition, ~0.1 μm for keeping lock (?)]
Combine geophone and LVDT signal [Crossover: ~0.1 Hz]
For control strategy, we have to learn a lot from Virgo and TAMA.

## Slide 40: Contents
Introduction of KAGRA-SAS
Prototype Experiment
Modeling of SAS

## Slide 41: For Better Modeling of SAS
Point-mass model (Super simple)
3D rigid-body model
(more realistic)
Only 1 dimension
No rotation coupling
No sensor noise estimation
…

## Slide 42: Output from Rigid-Body Model
Eigen mode calculation with 3D graphics

## Slide 43: Output from Rigid-Body Model
Attachment point of heat links, asymmetry in IPs
Asymmetry in wire lenghs, asymmetry in suspension points
Estimate angular fluctuation of the mirror

## Slide 44: For Better User Interface

## Slide 45: Future Works
Include active control in this model
  Strategy for length & angular control
  Control noise estimation (sensor & actuator noise)
  Verified at Pre-isolator Prototype
If you want to be a user, please contact me!!
Interface with MATLAB and other application

## Slide 46: END

## Slide 47: Appendix

## Slide 48: Sensor Noise: LVDT (Coupling from Actuator)
Due to high frequency (>2 kHz) noise from ADC, noise flour increases （Improved after digital system update）

## Slide 49: Sensor Noise: Geophone
Preamp designed at Nikhef
Noise of preamp is measured
Geophone + Preamp の雑音測定： バックグラウンドが大きすぎて難しい ⇒ 神岡鉱山での測定を予定

## Slide 50: Sensor Noise: Estimation

## Slide 51: Transfer Function of Inverted Pendulum
< 0.1 Hz：Sensor Noise
> 10 Hz ：Acoustic (Environmental) Noise

## Slide 52: Mechanics
LVDT
Coil-Magnet Actuator
Maraging Steel Spring
Stepper Motor

## Slide 53: KAGRA-SAS Overview
Type-A
Type-B
Type-C
Type-A 7-stage pendulum, 5-stage vertical spring, cryogenic system
Type-B 5-stage pendulum, 3-stage vertical spring
Type-C TAMA-Stack + double pendulum

## Slide 54: Simple Modeling
Simplified point-mass model
Meet the requirement!!

## Slide 55: LVDT v.s. Geophone
<0.1 Hz poor sensitivity of geophone
>10 Hz poor sensitivity of LVDT

## Slide 56: Active Control Demonstration
Displacement [μm]
Damping ON
DC Control ON
Xに500 μmのオフセット
ダンピングにより共振周波数での揺れを抑えることに成功
ステージのDC位置を制御することに成功

## Slide 57: Response to Virtual X Actuation

## Slide 58: Response to Virtual Y Actuation

## Slide 59: Response to Virtual θ Actuation

## Slide 60: What is Missing in the Model?
Coupling between translational and rotational DoFs
Detailed active control system and noise from it
Mechanical response of heat links (for heat paths)
Elastic mode of the wires, springs and bodies
Drift due to temperature change