Main Interferometer Subsystem
KAGRA F2F on 2016/2/22
Y. Aso (NAOJ)

---
iKAGRA configuration
ETMY
IMMT2
PR2
IFI
IMMT1
ETMX
PR3
PR3
BS
(CA74mm)
Φ100mm

---
Beam Splitter from CLIO

---
TAMA Suspension
    + TAMA PRM as ETMs
ROC = 9km
High Gain (R=85%)
Low Gain (R=48%)
Michelson Contrast = 0.96

---
Fixed PR2
Use a fixed 2-inch mirror
A specially made mirror by SIGMA Koki
ROC = -3.0m +/- 20cm
ROC error can be compensated with mirror position

---
Beam diameters (1σ)
Φ50.8mm
PR2
IMMT2
1.9mm
2.6mm
IFI
72mm
72mm
4.3mm
76mm
IMMT1
76mm
ETM
5.2mm
PR3
PR3
BS
(CA74mm)
Φ100mm
Φ250mm

---
Preparation status for iKAGRA
Electronics production -> done
Electronics installation -> on going
Realtime model for digital control -> exist (need to test)
Initial alignment work -> Michimura-kun's talk
Two major challenges
Collimation
Put the beam through 3km
The alignment work will start from 3/4 ?

---
Towards bKAGRA
Design of the MIF part is finished
ITM AR polish to compensate for the inhomogeneity
of the substrate
AS port optics (OFI, OMMT, OMC)