## Slide 1: KAGRA Status
The 1st International Meeting on KAGRA @ KISTI
Takayuki TOMARU
High Energy Accelerator Research Organization (KEK)

## Slide 2
aLIGO (Livingston), 4km
aLIGO (Hanford), 4km
KAGRA (Kamioka), 3km
aVIRGO (Pisa), 3km
LIGO India
Our Galaxy
Magellan
Andromeda
Virgo Cluster Hercules Cluster
200Mpc
GEO-HF (Hanover), 600m
2nd Generation GW Observation Network

## Slide 3
Why do we need a GW telescope in Asia?
 | Sensitivity in whole Sky-Average | Rate of Duty Time | Exposure Ave. Sens. x Duty time
Only one | 0.45 | - | -
H+L+V | 1.3 | 51% | 0.67
H+L+V+K | 2.0 | 82% | 1.4
x 2!
B. F. Schutz
N. Kanda
Sky Coverage and Duty Time
When maximum sensitivity of a telescope with best observation angle defines as 1.0
H + L + V
H + L + V + K

## Slide 4
Sensitivities of 2nd & 3rd Generation GW Telescopes
Comparable
sensitivities

## Slide 5: Noise Budget of KAGRA
h ~ factor x 10-24 [/√Hz] for observation band
Frequency [Hz]
Strain Sensitivity [1/rHz]
Photon Shot Noise
Radiation Pressure Noise
Broadband RSE operation
Detuned RSE operation
Suspension thermal noise
Seismic noise
Mirror thermal noise
+ coating thermal noise
Cryogenic
Underground

## Slide 6
Features in
KAGRA
Underground
Cryogenic Mirror System

## Slide 8: KAGRA Location
3km
3km
KAGRA
Mozumi Entrance
Shin-atotsu Entrance
◎Tokyo
Kamioka◎
Toyama airport
50min.
by car
Mt. Ikenoyama
Super-
Kamiokande
Kamland
CLIO
1000m underground
XMASS

## Slide 9
9
Tunnel excavation was
done at Mar. 2014
7km tunnel in total

## Slide 10
Cryostat Installation
<- First device installation
Search KAGRA on YouTube
Aug. 14, 2014

## Slide 11
Cryostat Assembly
Assemblies of all of main cryostats
has been done.
4.3m
2.6m

## Slide 12
Vacuum Tubes and Tanks Installation
Most of vacuum tubes and tanks has been
installed, and the installation will be
completed in this year.
We also confirmed no vacuum leakage;
< 1x10-10 [Pa m3/sec]
Mode cleaner and BS tanks
Beam tubes: φ800mm x12m x 478
Cryostat
Cryogenic Duct
Beam Duct

## Slide 13
Installation of Input Optics & Vibration Isolators
Laser bench
1st mirror (for mode cleaner) was installed
in Oct. 2015.
Details: Nakano and Takahashi
GAS filters

## Slide 14
iKAGRA operation
First critical milestone

## Slide 15
Test observation by Fabry-Perot Michelson
interferometer at room temperature
Test operation by simple Michelson
interferometer at room temperature
Even if interferometer configuration is very simple, we can check
• Laser transmission through 3km beam ducts.
• Installation procedures
• Facility Issues
• Control electronics
• Data storage and transfer
• etc…
Hard Landing of iKAGRA

## Slide 16: iKAGRA commissioning milestones
IO
MC
ETM
Y-arm
X-arm
ETM
BS
EXC
PR
EYC
SR
Jun. 9: PSL beam quality check
160621_SAITO
Oct. 11: MC mirror
was suspended
Nov. 11: IFI installed
Dec. 11: MC was ready
Type-B
Type-Bp
Feb. 25: PR3 was suspended.
Feb. 25: PR2 was installed.
Feb. 19: ETMX & ETMY were suspended.
(TAMA mirrors & suspensions)
Feb. 8: BS was suspended.
(CLIO BS)
Mar. 3 – 24: Interferometer commissioning
Mar. 18 : Michelson was locked.

## Slide 17
iKAGRA 1st run: Mar. 25 - 31, 2016
iKAGRA 2nd run: Apr. 11 - 25, 2016
Mar. 25: iKAGRA operation was started.
Typical Sensitivity
Duty Factor
1st run: 85.2%
2nd run: 90.4%
Injection test -> Yokozawa
Detector Characterization -> Hayama

## Slide 18
* Assembling mirror and suspension took longer time than expected.
  Full fit-check was only done during assembling.
  Re-designing/re-making of components were necessary during assembling.
  Small components, jigs and tools were insufficiently prepared, in advance.
  Installation manual was not fully prepared before working.
* Performance of the suspension system were not fully reviewed/examined.
  Although a prototype of VIS Type-B was tested, it was done in Summer of 2015. There was not enough time to feed-back to the on-site machine.
  Matching test of control system was done just before operation.
* Cleaning of floors/chambers took longer time than expected.
  Water drop/spring caused delay of starting booth filter operation, and further contaminated floor/chamber/booths.
  Cleanliness-keeping manual for in-booth work was not fully prepared.
* Task sharing was ambiguous during installation and commissioning.
  Cleaning, Chamber closing, Preparation of tools/bolts, Beam handling, , ,
* Manpower was insufficient, especially in the beginning stage.
  Not only for installing work, but also for delivering components, preparing the work-space, operating crane/heavy-machine, , ,
Learning from iKAGRA
Details of iKAGRA will be presented by Kokeyama-san

## Slide 19
Toward bKAGRA
Based on the experience of iKAGRA, we plan to proceed
bKAGRA in 3 steps.
Phase-1 : Operation of a 3km cryogenic Michelson
interferometer (-2018. 3).
Phase-2 : Operation with full configuration:
cryogenic and RSE (2018.4 – 2019 1Q??)
Phase-3 : Commissioning and Observation run
(2019 2Q ??-)

## Slide 21
Upper Floor
Bottom Floor
Arm tunnel
14m
We excavate upper-floors
and vertical holes for
Vibration Isolation System.
Base of the VIS is put
on the upper-floor
Type-A suspension:
4-stage GAS filters
@ room temperature
Cryogenic Payload
Main mirror parts
Frame-Free Suspension
Main Mirror Suspension
Type-A: Takahasi-san’s talk

## Slide 22
Cryogenic Payload
Cryostat
Under developing
in KEK and ICRR
Platform
Marionette &
Recoil mass
Intermediate mass
& recoil mass
Mirror &
Recoil mass
Prototype Cryo-Payload
Type-A
Cryogenics Talks
-> Kumar, Miyamoto,
Ushiba and Craig

## Slide 23
We have already rushed toward bKAGRA
X-end cryostat assembly (done at last week)
Inverted pendulum for Type-A suspension
Vacuum chamber
for Type-A

## Slide 26
Summary
• KAGRA is a new 2nd generation GW interferometer under
construction in Japan.
• Cryogenic mirror system and underground site is the most
advanced features in KAGRA.
• iKAGRA test operation was done in Apr. 2016.
We learned a lot of issues from this experience toward
bKAGRA.
• bKAGRA will be proceed in 3 steps. First phase will be
cryogenic Michelson and first run must be done by Mar. 2018.
• bKAGRA phase-2 will be full configuration and will start
around 2019.
• We will be a part of global GW observation network around then
and will lead new age of GW physics and astronomy together.