A photo sensor to monitor the motion of the recoil mass
during the suspension assembly
Since we do not have OSEM sensors on the mirrors, we do
not have any local sensor for the last stage until the suspension
system is installed into the chamber, where the length sensing OpLev can be used.
This document describe a photo sensor to monitor the recoil mass motion during the assembly work so that we can measure transfer functions to the last stage of the suspension to confirm nothing is touching
2016/11/16 Y. Aso
JGW-D1605845

---
Mechanical Design

---
Overview of the system
photo sensor
XYZ stage
clamp
fixed to the
base plate

---
Purple colored parts need to be manufactured
Everything else are off-the-shelf opto-mechanical parts

---
Installation Procedure 1
Retract the arm
move the stage
back

---
Installation Procedure 2
Move the stopper ring

---
Installation Procedure 3
Move the arm forward

---
Installation Procedure 4
Repeat the step 2 and 3 many times until the photo sensor head gets roughly 1cm from the recoil mass

---
Installation Procedure 5
Use the micro-meter to put the sensor head very close to the recoil mass surface

---
Off the shelf components
XYZ stage
駿河精機 B76-60C
Photo sensor clamp
Thorlabs CH1A
Other components from SIGMA Koki
PO-20-100
PO-12-100
CCHN-12-12 x 2
CCHN-20-12
RO-12-150 x 2
TR-12
TR-20
SP-109-1

---
Circuit Design

---
Original Photo Sensor Driving Topology

---
We need to make an interface box for KAGRA
Analog Out
(BNC)
To ADC
(DB9)
+/-18V
3pin DSUB
To PS (DB9)
signal
18V->5V
+5V/GND