## Slide 1: Status of PLL system of ALS
Shogo Kambara, Yoshiki Moriwaki, Kazuya Yokogawa, Satoshi Yoshioka, Tatsunari Sawada, Shuhei Miyata
University of Toyama
f2f meeting@ University of Toyama

## Slide 2: Contents
ALS
PLL system
Fiber noise
Experiment of PLL system

## Slide 3: Arm Length Stabilization (ALS)
PDH
40Mhz
AOM
EOM
PLL
Laser 1
PR2
PR3
BS
Optical fiber
X-Armcavity
PD
PD
SHG
Laser 2

## Slide 4: PLL system
40MHz
PLL
Main Laser
Green Laser
PD
Synthesizer
Single-mode fiber
Beatnote
To Michelson
To Arm cavity
PZT

## Slide 5: PLL system
40MHz
PLL
Main Laser
Green Laser
PD
Synthesizer
Single-mode fiber
Beatnote
To Michelson
To Arm cavity
PZT
Using a optical fiber for beatnote
Easy aligment
To save space of PSL table

## Slide 6: PLL system
40MHz
PLL
Main Laser
Green Laser
PD
Synthesizer
Single-mode fiber
Beatnote
To Michelson
To Arm cavity
PZT
Using a optical fiber for beatnote
Easy aligment
To save space of PSL table
Problem
Noisy

## Slide 7: PLL system
40MHz
PLL
Main Laser
Green Laser
PD
Synthesizer
Single-mode fiber
Beatnote
To Michelson
To Arm cavity
PZT
Single-mode fiber
Using a optical fiber for beatnote
Easy aligment
To free up space of PSL table
Problem
Noisy
Check the fiber noise

## Slide 8: Measurement of fiber noise
I measured power of beam for 10 minutes

## Slide 9
Notes: Transmittance

## Slide 10: Summary
When optical fiber is shaked, the poralization of beam is rotating
Future work
I will use POLARIZED WAVE HOLDING OPTICAL FIBER which is more stable.

## Slide 11: Experiment of PLL system
Beatnote
Frequency divider
Beatnote is locked at 129MHz

## Slide 12: Result
Lock!
180s
Unlock
Unlock
10MHz
Feedback signal to PZT (1MHz/V)
FWHM:100Hz
128.998680MHz
Beatnote

## Slide 13: Summary
We maintain frequency locking for 3 minutes.
Line width is about 100Hz.
The position of peak is shifted 1.3kHz from 129Mhz
What are these sideband？
Future work
I will upgrade the filter circuit of PLL for long time locking.
I will calculate the requirement of PLL system
Notes: upgrade