## Slide 1
Development of frequency dependent squeezing for future upgrades of KAGRA
K. Arai, Y. Aso, M. Barsuglia, E. Capocasa, M. Eisenmann, R. Flaminio, Y. Guo, M. Leonardi, M. Marchiò, L. Pinard, P. Prat, R. Schnabel,
K. Somiya, M. Tacca, R. Takahashi, D. Tatsumi
KAGRA F2F Toyama - 2017 August 30th

## Slide 2: Motivations
Second generation gravitational-wave interferometers sensitivity limited by quantum noise over a large fraction of the frequency bandwidth (KAGRA even more than Virgo and LIGO due to cryogenic operations).
aLIGO
AdV
KAGRA

## Slide 3: Context
Operation with squeezed light demonstrated with GEO [1] and LIGO [2].
BUT squeezed light increases radiation pressure at low frequencies.
[1] H. Grote et al., Phys. Rev. Lett. 110, 2013 - [2] LSC, Nature Photonics 7, 2013 - [3] S. Chelkowsky et al., Phys. Rev. A 71, 2005 [4] E. Oelker et al., Phys. Rev. Lett. 116, 2016
Need for frequency dependent squeezing (now included in the upgrade plans for Advanced LIGO and Advanced Virgo)
- Frequency dependent squeezing demonstrated first in the MHz region [3] and recently in the kHz bandwidth [4]

## Slide 4: Filter Cavity Optical Design
[5] E. Capocasa et al., Phys. Rev. D 93, 2016 - [6] P. Kwee et al., Phys. Rev. D 90, 2014
Squeezing ellipse rotation at a frequency of 70 Hz [5]
9 dB vacuum squeezed source
300 m length
Study of the mirrors flatness requirements: target 80 ppm of round trip losses (losses less important for longer cavities)

## Slide 5: Filter Cavity Optical Design
[5] E. Capocasa et al., Phys. Rev. D 93, 2016 - [6] P. Kwee et al., Phys. Rev. D 90, 2014
Squeezing ellipse rotation at a frequency of 70 Hz [5]
9 dB vacuum squeezed source
300 m length
Study of the mirrors flatness requirements: target 80 ppm of round trip losses (losses less important for longer cavities)
5.7 ppm
80 ppm
41 ppm
diameter[m]
RMS
[nm]
RMS
[nm]
RMS
[nm]
0.05 | 1.23 | 1.36 | 0.27
0.01 | 0.81 | 0.53 | 0.18
diameter[m]
Squeezing degradation budget [6]

## Slide 6: Impact on the KAGRA Sensitivity

## Slide 7: Frequency dependent squeezing @ NAOJ
300 m Filter Cavity
Faraday Isolator, Mode-Matching & Folding Mirrors
Vacuum Squeezed Source
- TAMA infrastructure unused after the big earthquake
- 300 m cavity length
- Interest in the NAOJ group
- Project approved in April 2015
- Use as much as possible of the TAMA infrastructure and equipment

## Slide 8: Vacuum Squeezed Source Layout
- Based on GEO and Advanced Virgo design
- Green beam from the SHG used to pump the OPO and to control the filter cavity

## Slide 9: Vacuum Squeezed Source Layout
- Second Harmonic Generator (SHG) installed
- Optical components (mirrors, lenses, EOM, AOM, Faraday Isolator) of the beam path towards mode-matching telescope and the cavity installed
SHG
Green FI
Filter Cavity FI
Filter Cavity AOM

## Slide 10: Vacuum Squeezed Source Layout
Green Mode Cleaner assembled and characterised:
first rough estimation of the finesse
design of the telescope for the matching in progress
theoretical = 313-522
measured = 316
Finesse

## Slide 11: Vacuum Squeezed Source Layout
Infrared path:
lasers purchased
mode cleaner ready to be assembled and installed
OPO cavity mechanical components in production
PLL and Homodyne detector development and assembly to be done

## Slide 12: Faraday Isolator & Mode-Matching Telescope
Faraday Isolator from TAMA
Green and IR beams recombination

## Slide 13: Faraday Isolator & Mode-Matching Telescope
@ 300 m

## Slide 14: Filter Cavity Mirrors
Diameter = 10 cm
Thickness = 6 cm
Beam Radius ~ 1 cm
Dichroic coating: green for control and IR
IR Finesse = 4500
Green Finesse = 270

## Slide 15: Filter Cavity
- Input and end mirrors suspended with double pendulum suspensions
- Virgo-like suspensions local control system installed
- Auxiliary optics installed
Cavity End Mirror
Suspension Control System
End Station Auxiliary Optics

## Slide 16: Filter Cavity
Vacuum in the cavity
Cavity controlled (aligned and locked) with the green beam
IR flashes superposed with the green ones
Cavity Transmitted Power
PDH
Cavity locking in green
IR flashes superposed with green

## Slide 17: Filter Cavity
Cavity Open Loop Transfer Function
UGF = 10 kHz
Phase Margin ~ 40 deg
Analog Servo to lock the frequency of the laser to the length of the cavity
Cavity locked using the green beam
Shift the frequency of the green using an AOM to have the green and the IR resonant at the same time in the cavity

## Slide 18: Conclusions
Squeezed source:
  Second Harmonic Generator installed
  Green Mode Cleaner characterized
  Optical components of the beam towards the filter cavity installed
Faraday Isolator and Mode Matching Telescope:
  Mirrors suspended, locally controlled and aligned
  Green and IR beams recombined
Filter Cavity:
  Cavity aligned and locked

## Slide 19: Next Steps
Squeezed source:
  IR mode cleaner ready to be assembled and installed
  OPO mechanical cavity in production
  PLL and Homodyne detector development and assembly to be done
Filter Cavity:
  AOM fine tuning to simultaneously lock the IR and the Green
  Automatic alignment control system
Inject Squeezed Vacuum into the Filter Cavity