## Slide 1: Commissioning in phase 1
Kiwamu izumi
For the commissioning team (it’s you all!)
KAGRA f2f at Osaka city univ. (May 18th 2018)
G1808254-v1

## Slide 2: CONTENTS
Review of the interferometer control
Issues that are identified
Future

## Slide 3: CONFIGURATION
Intentionally
misaligned
3 km
Pilot
mirror
~1 W at IMC input

## Slide 4
Slide by
Y. Enomoto
JGW-G1808217

## Slide 5: NOISE

## Slide 6: NOISE BUDGET
Angular control noise
PD dark noise

## Slide 7: CHACTERISTICS
High visibility (~ 99%, klog 4775)
  ETMs are balanced in their properties i.e., curvature and reflectivities including the BS’s splitting ratio.
ETM position asymmetry not well quantified (klog 4960)
  Measured to be 3.4(5) – 4.5(7) m while design = 3.3 m
  Needs to assess severity from P.O.V. of interferometer control.
F1 modulation depth (klog 4876)

## Slide 8: LENGTH CONTROL
Digital filter
Photo
detector
Farady
Pick-off
UGF ~ 50 Hz.
Feedback to BS TM and IM stages
with xover at ~ 0.1 Hz

## Slide 9: ALIGNMENT CONTROL
-1
-1
Only yaw

## Slide 10: ALIGNMENT CONTROL (contn’d)
Manual fine adjustment ~ every half a day
No global control on ETMY angle
  Optical level local control was good enough
ETMX needed a global control
  Servoing to optical lever had a long term drift issue (~ a day)
  Global control lets ETMX follow ETMY
  Seemingly worked fine

## Slide 11: QUALITATIVE ARG. ON ALIGNMENT
Things became stable once under vacuum.
  Smaller number of manual adjustment for suspension alignment
Several different sensors helped us understanding the alignment condition.
  VIS local sensors, optical levers, Tcams, gigE-cams and baffle PDs.
EXA temporary PD as seen by gigE cam

## Slide 12: HUNTING SOME NOISE
Slide by
Y. Enomoto
JGW-G1808217

## Slide 13: ISSUES THAT ARE IDENTIFIED

## Slide 14: PR3 SLIPPING
See logs 3634 and 3780.
PR3 found to be off in angle in pitch by 10 mrad.
Associated with a power-down of IO chassis.
  Best guess is a jolt onto the mirror bringing the mirror to another stable point.
Temporarily circumvented it by mechanically locking the mirror to its recoil mass.
No indication of another slippage so far.

## Slide 15: PR3 SLIPPING (contn’d)
Similar events was observed with PR2 which remained no issues since Nov. 2017
See also JGW-G1707405 by Shoda-san.
VIS group is incorporating Virgo’s technique to address this issue for SRs.

## Slide 16: DAC GLITCHES
Observed in ETMY, PRs 2 and 3, and BS controllers.
Klog 4254

## Slide 17: DAC GLITCHES (contn’d)
No real solution so far.
Reducing the sampling rate (16 -> 2 kHz) reduced the glitch rate to an OK-level.

## Slide 18: BRIGHT SPOTS
ETMY Tcam image
ETMX Tcam image, klog 4767

## Slide 19: ETMY BAFFLE PDs
Unable to bring the interferometer beam to the upper two PDs.
Needs to assess what went wrong.

## Slide 20: OTHER ISSUES
PR3 optical lever glitches.
Lots of challenges in ETMY local control
Brute-force coherence (BRUCO) not ready in time
How do we spot anomalous suspension drift and glitches?
etc.

## Slide 21: FUTURE

## Slide 22: REMOTE PARTICIPATION
A number of us actually reside afar
  VIS experts at Mitaka, MIF experts at Hongo, Detchar experts all around Asia…
Their remote participation for commissioning activities is a key to increase our productivity
High demand for rapid communication with the crew on site.
Aso-san is addressing the communication part of it by introducing remote participation systems.
  Zoom remote system, TeamSpeak, …
By N.Kijbunchoo

## Slide 23: SUMMARY
Overall, commissioning was successful.
A number of issues are identified.
Remote participation seems another key.