## Slide 1: Future Plans of Ground Based GW projects 地上の将来計画
S.Haino
KAGRA collaboration
CRC town meeting (Dec./21, 2019)

## Slide 2: Typical GW strain amplitude
h ~ I ~ =
e.g. Solar mass (rg~3km) NS-NS binary merging at ~speed of light located at 100 Mpc away h ~ = 10-21
GW signal is very tiny but propagate as 1/R (not 1/R2)
2G
c4R
..
rg
R
Distance to the source
Schwarzschild radius
3 km
100 Mpc

## Slide 3: Sensitivity and events
O2 80~100 Mpc
O3 ~130 Mpc

## Slide 4: Future Prospects (ground based)
Near term (5~10 years) - 2G (2nd Generation) - (Almost) funded in U.S. and Europe - O4 in 2022~ - O5 in 2025~
Far term (10~ years) - 3G (3rd Generation) - New facility and big funding needed - Cosmic Explorer (US) - Einstein Telescope (ET) - Japan ? Discussion in this session - …

## Slide 5: Quick review in GW science
Topic/Source | Ground (2G) | Ground (3G) | Space | Comment
BNS, NSBH | ○ | ◎ | ○ | Science: Test of GR, NS EoS, Multi messenger, sGRB, Standard siren, …
Stellar-mass BBH | ◎ | ◎ | ○ | Science: Test of GR, Formation scenario, … Space: inspiral phase
Intermediate BBH | △ | ◎ | ◎ | Science: Formation scenario, Test of GR, …
Pulsar CW | △(?) | ○(?) | △(?) | Depends on models Science: NS EOS and internal structure
Massive BBH | ✕ | ✕ | ◎ | Science: Formation scenario, Test of GR, …
EMRI Harmonics | ✕ | △ | ◎ | Science: Formation scenario, Test of GR, …
WD, GB | ✕ | ✕ | ◎ | Science: SN astrophysics, Standard siren
Supernovae | ? | ○(?) | △(?) | Depends on model and luck Science: explosion mechanism
Primordial GW | ? | ? | ◎(?) | Depends on models Science: Direct test of inflation
Cosmology | ○ | ◎ | ◎ | Source: BNS/NSBH, BBH, WD, Primordial
Test of GR | ◎ | ◎ | ◎ | Source: BNS/NSBH, BBH, EMRI
BNS: Binary Neutron Star, NSBH: Neutron Star-Black Hole, BBH: Binary Black Hole,
CW: Continuous Wave, EMRI: Extreme mass ratio inspiral, WD: White Dwarf, GB: Galactic Binary
Based on SH’s personal view with help of A.Nishizawa

## Slide 6: LIGO/Virgo O4, O5 projection
[LIGO-P1200087][arXiv:1304.0670]

## Slide 7: LIGO/Virgo O4, O5 projection
Updated on July/11/2019 at LIGO-P1200087 also at arXiv:1304.0670
LIGO O4: 160 – 190 Mpc O5: 330 Mpc
Virgo O4: 90 – 120 Mpc O5: 150-260 Mpc

## Slide 8: O5: A+
L. Cadonati 5th KIW 2019
(Advanced LIGO+ in U.S.)

## Slide 9: O5: AdV+
J. Degallaix GWADW 2019
(Advanced Virgo+ in Italy)

## Slide 10: 3G: Each region’s prospects
Projects being discussed for many years
U.S – CE1 (2030~) /CE2 (2040~)
Europe – ET (2030~)
Projects being proposed recently
Australia – oz-HF (?)
China – ZAIGA (?)

## Slide 11
L. Cadonati 5th KAGRA International Workshop 2019

## Slide 12: Cosmic Explorer (U.S.)
E. Hall DAWN-V (2019)

## Slide 13
Y. Michimura Lab seminor (2017)

## Slide 14: 40 km scale

## Slide 15: Cosmic Explorer (U.S.)
M. Evans GWADW 2019

## Slide 16
M. Punturo KIW5 2019

## Slide 17
M. Punturo KIW5 2019

## Slide 18
Operation planned from 2032
M. Punturo KIW5 2019

## Slide 19: oz-HF (Australia)
arXiv:1912.06305 (2019/12/16)

## Slide 20: ZAIGA-GW (China)
arXiv:1903.09288
Atomic Interferometer
300m vertical Tunnel funded and will be completed in 2020 Operation by 2025 (if fully funded)

## Slide 21: Then, KAGRA (Japan)

## Slide 22: Contributions expected by KAGRA
Detector network duty factor (N>=3) HLV 34% (3/3) → HLVK 65% (3/4) (assuming 70% each)
Sky localization improvement Typically factor of 3 - EM counterpart - Hubble constant
GW polarization measurements - Test of General Relativity including polarization modes
JGW-G1808212
(KAGRA design sensitivity)
H. Takeda+, PRD 98, 022008 (2018)

## Slide 23: Application of Accelerator technologies to KAGRA
KEK cryogenic center is leading the development of KAGRA cryogenic system
J-PARC neutrino
super-conducting beam line
KAGRA cryostat

## Slide 24: Specific issues for cryogenic
Not trivial to do both - high power (400 kW on mirror) - low temperature (20 K)
thinner and longer fibers preferred
for suspension thermal noise reduction
thicker and shorter preferred for efficient heat extraction
Dilemma
heat
extraction
heat absorption
(bulk, surface)
ITM
Laser from BS
Laser in arm cavity

## Slide 25: KAGRA Future Planning
KAGRA has been focusing to finish the installation of current configuration ; discussion on the future upgrade was not so active until 2018
Finally, KAGRA installation was almost completed and Future Planning Committee (FPC) has been established in Dec./2018 and started discussions on the future upgrade

## Slide 26: KAGRA now and future
Even though installation of components is done, we still have many issues [T. Tomaru’s talk]
Birefringence of sapphire bulk is one of the serious issue which prevents us from achieving the design sensitivity even in O4 (2022~)

## Slide 27: Sapphire birefringence issue
Laser
s-pol
a few % p-pol in reflection
Power and signal recycling cavities contaminated by p-pol
K. Somiya, et. al
PRD 100, 082005 (2019)
p-pol beam shape from ITM reflection

## Slide 28: KAGRA near future prospects
O4 limit (~80 Mpc)
Towards O4 (2022~)
Manage with the current (birefringent) sapphire
Most of the time for commissioning/noise hunting
Expected sensitivity up to 80 Mpc
Y. Michimura
JGW-G1911123

## Slide 29: KAGRA near future upgrade
Highest priority task is to develop high spec. sapphire mirrors with negligible birefringence
Then, KAGRA design sensitivity is mostly limited by quantum noise
Frequency dependent squeezing technique is expected to reduce quantum noise in wide frequency range
JGW-T1910879

## Slide 30: KAGRA near future upgrade
Highest priority task is to develop high spec. sapphire mirrors with negligible birefringence
Then, KAGRA design sensitivity is mostly limited by quantum noise
Frequency dependent squeezing technique is expected to reduce quantum noise in wide frequency range
JGW-T1910879

## Slide 31: High spec. sapphire mirror
We have been collaborating with crystal makers in Japan and a research institute in Lyon, France (iLM).
Recently iLM got a new funding focused on the development of high quality and bigger sapphire substrate
Gravitational Astronomy Sapphire Optics (OSAG)
Collaboration

## Slide 32: Freq. dependent squeezing
Active developments in NAOJ and oversea KAGRA institutes (e.g. Taiwan, Korea)

## Slide 33: KAGRA near future projection
O3
O4
O5
8-25 Mpc
25-80 Mpc
80-170 Mpc
arXiv:1304.0670
To be downscaled to ~1Mpc

## Slide 34: KAGRA’s contribution in O4~O5
Sky localization of BNS to be significantly improved
An example of BNS event for which KAGRA can improve the sky localization accuracy

## Slide 35: KAGRA far future upgrade idea
Even though KAGRA is facing a difficult time, once we find the solution of current issues, it is not a dream to consider the far future with ultimate potential of cryogenic sapphire

## Slide 36: Ultimate goal of KAGRA
Assuming 200kg, 10ppm/cm sapphire, 500 W laser and 10dB FD squeezing are available (in 10 years)
Estimated sensitivity as ~500 Mpc [JGW-G1910533]
It will be the most sensitive detector with the conventional (1064nm and existing facility) technology
We need a name; ultimate KAGRA (uKAGRA) ?

## Slide 37: Ultimate goal of KAGRA
Assuming 200kg, 10ppm/cm sapphire, 500 W laser and 10dB FD squeezing are available (in 10 years)
Estimated sensitivity as ~500 Mpc [JGW-G1910533]
It will be the most sensitive detector with the conventional (1064nm and existing facility) technology
We need a name; ultimate KAGRA (uKAGRA) ?

## Slide 38: Technological challenges
Big sapphire mirror with low absorption - Collaboration with iLM - Proposal accepted for 200kg sapphire facility
High power laser - 500W is not a dream in 5~10 years
Suspension and heat extraction
High power tolerance of room temp. optics
…

## Slide 39: uKAGRA example sensitivity curve
BNS range: 505 Mpc

## Slide 40: Comparison with other detectors
u

## Slide 41: Redshift reach VS total mass
30-30 Msun
uKAGRA z~3.9
A+ z~2.5
uKAGRA would be able to reach most of the BBH sources
Horizon
10% detected
50% detected
u

## Slide 42: In case of 100kg/350W
JGW-T1809537

## Slide 43: KAGRA future projection
O3
O4
O5
3G
8-25 Mpc
25-80 Mpc
80-170 Mpc
(?)
300-500 Mpc
uKAGRA can fill the “science gap”
between O5 and 3G
u

## Slide 44: Prospects of GW science
Continuous sensitivity improvements offer us increasing events (3rd power) and science cases - Neutron Star Equation of State (EoS) - Test of General Relativity at extreme conditions
New generation of Multi-messenger science - Short GRB - Precision and independent determination of cosmological constants
Possible detection of new sources - Supernovae (with EM, GW and neutrino) - Massive BBH, …

## Slide 45: Advantage of KAGRA in 3G era
Existing facility - KAGRA observatory should work for >15 years - New and huge facilities needed for 3G (CE, ET) → difficulty and unknown about the fundings
Long experience of cryogenic sapphire - New technology (e.g. cryogenic silicon mirror) is very challenging and uncertain for 3G (CE, ET) → they don’t even know what are the issues

## Slide 46: Concerns on a big facility - ILC
Science Council of Japan, Dec./ 2018
(中略)

## Slide 47: KAGRA future projection
O3
O4
O5
3G
8-25 Mpc
25-80 Mpc
80-170 Mpc
(?)
300-500 Mpc
uKAGRA can fill the “science gap”
between O5 and 3G
u

## Slide 48: Summary
Even though it is a difficult time for KAGRA, the future is still bright - At least we know what are the issues - KAGRA can maximize the advantage of existing underground facility
KAGRA should catch up to LV in ~5 years (~80 Mpc), reach the same sensitivity in ~10 years (~160 Mpc) and aim at the ultimate configuration (~500 Mpc)

## Slide 49: Parameters assumed (dimensions)
Parameter name | bKAGRA | uKAGRA
Mirror size (and mass) | 𝜙22cm ×15 cm (22.8 kg) | 𝜙45cm ×31.5 cm (200 kg)
Sapphire suspension | 𝜙1.6mm ×35cm | 𝜙2.7mm ×50cm
Wire safety factor | 12.58 | 5.0
Intermediate mass | 20.5 kg | 180 kg
Beam size | 3.5 cm | 7.0 cm
Clear aperture (4𝜎) | 14 cm | 28 cm
Coating improvement | None | x2
Squeezer | None | Freq. dependent (10 dB)
Filter cavity | None | 300 m
As an example; further optimization may be needed

## Slide 50: Parameters assumed (power-related)
Parameter name | bKAGRA | uKAGRA
Laser power (before PRM) | 70.1 W | 500 W
Power at BS | 674 W | 4.8 kW
Arm power | 0.32 MW | 2.3 MW
Mirror temperature | 22 K | 18.4 K
Heat to be extracted (ITM) | 0.72 W | 2.76 W
Heat absorption | 50 ppm/cm | 10 ppm/cm
Thermal conductivity coefficient (𝛼0)*1 | 7.98 W/K/m | 16 W/K/m
Thermal conductivity (𝜅)*1 | 7.2 kW/K/m | 19.8 kW/K/m
*1 𝜅 = 𝛼0 d/d0 T𝛽, where d0 is diameter of bKAGRA suspension (1.6mm)
As an example; further optimization may be needed