## Slide 1: The cooling scenario for O4 without frosting on the surface of the KAGRA Test Mass and ….
Nobuhiro KIMURA
Institute for Cosmic Ray Research
The University of Tokyo
On behalf of the cryogenic subgroup of KAGRA
2021 Gravitational Wave Advanced Detector Workshop 20/May/2021

## Slide 2
Outline
  Introduction
    An example of frosting on the surface of view ports
    Cryogenic system for KAGRA
    Issues in de-frosting experiment using KAGRA cryostat
  Results of de-frosting experiment using KAGRA cryostat
    Test mass cooling by the scenario for O4
    Residual gas measurement during the Test Mass cooling
    Performance defrost heaters
  Summaries

## Slide 3: An example of frosting on the surface of view port
TM oplev light source side
TM oplev QPD side
Photos show examples of the frosting on the surface of view ports with vacuum leak at TM temperature of ~25K. (@EXC 2020/08)
It was assumed that frog on the surface was formed by frosting of O2, N2 and H2O.
    Frosting
Frosting on the surface of the test mass and the viewports of
the radiation shields is a serious problem at the KAGRA.
In order to find a way to cool the test mass down to ~20 K while preventing frosting, KAGRA cryogenic subgroup have conducted the cooling experiment using the KAGRA cryostat.
Notes: Frost on the surface of the test mass and the viewports of
the radiation shield is a serious problem at the KAGRA.
In order to find a way to cool the test mass down to ~20 K while preventing frosting, KAGRA cryogenic subgroup have conducted the cooling experiment using the KAGRA cryostat.
In this experiment, we succeeded in preventing frosting on the surface of test mass and the viewports.
The results of the cryostat cooling experiments are reported in this talk.

## Slide 4: Structural view of KAGRA Cryostat with shield ducts
Shield duct
Shield duct
Test mass
Cryo-cooler units
View ports
Outer radiation shield
Inner radiation shield

## Slide 5: Cryo-cooler layout
Four 4K cryocooler units per one cryostat
Main Beam
Inner shield
cooling
Cooling
Cryo-Payload
Shield ducts
400kW
Cryostat
Outer radiation shield
Inner radiation shield
two units
Pulse Tube type Cryo-cooler (PTC) with Vibration reduction
two units
2 units for cool cryo-payload
2 units cool for the inner shield
4 units cool for the outer shield
300K
Radiation
Baffles
Cryo-payload
cooling

## Slide 6
1. Determine the cooling scheme for Test Mass without frosting
Including confirmation of the occurrence of frosting on the view ports under the condition of leak rate <10^-10Pam^-3/s)
2. Defrosting experiment by defrost heaters
Confirmation of defrost heater performances
(If no frost adheres, check the temperature profile of defrost heating.)
3. Measurement of partial pressure of residual gas to confirm frosting components
Issues in de-frosting experiment using KAGRA cryostat
Notes: IYC冷却実験での実証課題
1．冷却スキームの確定
（リーク <10^-9Pam^-3/sで条件で可視化窓の霜付きの発生するかの確認を含む）
真空引き:2 weeks、ダクトシールド冷却： 2 weeks、輻射シールド冷却： 4 weeks、
test mass冷却： 4 weeksぐらい
2．除霜ヒータの性能確認
（霜が付着しなかった場合はヒータ加熱による除霜ヒータ表面の温度プロファイルの確認）
3．テストマスの冷却時間の確定（熱伝導帯固定部の増し締め）山田君
4．テストマスの除霜実験？
（テストマス表面の霜付きをどのようにして測定するか未定）
ヒーターをＩＭに付ける。
5．残留ガスの分圧測定（窒素、水分）霜付きの成分を確認 Q-massをIXCから移設

## Slide 7: Proposed Test mass cooling scenario for O4 - Issure: How maintain mirror temperature lower than 100 K without frosting on the surface of the mirror -
Cooling steps at this experiment;
Step 1:
  Start vacuum pumps and wait inner pressure shall be lower than ~10^-4 Pa.
  It will take 21 days including vacuum leak test for 3 days.
Step 2:
  To trap H2O residual gas on the surface of duct shield, Start duct shield cryocoolers and wait surface temperature of duct shield shall be lower than lower than ~150 K.
  It will take 11 days.
Step 3:
  To trap nitrogen gas on the surface of inner shield, start two shield cryocooler units. The mirror is cooled by only radiation to the inner shield.
  Wait surface temperature of inner shield shall be lower than lower than ~20 K.
  It will take 24 days after switched on the coolers.
Step 4:
  Switched on payload cryo-coolers.
  It will take 10 days after switched on the coolers to reach steady state condition of mirror temperature.

## Slide 8: Temperature distribution and pressure in the KAGRA Cryostat after cooling
Shield duct
= ~125 K
Shield duct
=~ 125 K
Test mass
= 23 K
Outer radiation shield
=~100 K
Inner radiation shield
= ~15 K
Internal pressure = 5.8 x 10^-6 Pa

## Slide 9
Two turbo molecule pumps “ON”
One root pump “ON”
Temperature dependence of internal pressure
> 140 K
Two duct shield cooler “ON”
\
> 30 K
Two cryostat shield cooler “ON”, Tduct=150~200 K, TTM ~ 230 K
Pcryo=
5.8 x 10^-6 Pa
Two payload cooler “ON”, Tinner < 30 K,
TTM > 150 K

## Slide 10
15 < Tinner < 30 K
Touter > 130 K
> 1x10-6 Pa
Trap H2O by duct & outer shields
Trap O2 & N2 by inner shield

## Slide 11: Defrost heater layout
A small heater was attached on IM for defrost of mirror surface.
Two calibration heaters were equipped with
the top of inner radiation shield.
A defrost heater was attached on view port.
Three kinds of heaters for defrosting were installed in KAGRA cryostat.
Image of defrost heater

## Slide 12
Defrost heater
“ON”
Qdh=~5 W
Characteristics of heat input response
IM heater “ON”, QIM=2.5 W
~two days
TTM=~75 K
Inner top cal heater “ON”, QTh=~31 W
Inner Top cal heater “OFF”
~two days
Tinner shield=~45 K

## Slide 13
Temperature dependence of Q-mass

## Slide 14
H2O
N2
Temperature dependence of Q-mass

## Slide 15: Summaries
Frost on the surface of view ports were not appeared during this experiment!
Following items were confirmed in this experiment;
  Frost on the view ports are not appeared by proposed cooling scenario.
  Calibration heaters on the surface of inner radiation shield well worked as defrost heater for view ports on the surface of inner radiation shield up to ~50 K. It will take 2 days for defrosting for surface of the view ports.
  Heater on the IM well worked as defrost heater for mirror on the up to ~70 K. It will take 2 days for defrosting for surface of mirror.
  Partial pressure measurement of residual gas at each temperature was performed.

## Slide 16: Appendix

## Slide 17
Beam duct
14m
Main mirror parts
Cryostat with four cryocoolers
Overview of KAGRA Cryogenics system
Cryo shield ducts
in order to terminate
300 K radiation
Vibration isolation system
at room temperature

## Slide 18: Structure of KAGRA Cryostat
Seismic Attenuation System (SAS)
Duct Shield
Four Cryocooler Units
Main Laser Beam
Radiation Shields
4.3 m
2.6m
Cryogenic Payload
Sapphire Mirror
(-alumina crystal)
S. Koike
View Ports
Stainless steel t=20mm
Diameter 2.4 m
Height ~4.3 m
M ~ 12 ton
Cold Mass:
8K shield ~455 kg
80 K shield ~590 kg
Cryocoolers
Pulse tube, 60Hz
0.9 W at 4K (2nd)
36 W at 50K (1st)

## Slide 19: 1x10-3 Pa → ~-220 ℃（~53 K）
State diagrams of O2 and N2
Gas
1x10-5 Pa → ~-225 ℃（~48 K）
O2
super critical
Liquid
Solid
Pressure (MPa absolute)
Gas
Boiling point:-182.96 C
Temperature (℃)
N2
Pressure (MPa absolute)
Solid
Liquid
super critical
Gas
Boiling point:-147.1 C
Temperature (℃)

## Slide 20
O2
Temperature dependence of Q-mass