## Slide 1: Noise from birefringence fluctuations in laser interferometric gravitational wave detectors
birefringence
December 7, 2023
Yuta Michimura
LIGO Lab, Caltech
yuta@caltech.edu
RESCEU, UTokyo
michimura@phys.s.u-tokyo.ac.jp
JGW-G2315436
KAGRA Future Working Group 3rd open meeting (Online)

## Slide 2: Overview
Fluctuations in mirror birefringence will be phase noises for GW detectors
This can be avoided by aligning input polarization axis and mirror crystal axes
Requirements at 100 Hz will be - Δφ<~10-8 rad/√Hz (or Δn<~10-14/√Hz) for substrate - Δφ<~10-10 rad/√Hz for coating
Measurements and simulation work are necessary for further study
Y. Michimura, H. Wang, F. Salces-Carcoba, C. Wipf, A. Brooks, K. Arai, R. X. Adhikari,
arXiv:2308.00150 (to appear in PRD)

## Slide 3: Birefringence Noise
Crystalline materials (Silicon, Sapphire, AlGaAs etc.) are promising, but has birefringence
Static birefringence is (probably) small enough e.g., CQG 33, 015012 (2015), APL 122, 064101 (2023)
JILA found “birefringent noise” in AlGaAs PRX 13, 041002 (2023)
What is the requirement for mirror birefringence fluctuations for GW detectors?

## Slide 4: Birefringent FP Cavity ≒ FPMI
Fabry-Pérot cavity with birefringent mirror can be understood as unbalanced Fabry-Pérot Michelson
≒
Birefringent FP Cavity
Unbalanced FPMI

## Slide 5: Birefringent FP Cavity
Consider a FP cavity with mirrors that have substrate and coating birefringence
ITM
ETM
input
refl.
p-pol
s-pol
p-pol
Birefringent substrate
Birefringent coating

## Slide 6: Birefringent FP Cavity
This is equivalent to FP cavity with waveplates
ITM
ETM
input
refl.
p-pol
s-pol
p-pol
fast
slow
Birefringent substrate as WP
Birefringent coating as WP
Effects are enhanced by cavity

## Slide 7: Birefringent FP Cavity
FP cavity can be reduced to single “equivalent waveplate”
input
refl.
p-pol
s-pol
p-pol
Birefringent FP as equivalent WP
fast
slow
Two polarization eigenmodes have different resonant frequencies
Angle between axes θEQ

## Slide 8: Birefringent FP Cavity
“Equivalent waveplate” splits input polarization into two eigenmodes
input
p-pol
sinθEQ
cosθEQ
slow
fast
Different phase shift
due to birefringence
s-pol
p-pol
refl.
-sinθEQ
cosθEQ
“Unbalanced BS”
for axes rotation
to cavity axes
“Unbalanced BS”
for rotating back to p/s axes

## Slide 9: Birefringent FP Cavity
So, birefringent FP cavity is equivalent to FPMI with unbalanced BS
input
p-pol
“CARM”
(GW, usual thermal noise etc.)
mainly affects this phase
refl.
p-pol
slow
fast
refl.
s-pol
BS with
T=cosθEQ
R=sinθEQ
“DARM” (birefringence noise)
mainly affects this phase

## Slide 10: Avoiding Birefringence Noise
“CARM” (GW, usual thermal noise etc.) and “DARM” (birefringence noise) are mixed due to unbalanced BS, and therefore birefringence noise couples to GW signal
How to avoid? - Align polarization axis and mirror axes (make θEQ=1) - Make coating brief. large (make only one of the eigenmodes resonant; would not work for substrate brief.)
input
p-pol
refl.
p-pol
slow
fast
refl.
s-pol
T=cosθEQ
R=sinθEQ

## Slide 11: Requirements for Birefringence
Displacement noise coupling
Phase difference between axes
Angle between polarization axis and cavity axes
Factor only for substrate birefringence
Requirements on Δφ
For substrate
Δφ<~10-8 rad/√Hz
(or Δn<~10-14/√Hz)
For coating
Δφ<~10-10 rad/√Hz
assuming θ~1 deg

## Slide 12: Requirements for Axis Rotation
Displacement noise coupling
Phase difference between axes
Angle between polarization axis and cavity axes
Factor only for substrate birefringence
Requirements on θ
For substrate/coating
θ<~10-10 rad/√Hz
assuming Δn~10-7 or 10-4 for substrate, Δφ~1 mrad for coating
Strict requirement for KAGRA if Δn~10-4 (sapphire)
For others, assumed Δn~10-7 (e.g. silicon)

## Slide 13: Measurement at Caltech
Silicon birefringence measurements started
Sensitivity to Δn of 2x10-12 /rtHz @ 100 Hz achieved with Silicon @ 1550 nm, room temp. - Measurement at different input polarization suggest this is limited by noise not from silicon
Measurement and plot by Kushal Jain
Si (φ1 inch, t 5 mm)
Gran-Laser Prism
Measured

## Slide 14: Summary and Outlook
Fluctuations in mirror birefringence will be phase noises for GW detectors
Measurements of birefringence fluctuations in Silicon, Sapphire, AlGaAs etc. are necessary to see if they meet the requirement
Further simulation studies necessary for - Investigating PRC/SRC effects (unbalanced BS, ITM birefringence) - Noise from inhomogeneous birefringence x beam spot motion - Investigating effects for squeezing - Classical radiation pressure noise from orthogonal pol.
YM+, arXiv:2308.00150