## Slide 1: Proposal for modification of pumping unit between OMMT and OMC - prevention of vibration from vacuum pumping unit -
N. Kimura (ICRR)
2024/June/7

## Slide 2
Current setup of pumping units between SRM and OMMT-OMC
SRM
OMMT
OMC
TMP
Ion
Pump
Dry-
Pump
P
TMP
Ion
Pump
Dry-
Pump
P
GV-1
GV-2
Feature:
1. Separate pumping units between SRM and OMMT-OMC
2. Capable of returning the pressure between OMMT and OMC to atmospheric pressure (GV-2 closed, with optical window)
Connection to network
Connection to network

## Slide 3
Plan A: Modification of the pumping unit between SRM and OMMT-OMC
Features:
1. Rough pumping between OMMT and OMC with a dry pump. Achievable pressure 0.1~1Pa
2. Possible to return the pressure between OMMT and OMC to atmospheric pressure
(GV-2 closed, with optical window)
3. Pumping of the high vacuum region between OMMT and OMC is done by SRM's pumping unit. The pressure achieved is expected to be ~1x10^-4 Pa
4. Time required to switch from dry pump to TMP for pumping between OMMT and OMC: 1~2 days?
5. Remove the dry pump after switching the pumping between OMMT and OMC to TMP.
SRM
OMMT
OMC
Dry-
Pump
P
TMP
Ion
Pump
Dry-
Pump
P
GV-1
GV-2
Connection to network
Connection to network

## Slide 4
Plan B: Modification of the pumping unit between SRM and OMMT-OMC
Features.
1. Pumping OMMT and OMC with TMP. Achievable pressure ~1x10^-2 Pa and expected
2. Possible to return to atmospheric pressure between OMMT and OMC.
(GV-2 sealed, with optical window)
3. Pumping of the high vacuum region between OMMT and OMC is done by SRM's pumping unit. The pressure achieved is expected to be ~1x10^-4 Pa
4. Time required to switch pumping between OMMT and OMC to SRM's TMP: ~1 day?
5. After switching pumping between OMMT-OMC to TMP, isolate TMP
6. Need to obtain a TMP with pumping capacity of about 600 l/min.
SRM
OMMT
OMC
P
TMP
Ion
Pump
Dry-
Pump
P
GV-1
GV-2
Dry-
Pump
TMP
Connection to network
Connection to network