## Slide 1: Basics of Laser Interferometer Sensing and Control
Yuta Michimura
RESCEU, University of Tokyo
michimura@resceu.s.u-tokyo.ac.jp
JGW-G2416005
KAGRA Student Workshop 2024 @ Mozumi
August 27, 2024

## Slide 2: Topics
Michelson interferometer
Linear system
Power spectrum
Transfer function
Feedback system
Quantum noise

## Slide 3: Further Reading
Eric D. Black, Ryan N. Gutenkunst, An introduction to signal extraction in interferometric gravitational wave detectors, Am. J. Phys. 71, 365 (2003)
Peter R. Saulson, Fundamentals of Interferometric Gravitational Wave Detectors (World Scientific, 1994)
中村卓, 三尾典克, 大橋正健 編著『重力波をとらえる』(京都大学学術出版会, 1998)
日野幹雄『スペクトル解析』(朝倉書店, 2010)
片山徹『フィードバック制御の基礎』(朝倉書店, 2002)
東京大学 物理学実験II ブラウン運動 テキスト

## Slide 4: Michelson Interferometer
Measures differential arm length change
Movable mirror
Laser source
Interference
Beam
splitter
Photodiode

## Slide 5: Michelson Interferometer
Fringe change
Measures differential arm length change
Photodiode
Laser source
Beam
splitter
Interference
Movable mirror
Gravitational waves

## Slide 6: Interferometer Control
GW signal
Feedback control
Fringe
stop
Laser source
Beam
splitter
Interference
Movable mirror
Control mirror positions to stop the fringe
Gravitational waves

## Slide 7: Linear System
GW signal
Feedback control
Control makes the system linear
Actuator
(Mirror)
Sensor
(Interferometer)
Gravitational waves

## Slide 8: Noises and Sensitivity
GW signal
Feedback control
Noises in the loop limits the sensitivity
Thermal
vibrations
Seismic
motion
Electronics
noise
Shot
noise
Electronics
noise
Gravitational waves
Actuator
(Mirror)
Sensor
(Interferometer)

## Slide 9: Things You Will Learn (over the years)
GW signal
Feedback control
Sensor
(Interferometer)
Thermal
vibrations
Seismic
motion
Electronics
noise
Shot
noise
Electronics
noise
Gravitational waves
Actuator
(Mirror)
Mechanics
Electronics
Interferometry
Control Theory
Spectrum Analysis

## Slide 10: Laser Beam
Electro-magnetic waves
Electric field can be written as
amplitude
phase
angular
frequency
of laser
wavelength
phase at distance L
Electric field: E
Magnetic field
Speed of light: c

## Slide 11: Photodiodes
Photodiodes (PDs) Convert photons into electrons Detects light power (square of amplitude) We can only detect power change Phase change cannot be detected directly

## Slide 12: Transimpedance Amplifier
Power change signal will be converted into voltage change signal
Photons
Electrons
Quantum efficiency
Photoelectric effect
Photon energy
Current
Transimpedance gain
(Resistance)
[W] =[J/s]
[1/s]
[A]=[C/s]
[Ω]
Op amp
[V]

## Slide 13: Beam Splitter
Split beam in two
Half in power, 1/√2 in amplitude
Sign flip in back reflection

## Slide 14: Output of Michelson Interferometer
What is the power detected at the photodiode?
Photodiode
Laser
Beam
splitter
phase at distance L

## Slide 15: Output of Michelson Interferometer
What is the power detected at the photodiode?
From Y-am
From X-arm
Differential arm length
Input power

## Slide 16: Output of Michelson Interferometer
Power changes with differential arm length change (interference)
Laser
Bright fringe in every half wavelength change in differential arm length

## Slide 17: Output of Michelson Interferometer
Ratio between power change and length change
Differential arm length change can be detected from “linear” power change at the photodiode
Laser

## Slide 18: Linear System
System that has linear input and output relations
Linear System
Input
Output
Additivity
Homogeneity

## Slide 19: Fourier Transform
Handy to think in frequency domain
Linear System
Input
Output

## Slide 20: Power Spectrum Density
Handy to think in frequency domain
Linear System
Input
Output
[m]
[W]
[m2/Hz]
[W2/Hz]
[m/√Hz]
[W/√Hz]
Amplitude
Spectrum Density
Power
Spectrum Density
Fourier transform of

## Slide 21: Power Spectrum Density

## Slide 22: Transfer Function
Ratio of input and output
Linear System
Input
Output
[m]
[W]
[m2/Hz]
[W2/Hz]
[m/√Hz]
[W/√Hz]
Amplitude
Spectrum Density
Power
Spectrum Density

## Slide 23: Transfer Function of Interferometer
Constant if fringe is fixed

## Slide 24: Transfer Function of Actuator
Equation of motion of a suspended mirror
Transfer function from force to displacement
Resonant frequency
Q-value

## Slide 25: Feedback Control Loop
GW signal
Feedback control
Now we can analyze the loop in frequency domain
Actuator
(Mirror)
Sensor
(Interferometer)
Gravitational waves
We will design this filter later

## Slide 26: Feedback Control Loop
Open loop transfer function G(ω) is important
GW signal can be estimated from Y(ω) (feedback signal) if G(ω) >>1

## Slide 27: Feedback Control Loop
Open loop transfer function G(ω) is important
Loop can “oscillate” if G(ω)=-1
→ Nyquist stability criterion
Control filter is designed to meet this criterion

## Slide 28: Unstable Loop
GW signal
G(ω)=-1 at unity gain frequency
Actuator
(Mirror)
Sensor
(Interferometer)
GWs
If frequency independent
-1

## Slide 29: Stable Loop
GW signal
Phase margin at unity gain frequency
Actuator
(Mirror)
Sensor
(Interferometer)
GWs
Lead-lag filter
not -1
Phase margin

## Slide 30: Force Noise and Sensing Noise
GW signal
Loop calculation gives noise contributions
Actuator
(Mirror)
Sensor
(Interferometer)
GWs
Force
noise
Sensing
noise
Force noise
contribution
Sensing noise contribution
Estimated GW signal

## Slide 31: Shot Noise
Number of photons to photodiodes fluctuates
Quantum fluctuation of power
Photodiode
Number of photons
Photon energy
Shot noise
spectrum
Quantum efficiency

## Slide 32: Shot Noise Limit of Michelson
Power change
Shot noise
Shot noise limited sensitivity
Better shot noise with higher input power
Best at dark fringe (where PPD=0)

## Slide 33: Radiation Pressure Noise
Number of photons to mirror fluctuates
Power fluctuation
Mirror displacement
Mirror
Assumed Michelson with input power P0
Force on mirror
Force to displacement
(Actuator TF)
free-falling mirror
(above resonant frequency)

## Slide 34: Standard Quantum Limit
Shot noise is lower with higher power
Radiation pressure noise is lower with lower power
Standard Quantum Limit (SQL) for Michelson
Trade-off
√2 for two arms
m is mirror mass (m/2 is reduced mass)
Assuming BS with infinite mass
from Uncertainty principle

## Slide 35: Input Power and Sensitivity
SQL cannot be beaten by changing power
SQL Michelson
(3 km, 20 kg)
Michelson
(1000 W)
Michelson
(10 W)
Radiation pressure
Shot
Michelson
(100 W)

## Slide 36: Summary
GW signal
Feedback control
Sensor
(Interferometer)
Thermal
vibrations
Seismic
motion
Electronics
noise
Shot
noise
Electronics
noise
Gravitational waves
Actuator
(Mirror)
Mechanics
Electronics
Interferometry
Control Theory
Spectrum Analysis