## Slide 1: Release of KAGRA Instrument Science White Paper 2024 and Proposal for Amending Authorship Policy Regarding Long-Term Experimental Activities
December 18, 2024
Yuta Michimura
RESCEU, UTokyo
michimura@resceu.s.u-tokyo.ac.jp
for KAGRA FSC
JGW-G2416309 34th KAGRA Face-to-Face Meeting Dec 2024

## Slide 2: FSC Activities
https://fsc.org/
https://shitte-erabo.net/ fscproducts/fscmark/

## Slide 3: Instrument Science White Paper 2024
Released on December 3, 2024
Publicly available at JGW-T2416182
Comments welcome!
Contributors:
Tomotada Akutsu
Masaki Ando
Rishabh Bajpai
Marc Eisenmann
Kentaro Komori
Ray-Kuang Lee
Yuta Michimura
Kohei Mitsuhashi
Jyotirmaya Mohanta
Michael Page
Yohei Nishino
Munetake Otsuka
Atsushi Nishizawa
Shalika Singh
Kentaro Somiya
Ryosuke Sugimoto
Masahide Tamaki
Satoshi Tanioka
Haoyu Wang
Kazuhiro Yamamoto
Takaaki Yokozawa
paperless!

## Slide 4: WP Writing Workshop
Oct 2-3, 2024 @ Hiroshima University
Thanks to Nishizawa-san and ASPIRE-GW

## Slide 5: Instrument Science White Paper 2024
Executive Summary
Introduction - History from FPC white paper 2019 - Focus on post-O5 and beyond
Survey of Current Technologies - Over 60 technologies - Feasibility score: 0-5
Possible Upgrade Plans - Summary of outstanding issues - Example upgrade plans (LF, HF, BB)

## Slide 6: Executive Summary

## Slide 7: Technology Score
Relevance score: 0-2 for LF, HF, BB, stability, accuracy improvements
Relevance x Feasibility
Averaged over technologies

## Slide 8: Upgrade Plans by Swarm Intelligence
Interferometer parameters are tuned with particle swarm optimization to
- LF plans maximize 100-100 range - HF plans minimize BNS sky localization error or deep dip above kHz - BB plans maximize 1.4-1.4 range
YM+, PRD 97, 122003 (2018)

## Slide 9: Default bKAGRA Design Sensitivity
Default bKAGRA: Detuned RSE
NOTE: not all the requirements to achieve these fundamental noises are still not yet achieved e.g. - suspension loss 10-4 to 10-5 instead of 2x10-7 - substrate loss 10-6 instead of 10-8 - blade spring loss 4x10-5 instead of 7x10-7 - optical losses still higher by ~ x2

## Slide 10: With Current Mechanical Losses
If we cannot improve the mechanical losses from the current measured values, low frequency sensitivity limit is worse by ~ x5 compared with current aLIGO

## Slide 11: Possible Upgrade Plans
LF proposed by FPC in 2019
x4 heavier IM mass (82 kg) + Thinner and longer CuBe wires and sapphire fibers + 3 mW extra heat (instead of 50 mW)
~ A+ at LF

## Slide 12: Possible Upgrade Plans
LF2
LF2019 + 14.5 Hz to 5 Hz sapphire blade springs

## Slide 13: Possible Upgrade Plans
LF3
LF2 + 300-m long, 30 ppm loss filter cavity + 40 kg TM + x1/2 absorption
~A# at LF

## Slide 14: Possible Upgrade Plans
HF proposed by FPC in 2019
Shorter and thicker sapphire fibers + 3.4 MW/2 in each arm + 6 dB detected squeezing + 90.7% SRM
Beyond A+ at HF

## Slide 15: Possible Upgrade Plans
HFmod (similar but different from HFmod by 10 yr TF)
Shorter and thicker sapphire fibers + 3.1 MW/2 in each arm + 7 dB detected squeezing (lower loss) + 95.6 % SRM
~A# at HF

## Slide 16: Possible Upgrade Plans
HF2k (similar but different from HF2k by 10 yr TF)
Short and thicker sapphire fibers + 3.5 MW in each arm + 0.2% ITM + 7 dB detected squeezing (lower loss) + 99.5% SRM
Beyond A# at ~2 kHz

## Slide 17: Possible Upgrade Plans
HF3k (similar but different from HF3k by 10 yr TF)
Short and thicker sapphire fibers + 3.5 MW/2 in each arm + 7 dB detected squeezing (lower loss) + 99.5% SRM
Beyond A# at ~3 kHz

## Slide 18: Possible Upgrade Plans
40kg proposed by FPC in 2019
40 kg TM (largest mass that can be put into current cryostat without changing shields etc. design)

## Slide 19: Possible Upgrade Plans
FDSQZ proposed by FPC in 2019
Frequency dependent squeezing with 30-m filter cavity

## Slide 20: Possible Upgrade Plans
BB1
40 kg TM + 85-m filter cavity (studied by KFC project) giving 5 dB detected squeezing

## Slide 21: Possible Upgrade Plans
BB2
BB1 + 9.1 dB detected squeezing (lower loss)

## Slide 22: Possible Upgrade Plans
BB3
BB2 + LF2019 improvements + 5 Hz blade springs
~A+ at mid freq.

## Slide 23: Possible Upgrade Plans
BB4
BB3 + 100 kg TM + x1/4 coating thermal noise + x1/4 absorption + 2.9 MW/2 in each arm
~A# at mid freq.

## Slide 24: Lessons Learned
Improvements in sapphire fibers and blade springs are crucial for LF improvements
Improvements in sapphire mirrors and coatings are crucial for mid. frequencies
Developments in lower loss optics, high power operations, and higher finesse arm cavities and SRC are crucial for HF improvements
To compete with A#, HF would be most feasible
Even with less sensitive BB plans, KAGRA’s contributions to the network observation are important. Needs further study.

## Slide 26: Proposal to allow for long term experimental activities for KAGRA authorship

## Slide 27: Current Authorship Policy
Long-term activities may count up to 15% of research time in total. Long term activities are defined in the data analysis and theoretical subgroup's task lists.
Why not include experimental R&Ds?
JGW-M1503490-v7

## Slide 28: Amendment Proposal
Long-term activities may count up to 15% of research time in total. Long term activities are defined in the data analysis and theoretical subgroup's task lists.
Proposed amendment
Long-term activities may count up to 15% of research time in total. Long term activities are defined in the data analysis, theoretical subgroup, and instrumental science task lists.

## Slide 29: Summary Table for Authorship
Activity |  | Management | White Paper | Time frame | Author-ship
Data analysis / Theory |  | KSC-DAC/ Theory Group | LVK Observational Science WP | Short Term | <= 100%
 |  |  |  | Long Term | <= 15% in total
 | Project task | EO-SEO/ Operations | LVK Operations WP | Short Term | <= 100%
 | Project R&D | KSC-FSC-PRDC | KAGRA Instrument Science WP | Short Term | <= 100%
 | Advanced R&D | KSC-FSC |  | Long Term | <= 0% → <= 15%
EPO |  | KSC-EPO | LVK Communications and Education WP | - | <= 15% in total
Experiment
Note that current KAGRA Instrument Science WP does not include tasks under SEO. Instrument Science WPs for LIGO, Virgo, KAGRA are independent right now.

## Slide 30: Summary
KAGRA Instrument Science White Paper 2024 is released
Any comments welcomed
Welcome to join FSC or FWG
FWG 4th open meeting on December 19 @ Ookayama