## Slide 1
 |  | KAGRA | A# | LF2019 | LF2024 | BB2019 | BB2024 | HF2019 | HF2024 | HF3k
 | 100M☉ - 100M☉ | 353 Mpc | 4927 Mpc | 2019 Mpc | 3787 Mpc | 306 Mpc | 2154 Mpc | 112 Mpc | 200 Mpc | 277 Mpc
 | 30M☉- - 30M☉ | 1095 Mpc | 6144 Mpc | 1088 Mpc | 2382 Mpc | 842 Mpc | 4229 Mpc | 270 Mpc | 407 Mpc | 552 Mpc
 | 1.4M☉ - 1.4M☉ | 153 Mpc | 670 Mpc | 85 Mpc | 196 Mpc | 178 Mpc | 537 Mpc | 155 Mpc | 133 Mpc | 104 Mpc
BNS sky localization ※ |  | 10.64 deg2 (HL-only) → 1.40 deg2 (with K) |  | 10.28 deg2 | 2.65 deg2 | 0.77 deg2 | 0.42 deg2 | 0.57 deg2 | 0.61 deg2 | 0.93 deg2
BNS post-merger signal detection rate (LF & BB plans are less than 10-3 events/year) Based on merger rate estimate from O3; SNR>5. See H. Tagoshi & S. Morisaki, JGW-P2416311 for details. |  |  |  |  |  |  |  | 10-5-10-3 /year | 10-3-0.06 /year | 10-3-0.2 /year
Technical challenges FC = filter cavity SQZ = squeezing SRM = signal recycling mirror |  | * Low loss suspension * Sapphire birefringence * 0.35 MW arm power | * 40 kg → 100 kg test mass * 300 m FC, 10 dB SQZ * 1.5 MW arm power * 1/4 coating thermal | * Heavier & longer suspensions + for 2024 ver... * Reducing vertical resonant frequency of blade springs * 23 kg → 40 kg test mass * 300 m FC w/ 30 ppm loss * 1/2 absorption * Various technical noises at low frequencies |  | * 30 m FC with 30 ppm loss + for 2024 ver... * Reducing vertical resonant frequency of blade springs * 23 kg → 100 kg test mass * 30 m → 85 m FC, 9 dB SQZ * 1.5 MW arm power * 1/4 coating thermal * 1/4 absorption |  | * Shorter and thicker sapphire fibers * No FC, 6 dB SQZ * 1.7 MW arm power * 90.7% SRM | * 96% SRM | * 99.5% SRM
References: For plans 2019 (~5-year plans), see YM+, PRD 102, 022008 (2020) For other plans (~10-year plans), see JGW-T2416182 (public document) For various science cases, see KAGRA, PTEP 2021, 05A103 (2021) |  |  |  | Which KAGRA upgrade plan do you like? |  |  |  |  |  | 
From Quarks to Neutron Stars: Insights from kHz gravitational waves (UTokyo, Apr 23-24, 2025)
upgrade in the kHz band for probing neutron star physics
To make multi-messenger observations like GW170817 routine, LIGO and Virgo are planning broadband upgrades, and next-generation projects such as Einstein Telescope and Cosmic Explorer are underway. The world’s only cryogenic interferometer, KAGRA, requires a different upgrade strategy, as high-frequency sensitivity demands higher laser power, while low-frequency sensitivity requires thin fibers with limited heat extraction capability. After evaluating various upgrade scenarios, we find that high-frequency option is the most feasible as a first step towards a broadband upgrade. This upgrade would improve sky localization of binary neutron stars and enable post-merger signal detections.
※ Fisher analysis using IMRPhenomD waveform for GW170817-like binary at z=0.03 (127 Mpc) with two A#s and KAGRA.
Median of 108 uniformly distributed sets of the source location and the polarization angle is shown.
Design and status of KAGRA
Download online
Possible upgrade plans
April 2016
May 2018
Aug 2019
Nov 2019
Dec 2019
Feb 2020
Mar 2020 (O3GK)
May 2023 (O4a)
Target by June 2025
aLIGO 2024 (O4)
aLIGO design
A+ design (O5; 2027?)
A# design (O6; 2030?)
LIGO Voyager (cryo)
NEMO (Australia 4 km)
Einstein Telescope (EU 3G 10-15 km LF+HF xylophone; 2035~?)
KAGRA design
Seismic noise + gravity gradient
noise is low due to underground
Quantum shot noise is high due to limited laser power
Suspension thermal noise is high due to thick sapphire fibers to extract heat
Sensitivity improvement
of KAGRA
ET-LF
ET-HF
LF2019
LF2024
BB2024
BB2019
HF2019
HF2024
HF3k
Low frequency focus
Broadband plans
BBH100-100
at 1Gpc
* No FC, 10 dB SQZ * 0.75 MW arm power
* No changes in the suspensions required. Can go to other configurations just by changing the SRM.
Mirror thermal noise is low due to cryogenic sapphire mirror (22 K)
LIGO Hanford
LIGO Livingston
(4 km)
Virgo (3 km)
KAGRA
(3 km, cryogenic)
LIGO-India
(4km; 2030?~)
KAGRA
Virgo
LIGO
TAMA
Cosmic Explorer
Einstein Telescope
KAGRA upgrade?
Binary neutron star range
evolution of LVK
A+
A#
BBH / BNS
ranges (SNR>8)
Binary Black Holes / Binary Neutron Stars
Upgrade
Yuta Michimura
RESCEU, University of Tokyo
michimura@resceu.s.u-tokyo.ac.jp
KAGRA 10yr Task Force, KAGRA Future Strategy Committee
(LIGO O6
upgrade)
Baseline design
BNS1.5-1.5 at 100 Mpc
Post-merger signal example R. Harada+, PRD 110, 123005 (2024)
High frequency focus
Cosmic Explorer (US 3G 20-40 km; 2035~?)