## Slide 1: Power recycling cavity length and power recycling gain measurements
Yuta Michimura
RESCEU, University of Tokyo
Kavli IPMU, WPI, UTIAS, University of Tokyo
February 13, 2026
JGW-G2617195

## Slide 2: Scope
This slide explains recent measurements of - Power recycling cavity length - Power recycling gain - Beam Splitter T and R for s-pol and p-pol using PRX and PRY (and ITMX/Y single bounce)
See klog #36249 and klog #36340
See, also, klog #36283
See JGW-T2617194 for simulations and how to deal with f2-PRCL mismatch

## Slide 3: Configuration
PRM
PR2
PR3
BS
ITMX
ITMY
POP_PDA1_DC
POP_SPOL
POP_PPOL
SR3
SR2
AS_PDA1_DC
SRM, OMMT1, OMMT2, OFI, OSTM
This is basically s-pol power
POS_SPOL
POS_PPOL
JGW-L1605744
s-pol to s-pol or
s-pol to p-pol conversion
klog #14575

## Slide 4: BS ratios from ITM single bounce
From AS and POS_SPOL, ITM reflectivity of s-pol to s-pol can be measured
Next, using POP_SPOL, BS T:R for s-pol can be measured
Then, using POP_PPOL and POS_PPOL, BS T:R for p-pol and ITM reflectivity of s-pol to p-pol can be measured
Power when ITMX single bounce
ITMY single bounce

## Slide 5: BS ratios from ITM single bounce
Results are the following (no significant loss in BS assumed): ITM reflectivity ratio X/Y for s-pol 1.039+/-0.005 BS T/R ratio for s-pol 0.998+/-0.012 BS T for s-pol 0.4995+/-0.0030 BS R for s-pol 0.5005+/-0.0030 BS T/R ratio for p-pol 4.025+/-0.031 BS T for p-pol 0.8010+/-0.0012 BS R for p-pol 0.1990+/-0.0012 ITM p-pol conversion ratio X/Y 0.663+/-0.005
BS T:R=50:50 for s-pol and 80:20 for p-pol consistent with Hirose-san’s characterizations and coating design (JGW-T1503347)
ITM p-pol conversion is 6-7% for X and 9-10% for Y (klog #36283). This asymmetry explains ITM reflectivity asymmetry for s-pol as well.
klog #36249

## Slide 6: PRC resonant conditions: Design
PRX/PRY sideband
PRC in PRFPMI
2.251 MHz
Carrier
f2
2*f2
45.015898 MHz
20FSR
40FSR
40FSR
40FSR
PRX/PRY carrier
2.196 MHz
2.309 MHz
Frequency
Frequency
Frequency
POP90 will be the same for X and Y
Locked on carrier resonance
Locked on f2 resonance
POP90 will be the same for X and Y

## Slide 7: PRC resonant conditions: Detuned
PRX/PRY sideband
PRC in PRFPMI
Carrier
f2
2*f2
20FSR
40FSR
PRX/PRY carrier
Frequency
Frequency
Frequency
Locked on carrier resonance
Locked on f2 resonance
40FSR
40FSR
POP90 will not be the same for X and Y
POP90 will not be the same for X and Y

## Slide 8: PRGs for PRX and PRY
From power ratio at POP_DC and AS_DC when ITM single bounce and PRX/PRY, carrier PRG for carrier lock can be estimated: Carrier PRG for PRX 0.341+/-0.006 Carrier PRG for PRY 0.330+/-0.009
f2 PRG is given by
klog #36249
Carrier PRG
f2 detuning
f2 PRG for PRY
f2 PRG for PRX
f2 detuning
FSR of PRC
Finesse of PRC
3.71(14) with optical loss of 13(5)%
Detuning
Detuning from Schnupp asymmetry
(HWHM is therefore ~0.303 MHz)
Optical loss estimated
from carrier PRG for PRX/Y

## Slide 9: PRGs for PRX and PRY
From POP90 √(I2+Q2) ratios, f2 detuning can be estimated: Estimated f2 detuning of PRC 0.0599+/-0.0033 MHz
From this detuning PRC length can be estimated: Average PRC length 66.540+/-0.005 m
Using carrier PRG, f2 PRG can be estimated: f2 sideband PRG for PRX 0.0244+/-0.0017 f2 sideband PRG for PRY 0.0200+/-0.0014
Carrier PRG
f2 detuning
f2 PRG for PRY
f2 PRG for PRX
f2 detuning
Detuning from Schnupp asymmetry
klog #36340
0.34
0.0244
0.0200
0.0599 MHz
1.135 MHz
0.0599 MHz
* HWHM is ~0.303 MHz
* These values do not mean that f2 power is enhanced by these amounts

## Slide 10: Losses in PRC for PRFPMI
Schnupp asymmetry of (klog #14575) gives loss-less Michelson reflectivity for f2 of
This gives f2 PRG of = 36.62(4), if PRC length is perfectly matched with f2.
The finesse for loss-less PRC is
The FSR for PRC using the measured value 66.540(5) m is = 2.25272(17) MHz.
Using the measured f2 detuning , PRG for detune f2 is
To explain measured f2 PRG in PRFPMI of 2.44(12), additional 12.6-16.1% loss is necessary. This is consistent with loss measurements in PRX and PRY.
klog #36340